ETSI TS 100 901 V7.3.0 (1999-11)

Technical Specification

Digital cellular telecommunications system (Phase 2+);

Technical realization of the Short Message Service (SMS);

Point-to-Point (PP)

(GSM 03.40 version 7.3.0 Release 1998)

GLOBAL SYSTEM FOR

MOBILE COMMUNICATIONS

R

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 2 (GSM 03.40 version 7.3.0 Release 1998)

Reference

RTS/SMG-040340Q7R1 (8cc03j03.PDF)

Keywords

Digital cellular telecommunications system,

Global System for Mobile communications (GSM)

ETSI

Postal address

F-06921 Sophia Antipolis Cedex - FRANCE

Office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Internet

secretariat@etsi.fr

Individual copies of this ETSI deliverable

can be downloaded from

http://www.etsi.org

If you find errors in the present document, send your

comment to: editor@etsi.fr

Important notice

This ETSI deliverable may be made available in more than one electronic version or in print. In any case of existing or

perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF).

In case of dispute, the reference should be the printing on ETSI printers of the PDF version kept on a specific network

drive within ETSI Secretariat.

Copyright Notification

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 1999.

All rights reserved.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 3 (GSM 03.40 version 7.3.0 Release 1998)

Contents

Intellectual Property Rights...............................................................................................................................6

Foreword............................................................................................................................................................6

Introduction .......................................................................................................................................................6

1 Scope .......................................................................................................................................................8

2 References ...............................................................................................................................................8

2.1 Definitions and abbreviations ...........................................................................................................................10

2.1.1 Definitions .................................................................................................................................................10

2.2.2 Abbreviations.............................................................................................................................................12

3 Services and service elements................................................................................................................12

3.1 Basic services ..................................................................................................................................................12

3.2 Short Message Service elements.......................................................................................................................13

3.2.1 Validity-Period ..........................................................................................................................................14

3.2.2 Service-Centre-Time-Stamp .......................................................................................................................14

3.2.3 Protocol-Identifier......................................................................................................................................14

3.2.4 More-Messages-to-Send .............................................................................................................................14

3.2.5 Delivery of Priority and non-Priority Messages..........................................................................................14

3.2.6 Messages-Waiting......................................................................................................................................14

3.2.7 Alert-SC.....................................................................................................................................................17

3.2.8 Options concerning MNRG, MNRF, MNRR, MCEF and MWD...............................................................17

3.2.9 Status report capabilities............................................................................................................................18

3.2.10 Reply Path..................................................................................................................................................19

3.3 Unsuccessful short message TPDU transfer SC -> MS....................................................................................19

3.3.1 Errors occurring during transfer of TPDU to MS.......................................................................................19

3.3.2 Errors occurring after TPDU arrives at MS................................................................................................19

3.4 Unsuccessful short message TPDU transfer MS -> SC....................................................................................21

3.4.1 Errors occurring during transfer of TPDU to SC........................................................................................21

3.4.2 Errors occurring after TPDU arrives at SC.................................................................................................21

3.5 Use of Supplementary Services in combination with the Short Message Service ............................................21

3.6 Applicability of Operator Determined Barring to the Short Message Service..................................................22

3.7 Multiple short message transfer.......................................................................................................................22

3.8 SMS and Internet Electronic Mail interworking...............................................................................................22

3.8.1 Basic Format ..............................................................................................................................................22

3.8.2 Optional Fields...........................................................................................................................................23

3.8.2.1 Subject..................................................................................................................................................23

3.8.2.2 Real Name............................................................................................................................................23

3.8.2.3 Optional Control Flag...........................................................................................................................23

3.8.3 Text concatenation.....................................................................................................................................23

3.8.4 Alternative characters for Internet email addresses in MO SMS................................................................24

3.9 SMS COMPRESSION ....................................................................................................................................24

4 Network architecture.............................................................................................................................25

4.1 Basic network structure ...................................................................................................................................25

4.2 Transfer on link 3 ............................................................................................................................................26

5 Service Centre and PLMN interconnection ...........................................................................................26

5.1 Service centre connection................................................................................................................................26

5.2 Routing requirements ......................................................................................................................................26

5.2.1 Mobile terminated short message................................................................................................................26

5.2.2 Mobile originated short message ................................................................................................................26

6 Service Centre functionality..................................................................................................................26

6.1 Service Centre capabilities ...............................................................................................................................27

6.2 SC functional requirements ..............................................................................................................................27

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 4 (GSM 03.40 version 7.3.0 Release 1998)

7 MS functionality....................................................................................................................................27

7.1 MS capabilities ................................................................................................................................................27

7.2 MS configuration.............................................................................................................................................28

8 Node functionality.................................................................................................................................28

8.1 Node functionality related to SM MT ..............................................................................................................28

8.1.1 Functionality of the SMS-GMSC................................................................................................................28

8.1.2 Functionality of the MSC............................................................................................................................30

8.1.3 Functionality of the SGSN..........................................................................................................................31

8.2 Node functionality related to SM MO..............................................................................................................32

8.2.1 Functionality of the MSC............................................................................................................................32

8.2.2 Functionality of the SMS-IWMSC .............................................................................................................32

8.2.3 Functionality of the SGSN..........................................................................................................................33

8.3 SMS-IWMSC functionality related to alerting .................................................................................................33

9 Protocols and protocol architecture .......................................................................................................33

9.1 Protocol element features ................................................................................................................................34

9.1.1 Octet and Bit transmission order.................................................................................................................34

9.1.2 Numeric and alphanumeric representation..................................................................................................34

9.1.2.1 Integer representation...........................................................................................................................34

9.1.2.2 Octet representation ..............................................................................................................................35

9.1.2.3 Semi-octet representation ......................................................................................................................35

9.1.2.4 Alphanumeric representation.................................................................................................................36

9.1.2.5 Address fields.......................................................................................................................................36

9.2 Service provided by the SM-TL.......................................................................................................................38

9.2.1 General.......................................................................................................................................................38

9.2.2 PDU Type repertoire at SM-TL..................................................................................................................38

9.2.2.1 SMS-DELIVER type............................................................................................................................38

9.2.2.1a SMS-DELIVER-REPORT type ............................................................................................................41

9.2.2.2 SMS-SUBMIT type ..............................................................................................................................43

9.2.2.2a SMS-SUBMIT-REPORT type..............................................................................................................45

9.2.2.3 SMS-STATUS-REPORT type ..............................................................................................................48

9.2.2.4 SMS-COMMAND type ........................................................................................................................50

9.2.3 Definition of the TPDU parameters ............................................................................................................51

9.2.3.1 TP-Message-Type-Indicator (TP-MTI).................................................................................................51

9.2.3.2 TP-More-Messages-to-Send (TP-MMS)...............................................................................................51

9.2.3.3 TP-Validity-Period-Format (TP-VPF) ..................................................................................................52

9.2.3.4 TP-Status-Report-Indication (TP-SRI)..................................................................................................52

9.2.3.5 TP-Status-Report-Request (TP-SRR)....................................................................................................52

9.2.3.6 TP-Message-Reference (TP-MR)..........................................................................................................52

9.2.3.7 TP-Originating-Address (TP-OA).........................................................................................................53

9.2.3.8 TP-Destination-Address (TP-DA).........................................................................................................53

9.2.3.9 TP-Protocol-Identifier (TP-PID)...........................................................................................................53

9.2.3.10 TP-Data-Coding-Scheme (TP-DCS) .....................................................................................................55

9.2.3.11 TP-Service-Centre-Time-Stamp (TP-SCTS).........................................................................................55

9.2.3.12 TP-Validity-Period (TP-VP) .................................................................................................................55

9.2.3.12.1 TP-VP (Relative format) .................................................................................................................55

9.2.3.12.2 TP-VP (Absolute format ) ...............................................................................................................55

9.2.3.12.3 TP-VP ( Enhanced format ) .............................................................................................................56

9.2.3.13 TP-Discharge-Time (TP-DT)................................................................................................................56

9.2.3.14 TP-Recipient-Address (TP-RA) ............................................................................................................57

9.2.3.15 TP-Status (TP-ST)................................................................................................................................57

9.2.3.16 TP-User-Data-Length (TP-UDL) ..........................................................................................................58

9.2.3.17 TP-Reply-Path (TP-RP) ........................................................................................................................58

9.2.3.18 TP-Message-Number (TP-MN) ............................................................................................................58

9.2.3.19 TP-Command-Type (TP-CT) ................................................................................................................59

9.2.3.20 TP-Command-Data-Length (TP-CDL) .................................................................................................59

9.2.3.21 TP-Command-Data (TP-CD) ................................................................................................................59

9.2.3.22 TP-Failure-Cause (TP-FCS)..................................................................................................................60

9.2.3.23 TP-User-Data-Header-Indicator (TP-UDHI) ........................................................................................61

9.2.3.24 TP-User Data (TP-UD) .........................................................................................................................61

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 5 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.24.1 Concatenated Short Messages .........................................................................................................64

9.2.3.24.2 Special SMS Message Indication ....................................................................................................65

9.2.3.24.3 Application Port Addressing 8 bit address ......................................................................................67

9.2.3.24.4 Application Port Addressing 16 bit address ....................................................................................67

9.2.3.24.5 SMSC Control Parameters...............................................................................................................68

9.2.3.24.6 UDH Source Indicator .....................................................................................................................69

9.2.3.24.7 SIM Toolkit Security Headers.........................................................................................................69

9.2.3.24.8 Concatenated short messages, 16-bit reference number ..................................................................69

9.2.3.24.9 Wireless Control Message Protocol.................................................................................................70

9.2.3.25 TP-Reject-Duplicates (TP-RD) .............................................................................................................70

9.2.3.26 TP-Status-Report-Qualifier (TP-SRQ) ..................................................................................................71

9.2.3.27 TP-Parameter-Indicator (TP-PI)............................................................................................................71

9.3 Service provided by the SM-RL.......................................................................................................................71

9.3.1 General.......................................................................................................................................................71

9.3.2 Protocol element repertoire at SM-RL........................................................................................................71

9.3.2.1 RP-MO-DATA.....................................................................................................................................72

9.3.2.2 RP-MT-DATA.....................................................................................................................................72

9.3.2.3 RP-ACK...............................................................................................................................................73

9.3.2.4 RP-ERROR..........................................................................................................................................73

9.3.2.5 RP-ALERT-SC.....................................................................................................................................73

9.3.2.6 RP-SM-MEMORY-AVAILABLE........................................................................................................74

10 Fundamental procedures within the point-to-point SMS.......................................................................74

10.1 Short message mobile terminated .....................................................................................................................74

10.2 Short message mobile originated.....................................................................................................................86

10.3 Alert transfer....................................................................................................................................................91

11 Mapping of error causes between RP layers ..........................................................................................93

11.1 Mobile Terminated short message transfer.......................................................................................................93

11.2 Memory available notification.........................................................................................................................94

11.3 Mobile Originated short message transfer ........................................................................................................94

Annex A (informative): Protocol stacks for interconnecting SCs and MSCs...................................96

Annex B (informative): Information now contained in GSM 03.38 ..................................................97

Annex C (informative): Short message information flow...................................................................98

Annex D (informative): Mobile Station reply procedures................................................................116

D.1 Introduction .........................................................................................................................................116

D.2 The scope of applicability ....................................................................................................................116

D.3 Terminology........................................................................................................................................116

D.4 The reply path requesting procedure....................................................................................................116

D.5 The reception of an original MT SM...................................................................................................117

D.6 The submission of the reply MO SM...................................................................................................117

D.7 Usage of SCs for replying ....................................................................................................................117

D.8 Replying possibilities for Phase 1 mobile stations...............................................................................118

D.9 The resulting service for originating SMEs.........................................................................................118

Annex E (informative): Change History ............................................................................................119

History ...........................................................................................................................................................120

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 6 (GSM 03.40 version 7.3.0 Release 1998)

Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information

pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found

in SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect

of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server

(http://www.etsi.org/ipr).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee

can be given as to the existence of other IPRs not referenced in SR 000 314 (or the updates on the ETSI Web server)

which are, or may be, or may become, essential to the present document.

Foreword

This Technical Specification (TS) has been produced by ETSI Technical Committee Special Mobile Group (SMG).

The present document describes the point-to-point Short Message Service (SMS) of the digital cellular

telecommunications system.

The contents of the present document is subject to continuing work within SMG and may change following formal SMG

approval. Should SMG modify the contents of the present document, it will be re-released by SMG with an identifying

change of release date and an increase in version number as follows:

Version 7.x.y

where:

7 indicates GSM Phase 2+ Release 1998;

x the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates,

etc.;

y the third digit is incremented when editorial only changes have been incorporated in the specification.

Introduction

The Point-to-Point Short Message Service (SMS) provides a means of sending messages of limited size to and from

GSM mobiles. The provision of SMS makes use of a Service Centre, which acts as a store and forward centre for short

messages. Thus a GSM PLMN needs to support the transfer of short messages between Service Centres and mobiles.

Two different point-to-point services have been defined: mobile originated and mobile terminated. Mobile originated

messages will be transported from an MS to a Service Centre. These may be destined for other mobile users, or for

subscribers on a fixed network. Mobile terminated messages will be transported from a Service Centre to an MS. These

may be input to the Service Centre by other mobile users (via a mobile originated short message) or by a variety of other

sources, e.g. speech, telex, or facsimile.

The present document includes references to features which were introduced into the GSM Technical specifications after

Release 96 of GSM Phase 2+.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 7 (GSM 03.40 version 7.3.0 Release 1998)

The following table lists all features that were introduced after Release 96 and have impacted the present document:

Feature Designator

Optional SMSC Control Parameters - Selective Status Report not used

Optional Source Indicator in the User Data Header not used

Optional Status Report PDU Enhancement not used

Optional UDH in all PDUs containing user data. not used

Optional SMS Secured Messaging not used

Optional Transmission of the SME Originating Address

between the SMSC and the SMS-GMSC

not used

GPRS not used

Mobile phone management not used

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 8 (GSM 03.40 version 7.3.0 Release 1998)

1 Scope

The present document describes the point-to-point Short Message Service (SMS) of the GSM PLMN system. It defines:

- the services and service elements;

- the network architecture;

- the Service Centre functionality;

- the MSC functionality (with regard to the SMS);

- the SGSN functionality (with regard to the SMS);

- the routing requirements;

- the protocols and protocol layering;

for the Teleservices 21 and 22, as specified in the GSM 02.03.

The use of radio resources for the transfer of short messages between the MS and the MSC or the SGSN is described in

GSM 04.11 "Point-to-Point Short Message Service Support on Mobile Radio Interface", and is dealt with in that

specification.

The network aspects of Short Message Service provision are outside the scope of the present document (i.e. the

provision of network connectivity between the PLMN subsystems). There is no technical restriction within the present

document for the transfer of short messages between different PLMN's. Any such restriction is likely to be subject to

commercial arrangements and PLMN operators must make their own provision for interworking or for preventing

interworking with other PLMN's as they see fit.

The required and assumed network service offered to the higher layers is defined in the present document.

The Cell Broadcast Short Message Service (Teleservice 23) is a separate service, and is described in GSM 03.41

"Technical Realization of the Short Message Service - Cell Broadcast".

2 References

The following documents contain provisions which, through reference in this text, constitute provisions of the present

document.

References are either specific (identified by date of publication, edition number, version number, etc.) or nonspecific.

For a specific reference, subsequent revisions do not apply.

For a non-specific reference, the latest version applies.

A non-specific reference to an ETS shall also be taken to refer to later versions published as an EN with the same

number.

For this Release 1998 document, references to GSM documents are for Release 1998 versions (version 7.x.y).

[1] GSM 01.04: "Digital cellular telecommunication system (Phase 2+); Abbreviations and acronyms".

[2] GSM 02.03: "Digital cellular telecommunication system (Phase 2+); Teleservices supported by a

GSM Public Land Mobile Network (PLMN)".

[3] GSM 02.04: "Digital cellular telecommunication system (Phase 2+); General on supplementary

services".

[4] GSM 02.41: "Digital cellular telecommunication system (Phase 2+); Operator determined barring".

[5] GSM 03.02: "Digital cellular telecommunication system (Phase 2+); Network architecture".

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 9 (GSM 03.40 version 7.3.0 Release 1998)

[6] GSM 03.08: "Digital cellular telecommunication system (Phase 2+); Organization of subscriber

data".

[7] GSM 03.11: "Digital cellular telecommunication system (Phase 2+); Technical realization of

supplementary services".

[8] GSM 03.15: "Digital cellular telecommunication system (Phase 2+); Technical realization of

operator determined barring".

[9] GSM 03.38: "Digital cellular telecommunication system (Phase 2+); Alphabets and

language-specific information".

[10] GSM 03.41: "Digital cellular telecommunication system (Phase 2+); Technical realization of Short

Message Service Cell Broadcast (SMSCB)".

[11] GSM 03.47 (ETR 354): "Digital cellular telecommunication system; Example protocol stacks for

interconnecting Service Centre(s) (SC) and Mobile-services Switching Centre(s) (MSC)".

[12] GSM 04.08: "Digital cellular telecommunication system (Phase 2); Mobile radio interface layer 3

specification".

[13] GSM 04.11: "Digital cellular telecommunication system (Phase 2+); Point-to-Point (PP) Short

Message Service (SMS) support on mobile radio interface".

[14] GSM 07.05: "Digital cellular telecommunication system (Phase 2+); Use of Data Terminal

Equipment - Data Circuit terminating Equipment (DTE - DCE) interface for Short Message

Service (SMS) and Cell Broadcast Service (CBS)".

[15] GSM 09.02: "Digital cellular telecommunication system (Phase 2+); Mobile Application Part

(MAP) specification".

[16] GSM 11.11: "Digital cellular telecommunication system (Phase 2+); Specification of the

Subscriber Identity Module - Mobile Equipment (SIM - ME) interface".

[17] CCITT Recommendation E.164 (Blue Book): "Numbering plan for the ISDN era".

[18] CCITT Recommendation E.163 (Blue Book): "Numbering plan for the international telephone

service".

[19] CCITT Recommendation Q.771: "Specifications of Signalling System No.7; Functional

description of transaction capabilities".

[20] CCITT Recommendation T.100 (Blue Book): "International information exchange for interactive

videotex".

[21] CCITT Recommendation T.101 (Blue Book): "International interworking for videotex services".

[22] CCITT Recommendation X.121 (Blue Book): "International numbering plan for public data

networks".

[23] CCITT Recommendation X.400 (Blue Book): "Message handling system and service overview".

[24] ISO/IEC10646, "Universal Multiple-Octet Coded Character Set (USC); UCS2, 16 bit coding".

[25] GSM 02.22: "Digital cellular telecommunication system (Phase 2+); Personalization of GSM

Mobile Equipment (ME); Mobile functionality specification".

[26] GSM 03.42: "Digital cellular telecommunication system (Phase 2+); Compression Algorithm for

Text Messaging Services"

[27] GSM 03.60: "Digital cellular telecommunications system (Phase 2+); General Packet Radio

Service (GPRS); Service description; Stage 2".

[28] GSM 03.48: "Digital cellular telecommunications system (Phase 2+); Security Mechanisms for the

SIM application toolkit; Stage 2".

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 10 (GSM 03.40 version 7.3.0 Release 1998)

2.1 Definitions and abbreviations

NOTE: Use of hyphens and full stops:

Care is needed when reading the present document as names containing words separated by hyphens have

different meaning than when separated with full stops. E.g. TS-Status-Report-Request is a parameter

within a TS-Submit primitive, whilst TS-Status-Report. Request is a primitive in its own right.

2.1.1 Definitions

active MS: A switched-on mobile station with a SIM module attached.

alert-SC: Service element provided by a GSM PLMN to inform an SC which has previously initiated unsuccessful short

message delivery attempt(s) to a specific MS, that the MS is now recognized by the PLMN to have recovered operation.

status report: SC informing the originating MS of the outcome of a short message submitted to an SME.

Gateway MSC For Short Message Service (SMS-GMSC): A function of an MSC capable of receiving a short

message from an SC, interrogating an HLR for routing information and SMS info, and delivering the short message to

the VMSC or the SGSN of the recipient MS.

Interworking MSC For Short Message Service (SMS-IWMSC): A function of an MSC capable of receiving a short

message from within the PLMN and submitting it to the recipient SC.

Messages-Waiting (MW): Service element that makes a PLMN store information (Messages-Waiting-Indication),

listing those SCs that have made unsuccessful short message delivery attempts to MSs in that PLMN.

Messages-Waiting-Indication (MWI): Data to be stored in the HLR and VLR with which an MS is associated,

indicating that there is one or more messages waiting in a set of SCs to be delivered to the MS (due to unsuccessful

delivery attempt(s)).

Messages-Waiting-Data (MWD): A part of theMWI to be stored in the HLR.MWD consists of an address list of the

SCs which have messages waiting to be delivered to the MS.

Mobile-services Switching Centre (MSC): The Mobile-services Switching Centre is an exchange which performs

switching functions for mobile stations located in a geographical area designated as the MSC area.

Mobile-Station-Memory-Capacity-Exceeded-Flag (MCEF): Apart of theMWI to be stored in the HLR.MCEF is a

Boolean parameter indicating if the address list of MWD contains one or more entries because an attempt to deliver a

short message to an MS has failed with a cause of MS Memory Capacity Exceeded.

Mobile-Station-Not-Reachable-Flag (MNRF): The part of the MWI to be stored in the VLR and the HLR. MNRF is a

Boolean parameter indicating if the address list of MWD contains one or more entries because an attempt to deliver a

short message to an MS has failed with a cause of Absent Subscriber.

Mobile-station-Not-Reachable-for-GPRS (MNRG): The part of theMWI to be stored in the SGSN and the HLR.

MNRG is a Boolean parameter indicating if the address list of MWD contains one or more entries because an attempt to

deliver a short message to an MS has failed with a cause of Absent Subscriber.

Mobile-Station-Not-Reachable-Reason (MNRR): The part of the MWI in the HLR which stores the reason for an MS

being absent when an attempt to deliver a short message to an MS fails at the MSC with a cause of Absent Subscriber.

More-Messages-To-Send (MMS): Information element offering an MS receiving a short message from an SC the

information whether there are still more messages waiting to be sent from that SC to the MS. The TP-MMS element

(conveyed in the Transfer layer) is copied into the RP-MMS element (conveyed in the Relay layer). It is possible with

Phase 2 and later versions of MAP (GSM TS 09.02) for the RP-MMS element to keep an SM transaction open between

the GMSC and the MS in the case where there are more-messages-to-send. Earlier versions of MAP will support the

transport of the TP-MMS element.

priority: Service element enabling the SC or SME to request a short message delivery attempt to an MS irrespective of

whether or not the MS has been identified as temporarily absent.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 11 (GSM 03.40 version 7.3.0 Release 1998)

protocol-identifier: Information element by which the originator of a short message (either an SC or an MS) may refer

to a higher layer protocol.

reply path procedure: A mechanism which allows an SME to request that an SC should be permitted to handle a reply

sent in response to a message previously sent from that SME to another SME. This may happen even though the SC may

be unknown to the SME which received the initial message.

report: Response from either the network or the recipient upon a short message being sent from either an SC or an MS.

A report may be a delivery report, which confirms the delivery of the short message to the recipient, or it may be a

failure report, which informs the originator that the short message was never delivered and the reason why.

When issued by the Service Centre, the delivery report confirms the reception of the Short Message by the SC,

and not the delivery of the Short Message to the SME.

When issued by the Mobile Station, the delivery report confirms the reception of the Short Message by the

Mobile Station, and not the delivery of the Short Message to the user.

replace short message type: A range of values in the Protocol Identifier which allows an indication to be sent with a

short message (MT or MO) that the short message is of a particular type allowing the receiving MS or the SC to replace

an existing message of the same type held in the SC, the ME or on the SIM, provided it comes:

- in MT cases: from the same SC and originating address;

- in MO cases: from the same MS.

Service Centre (SC): Function responsible for the relaying and store-and-forwarding of a short message between an

SME and an MS. The SC is not a part of the GSM PLMN, however MSC and SC may be integrated.

Serving GPRS Support Node (SGSN): The Serving GPRS Support Node is an exchange which performs packet

switching functions for mobile stations located in a geographical area designated as the SGSN area.

short message: Information that may be conveyed by means of the Short Message Service described in the present

document.

Short Message Entity (SME): An entity which may send or receive Short Messages. The SME may be located in a

fixed network, an MS, or an SC.

SMS-STATUS-REPORT: Short message transfer protocol data unit informing the receiving MS of the status of a

mobile originated short message previously submitted by the MS, i.e. whether the SC was able to forward the message

or not, or whether the message was stored in the SC for later delivery.

SMS-COMMAND: Short message transfer protocol data unit which enables an MS to invoke an operation at the SC.

An MS may then, for example, delete a short message, cancel a Status Report Request, enquire about the status of a

short message or request another function to be performed by the SC.

The type of operation is indicated by the TP-Command-Type and the particular SM to operate on is indicated by the

TP-Message-Number and the TP-Destination-Address. Receipt of an SMS-COMMAND is confirmed by an RP-ACK or

RP-ERROR. In the case of certain SMS-COMMANDs, an SMS-STATUS-REPORT may be sent, where the outcome of

the SMS-COMMAND is passed in its TP-Status field.

SMS-DELIVER: Short message transfer protocol data unit containing user data (the short message), being sent from an

SC to an MS.

SMS-SUBMIT: Short message transfer protocol data unit containing user data (the short message), being sent from an

MS to an SC.

Service-Centre-Time-Stamp (SCTS): Information element offering the recipient of a short message the information of

when the message arrived at the SM-TL entity of the SC. The time of arrival comprises the year, month, day, hour,

minute, second and time zone.

Validity-Period (VP): Information element enabling the originator MS to indicate the time period during which the

originator considers the short message to be valid.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 12 (GSM 03.40 version 7.3.0 Release 1998)

2.2.2 Abbreviations

For the purposes of the present document, the following abbreviations apply:

ACSE Association Control Service Element

E.163 CCITT Rec. E.163 (Blue Book)

E.164 CCITT Rec. E.164 (Blue Book)

SM MT Short Message Mobile Terminated Point-to-Point

SM MO Short Message Mobile Originated Point-to-Point

SM-AL Short Message Application Layer

SM-TL Short Message Transfer Layer

SM-RL Short Message Relay Layer

SM-LL Short Message Lower Layers

SM-TP Short Message Transfer Layer Protocol

SM-RP Short Message Relay Layer Protocol

SM-TS Short Message Transfer Service

SM-RS Short Message Relay Service

T.100 CCITT Rec. T.100 (Blue Book)

T.101 CCITT Rec. T.101 (Blue Book)

TPDU Transfer protocol data unit

X.121 CCITT Rec. X.121 (Blue Book)

X.400 CCITT Rec. X.400 (Blue Book)

In addition to those above, definitions used in the present document are listed in GSM 01.04.

3 Services and service elements

The SMS provides a means to transfer short messages between a GSM MS and an SME via an SC. The SC serves as an

interworking and relaying function of the message transfer between the MS and the SME.

The present document describes only the short message point-to-point services between the MS and SC. It may,

however, refer to possible higher layer applications.

3.1 Basic services

The short message point-to-point services comprise two basic services:

- SM MT (Short Message Mobile Terminated Point-to-Point);

- SM MO (Short Message Mobile Originated Point-to-Point).

SM MT denotes the capability of the GSM system to transfer a short message submitted from the SC to one MS, and to

provide information about the delivery of the short message either by a delivery report or a failure report with a specific

mechanism for later delivery; see figure 03.40/1.

SM MO denotes the capability of the GSM system to transfer a short message submitted by the MS to one SME via an

SC, and to provide information about the delivery of the short message either by a delivery report or a failure report.

The message must include the address of that SME to which the SC shall eventually attempt to relay the short message;

see figure 03.40/2.

The text messages to be transferred by means of the SM MT or SM MO contain up to 140 octets.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 13 (GSM 03.40 version 7.3.0 Release 1998)

Short message delivery

>

<

SC MS

Report

Figure 03.40/1: The Short Message Service mobile terminated, point-to-point

Short message submission

>

<

SC MS

Report

Figure 03.40/2: The Short Message Service mobile originated, point-to-point

An active MS shall be able to receive a short message TPDU (SMS-DELIVER) at any time, independently of whether

or not there is a speech or data call in progress. A report will always be returned to the SC; either confirming that the

MS has received the short message, or informing the SC that it was impossible to deliver the short message TPDU to the

MS, including the reason why.

An active MS shall be able to submit a short message TPDU (SMS-SUBMIT) at any time, independently of whether or

not there is a speech or data call in progress. A report will always be returned to the MS; either confirming that the SC

has received the short message TPDU, or informing the MS that it was impossible to deliver the short message TPDU to

the SC, including the reason why.

NOTE: When the transmission or reception of a short message coincide with a change of state in the MS, i.e. from

busy to idle or from idle to busy, or during a handover, the short message transfer might be aborted.

It is also possible for two short messages to be received in sequence having the same originating address

and identification, i.e. message reference number (MO) or SC Timestamp (MT). Such a situation may be

due to errors at the RP or CP layers (e.g. during inter MSC handover) where it may be a duplicated

message or otherwise it may be a valid new message.

The receiving entity should therefore make provision to check other parameters contained in the short

message to decide whether the second short message is to be discarded.

3.2 Short Message Service elements

The SMS comprises 7 elements particular to the submission and reception of messages:

- Validity-Period;

- Service-Centre-Time-Stamp;

- Protocol-Identifier;

- More-Messages-to-Send;

- Priority;

- Messages-Waiting;

- Alert-SC.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 14 (GSM 03.40 version 7.3.0 Release 1998)

3.2.1 Validity-Period

The Validity-Period is the information element which gives an MS submitting an SMS-SUBMIT to the SC the

possibility to include a specific time period value in the short message (TP-Validity-Period field, see clause 9). The

TP-Validity-Period parameter value indicates the time period for which the short message is valid, i.e. for how long the

SC shall guarantee its existence in the SC memory before delivery to the recipient has been carried out.

3.2.2 Service-Centre-Time-Stamp

The Service-Centre-Time-Stamp is the information element by which the SC informs the recipient MS about the time of

arrival of the short message at the SM-TL entity of the SC. The time value is included in every SMS-DELIVER

(TP-Service-Centre-Time-Stamp field, see clause 9) being delivered to the MS.

3.2.3 Protocol-Identifier

The Protocol-Identifier is the information element by which the SM-TL either refers to the higher layer protocol being

used, or indicates interworking with a certain type of telematic device.

The Protocol-Identifier information element makes use of a particular field in the message types SMS-SUBMIT, SMSSUBMIT-

REPORT for RP-ACK, SMS-DELIVER DELIVER, SMS-DELIVER-REPORT for RP-ACK,

SMS_STATUS_REPORT and SMS-COMMAND TP-Protocol-Identifier (TP-PID).

3.2.4 More-Messages-to-Send

The More-Messages-to-Send is the information element by which the SC informs the MS that there is one or more

messages waiting in that SC to be delivered to the MS. The More-Messages-to-Send information element makes use of a

Boolean parameter in the message SMS-DELIVER, TP-More-Messages-to-Send (TP-MMS).

3.2.5 Delivery of Priority and non-Priority Messages

Priority is the information element provided by an SC or SME to indicate to the PLMN whether or not a message is a

priority message.

Delivery of a non-priority message will not be attempted if the MS has been identified as temporarily absent (see

subclause 3.2.6).

Delivery of a non-priority message will be attempted if the MS has not been identified as temporarily absent irrespective

of whether the MS has been identified as having no free memory capacity (see subclause 3.2.6).

Delivery of a priority message will be attempted irrespective of whether or not the MS has been identified as temporarily

absent, or having no free memory capacity.

3.2.6 Messages-Waiting

The Messages-Waiting is the service element that enables the PLMN to provide the HLR, SGSN and VLR with which

the recipient MS is associated with the information that there is a message in the originating SC waiting to be delivered

to the MS. The service element is only used in case of previous unsuccessful delivery attempt(s) due to temporarily

absent mobile or MS memory capacity exceeded. This information, denoted the Messages-Waiting-Indication (MWI),

consists of Messages-Waiting-Data (MWD), ), the Mobile-station-Not-Reachable-for-GPRS (MNRG), the

Mobile-Station-Not-Reachable-Flag (MNRF), the Mobile-Not-Reachable-Reason (MNRR) and the

Mobile-Station-Memory-Capacity-Exceeded-Flag (MCEF) located in the HLR; the Mobile-station-Not Reachable-for-

GPRS (MNRG) located in the SGSN, and the Mobile-Station-Not-Reachable-Flag (MNRF) located in the VLR.

figure 03.40/3 shows an example.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 15 (GSM 03.40 version 7.3.0 Release 1998)

...

...

MSIsdn-Alert SC address1 SC address

2

SC addressn

MNRF MNRG

HLR;

MWD:

MNRF

VLR;

MCEF MNRR

MNRG

SGSN;

Figure 03.40/3: Example of how information on one MS can be put in relation to SC(s)

in order to fulfil the requirement of Alert-SC mechanism

The MWD shall contain a list of addresses (SC-Addr) of SCs which have made previous unsuccessful delivery attempts

of a message (see clause 5). In order to be able to send alert messages to every SC which has made unsuccessful delivery

attempts to an MS, the HLR shall store the MSIsdn-Alert (see subclause 3.2.7) together with references to the SC

addresses. The requirements placed upon the HLR are specified in GSM 03.08. The description of how the HLR is

provided with SC and MS address information is given in GSM 09.02.

The Mobile-Station-Memory-Capacity-Exceeded-Flag (MCEF) within the HLR is a Boolean parameter with the value

TRUE an attempt to deliver a short message to an MS has failed with a cause of MS Memory Capacity Exceeded, and

with the value FALSE otherwise.

The Mobile-station-Not Reachable-for-GPRS (MNRG) within the HLR and the SGSN is a Boolean parameter with the

value TRUE when an attempt to deliver a short message to an MS has failed with a cause of Absent Subscriber, and with

the value FALSE otherwise (except as described in note 1 below).

The Mobile-Station-Not-Reachable-Flag (MNRF) within the HLR and the VLR is a Boolean parameter with the value

TRUE when the list MWD contains one or more list elements because an attempt to deliver a short message to an MS

has failed with a cause of Absent Subscriber, and with the value FALSE otherwise.

The Mobile-Station-Not-Reachable-Reason (MNRR) within the HLR stores the reason for the MS being absent when an

attempt to deliver a short message to an MS fails at the MSC, SGSN or both with the cause Absent Subscriber. The HLR

updates the MNRR with the reason for absence when an absent subscriber diagnostic information is received from the

GMSC and the MNRF, MNRG or both are set. The HLR clears the MNRR when the MNRF and MNRG are cleared. If

the MNRF is set due to a failure at the MSC with cause Absent Subscriber and information pertaining to the absence of

the MS is not available from the GMSC, the MNRR will remain in a cleared state. Also, if the MNRG is set due to a

failure at the SGSN with cause Absent Subscriber and information pertaining to the absence of the MS is not available

from the GMSC, the MNRR will remain in a cleared state. The MNRR shall either be in a cleared state or contain one of

the following reasons:

No Paging Response via the MSC;

No Paging Response via the SGSN;

IMSI Detached;

GPRS Detached.

NOTE 1: The MNRG can also be set in the HLR and in the SGSN after an unsuccessful attempt to invoke the

network requested PDP-Context Activation procedure. In this case, no SC address is stored in MWD list

(see TS GSM 03.60).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 16 (GSM 03.40 version 7.3.0 Release 1998)

NOTE 2: When a short message delivery attempt fails at the HLR due to Roaming being Restricted, the MS being

deregistered in HLR or the MS being Purged the absent subscriber diagnostic reason is returned to the SC,

however the reason is not stored in the MNRR.

The MWD, MCEF, MNRR, MNRG and MNRF are updated in the following way:

1a)When a mobile terminated short message delivery fails due to the MS being temporarily absent (i.e. either IMSI

DETACH flag is set or there is no response from the MS to a paging request via the MSC), the SC address is

inserted into the MWD list (if it is not already present), the MNRF is set (if it is not already set) and the MNRR

via the MSC is updated (if the information is available), as described in clause 10.

1b)When a mobile terminated short message delivery fails due to the MS being temporarily absent (i.e. either GPRS

DETACH flag is set or there is no response from the MS to a paging request via the SGSN), the SC address is

inserted into the MWD list (if it is not already present), the MNRG is set (if it is not already set) and the MNRR

via the SGSN is updated (if the information is available), as described in clause 10.

1c)When a mobile terminated short message delivery fails due to the MS memory capacity via the MSC being

exceeded, the SC address is inserted into the MWD list (if it is not already present) ,the MCEF is set (if it is not

already set), the MNRF is cleared and the MNRR via the MSC is updated as described in clause 10.

1d)When a mobile terminated short message delivery fails due to the MS memory capacity via the SGSN being

exceeded, the SC address is inserted into the MWD list (if it is not already present), the MCEF is set (if it is not

already set), the MNRG is cleared and the MNRR via the SGSN is updated as described in clause 10.

1e) If the MSIsdn used by the SC to address the recipient MS for alerting purposes is different from the

MSIsdn-Alert of the MS (see subclause 3.2.7), the HLR returns the MSIsdn-Alert to the SC within the failure

report, see "1c Failure report" in figures 03.40/15 and /16.

2a)When either the HLR or VLR detects that the MS (with a non-empty MWD and the MCEF clear in the HLR and

the MNRF set in the VLR) has recovered operation (e.g. has responded to a paging request over MSC), the HLR

directly or on request of the VLR will invoke operations to alert the SCs within the MWD (see subclause 3.2.7

and clause 10). Once the Alert SC operations have been invoked, the MNRF and MNRR via the MSC are

cleared. After each SC is alerted by the HLR, the address for that SC is deleted from the MWD. If the MCEF is

set in the HLR, the HLR clears the MNRF and MNRR via the MSC, but does not invoke operations to alert the

SCs within the MWD and data are not cleared from the MWD.

2b)When either the HLR or SGSN detects that the MS (with a non-empty MWD and the MCEF clear in the HLR

and the MNRG set in the SGSN) has recovered operation (e.g. has responded to a paging request via the SGSN),

the HLR directly or on request of the SGSN will invoke operations to alert the SCs within the MWD (see

subclause 3.2.7 and clause 10). Once the Alert SC operations have been invoked, the MNRG and MNRR via the

SGSN are cleared. After each SC is alerted by the HLR, the address for that SC is deleted from the MWD. If the

MCEF is set in the HLR, the HLR clears the MNRG and MNRR via the SGSN, but does not invoke operations to

alert the SCs within the MWD and data are not cleared from the MWD.

2c)When the HLR receives (via the MSC and the VLR) a notification that the MS (with a non-empty MWD and the

MCEF set in the HLR) has memory capacity available to receive one or more short messages, the HLR will

invoke operations to alert the SCs within the MWD (see subclause 3.2.7 and clause 10). Once the Alert SC

operations have been invoked, the MNRF is cleared in the VLR and the MCEF, MNRF and MNRR via the MSC

are cleared in the HLR. After each SC is alerted by the HLR, the address for that SC is deleted from the MWD.

2d)When the HLR receives (via the SGSN) a notification that the MS (with a non-empty MWD and the MCEF set in

the HLR) has memory capacity available to receive one or more short messages, the HLR will invoke operations

to alert the SCs within the MWD (see subclause 3.2.7 and clause 10). Once the Alert SC operations have been

invoked, the MNRG is cleared in the SGSN and the MCEF, MNRG and MNRR via the SGSN are cleared in the

HLR. After each SC is alerted by the HLR, the address for that SC is deleted from the MWD.

2e)When the HLR receives from the SMS-GMSC a notification that a short message has been successfully delivered

from an SC to an MS via the MSC for which the MCEF is set and the MWD are not empty, the HLR will invoke

operations to alert other SCs within the MWD (see subclause 3.2.7 and clause 10). Once the Alert SC operations

have been invoked, the MCEF, MNRF and MNRR via the MSC are cleared in the HLR. After each SC is alerted

by the HLR, the address for that SC is deleted from the MWD. The SC which successfully delivered the message

is also deleted from the MWD, if present.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 17 (GSM 03.40 version 7.3.0 Release 1998)

2f) When the HLR receives from the SMS-GMSC a notification that a short message has been successfully delivered

from an SC to an MS via the SGSN for which the MCEF is set and the MWD are not empty, the HLR will invoke

operations to alert other SCs within the MWD (see subclause 3.2.7 and clause 10). Once the Alert SC operations

have been invoked, the MCEF, MNRG and MNRR via the SGSN are cleared in the HLR. After each SC is

alerted by the HLR, the address for that SC is deleted from the MWD. The SC which successfully delivered the

message is also deleted from the MWD, if present.

2g)When the HLR receives (via the MSC and the VLR, or the SGSN) a notification that the MS has memory

capacity available to receive one or more short messages but the MCEF is not set and the MWD are empty, the

HLR acknowledges the notification but does not alert any service centre.

NOTE 1: The HLR can be in a situation where the MWD list is empty but where either MNRF or MNRG (with the

related MNRR) is still set. This enables the HLR to return the correct address (MSC or SGSN address) at

the next Send Routing Information Request from the SMS-GMSC.

NOTE 2: If the SMS delivery failed on first attempt via the MSC or the SGSN (see cases 1a for IMSI Detach and 1b

for GPRS Detach), and is successful on the second attempt (see cases 2e and 2f), the SC address shall not be

inserted into the MWD list

3.2.7 Alert-SC

The Alert-SC is the service element, which may be provided by some GSM PLMNs, to inform the SC that an MS

1) to which a delivery attempt has failed because the MS is not reachable or because the MS memory capacity was

exceeded;

and

2) which is now recognized by the PLMN:

a) to have resumed operation (e.g. to have responded to a paging request); or

b) to have memory newly available (which implies that the mobile is reachable).

is again ready to receive one or more short messages. The SC may - on reception of an Alert-SC - initiate the delivery

attempt procedure for the queued messages destined for this MS.

To each MS there may be allocated several MSIsdns. When the HLR is to alert an SC that an MS is again attainable it

will use a specific MSIsdn value for this purpose; in the present document called MSIsdn-Alert.

NOTE: Repeated delivery attempts from the SC may be of two types:

i) A repeated delivery attempt because the SC has been informed that the MS is active and available to

receive short messages.

ii) An autonomous repeated delivery attempt by the SC.

The application of these two options is defined by the providers of the SC and the network.

3.2.8 Options concerning MNRG, MNRF, MNRR, MCEF and MWD

Setting the Mobile-Station-Not-Reachable-Flag (MNRF) in the VLR is mandatory. Setting the Mobile-station-Not-

Reachable-for-GPRS (MNRG) in the SGSN is mandatory. It is mandatory for the VLR or the SGSN to send the "MS

Reachable" message (see clause 10) to the HLR when the MS has been detected as becoming active and then to clear

MNRF in the VLR or the MNRG in SGSN.

The Messages-Waiting-Data (MWD), the Mobile-Station-Not-Reachable-Flag (MNRF), the Mobile-station-Not-

Reachable-for-GPRS (MNRG), the Mobile-Station-Not-Reachable-Reason (MNRR) and the

Mobile-Station-Memory-Capacity-Exceeded-Flag (MCEF)) within the HLR are optional, but if one is implemented all

must be implemented (except MNRG if the HLR does not support GPRS). This is linked to the transmission of the

"Alert SC" message.

The following describes what happens when a delivery fails.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 18 (GSM 03.40 version 7.3.0 Release 1998)

Case 1: MWD, MNRF, MNRG, MNRR and MCEF are implemented in the HLR

In the case of a delivery failure (to an MS) with cause Absent Subscriber, the SMS-GMSC requests the HLR to

add, if needed, a new entry in the MWD with cause Absent Subscriber. This new entry contains the SC address.

The HLR sets its copy of the MNRF, MNRG or both and updates the MNRR (if the information is available).

The SC is notified of the failure, the reason for the MS being absent and also of the MWD setting in the HLR

within the Report message (see clause 10).

In the case of a delivery failure (to an MS) with cause Mobile Station Memory Capacity Exceeded via the SGSN

or the MSC, the SMS-GMSC requests the HLR to add, if needed, a new entry in the MWD with cause Mobile

Station Memory Capacity Exceeded. This new entry contains the SC address. The HLR sets the MCEF and reset

MNRF or MNRG. The SC is notified of the failure and also of the MWD setting in the HLR within the Report

message (see clause 10).

If the HLR indicates that it is able to store the SC address, then the SC will receive an Alert SC message when the

MS becomes active.

If the HLR indicates that it is unable to store the SC address (e.g. because MWD is full), then the only way to

ensure delivery is for the SC to try to retransmit the message periodically.

When the HLR receives the MS Reachable message, if the MCEF is clear it sends an Alert SC message to the

concerned SC, updates MWD and clears MNRF (if the MS is reachable via the MSC) or MNRG (if the MS is

reachable via the SGSN).

When the HLR receives the MS Memory Capacity Available message, it sends an Alert SC message to the

concerned SC, updates MWD, clears the MCEF and clears MNRF (if the MS is reachable via the MSC) or

MNRG (if the MS is reachable via the SGSN).

Case 2: MWD, MNRF, MNRG, MNRR and MCEF are not implemented in the HLR

In the case of a delivery failure, the SC is notified that the HLR is unable to store its address in the MWD. In case

of a delivery failure (to a MS) with cause Absent Subscriber, the SC is notified of the reason for the MS being

absent (if the information is available). The SC must retransmit the short message periodically in order to ensure

delivery.

The HLR discards the MS Reachable message received from the VLR or SGSN without any failure or error

report.

The HLR discards the MS Memory Capacity Available message received from the MS via the MSC and the VLR

or SGSN without any failure or error report.

3.2.9 Status report capabilities

The SMS also offers to the SC the capabilities of informing the MS of the status of a previously sent mobile originated

short message. The status of the message can be:

- Successfully delivered to the SME;

- The SC was not able to forward the message to the SME. The reason can be an error of permanent or temporary

nature. Permanent errors can be e.g. validity period expired, invalid SME address. Errors of temporary nature can

be e.g. SC-SME connection being down, SME temporarily unavailable.

This is achieved by the SC returning a status report TPDU (SMS-STATUS-REPORT) to the originating MS when the

SC has concluded the status of the short message. The status report may be initiated by a status report request within the

mobile originated short message. The status report TPDU is treated as an SMS-DELIVER TPDU by the SC when it

comes to delivery procedures e.g. the alerting mechanism.

The SC may also return to a non-MS SME the status of a mobile terminated short message. This is however outside the

scope of the present document.

The status report capabilities of the SMS are optional, i.e. the choice of whether to offer status report or not is left to the

SC operator.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 19 (GSM 03.40 version 7.3.0 Release 1998)

For reasons of resilience and/or load sharing architecture of SMSC's by network operators, the SMSC address (the

RP-OA) used by the SMSC to send the Status Report to the MS cannot be guaranteed to be the same SMSC address

(RP-DA) used by the MS to submit the SM to which the Status Report refers. Where an MS wishes to implement a

check that these addresses correlate, a means of disabling the correlation check shall be provided at the MS through

MMI.

3.2.10 Reply Path

Reply Path specified in the present document provides a way of both requesting and indicating a service centre's

commitment to deliver a reply from the replying MS to the originating SME.

Annex D deals with MS procedures, which in general are outside the scope of GSM specifications. However, for

advanced use of the SMS, including both application level protocols and human responses, it is of vital importance to

guarantee that a reply-supporting MS is able to reply on every SM, to every SME capable of receiving such reply short

messages.

3.3 Unsuccessful short message TPDU transfer SC -> MS

Unsuccessful message transfer SC -> MS may be caused by a variety of different errors. The description of the

occurrence of the different errors and how to handle and transfer the error indications is given in GSM 04.08,

GSM 04.11 and GSM 09.02.

The different error indications which the SMS-GMSC shall be capable of returning to the SC following an unsuccessful

short message TPDU transfer SC -> MS, are given in table 03.40/1. In some cases, additional diagnostic information

may be provided.

3.3.1 Errors occurring during transfer of TPDU to MS

These errors are generally due to barring or unsupported service in the PLMN or MS. An error indication is returned to

the SC from the SMS-GMSC, but further diagnostic information from the MS will not be available.

3.3.2 Errors occurring after TPDU arrives at MS

These errors may occur due to the MS not supporting optional short message service features, or in connection with a

short message application. An error indication shall be returned to the SC from the SMS-GMSC. Additionally, a TPDU

(SMS-DELIVER-REPORT) containing diagnostic information may be conveyed from the MS to the originating SC,

transparently through the PLMN, by means defined in GSM 04.11 and GSM 09.02. The sending of the diagnostic

information is optional at the MS, but when it is sent, the PLMN shall convey the information to the SC, and the SC

shall support reception of the information.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 20 (GSM 03.40 version 7.3.0 Release 1998)

Table 03.40/1: Error indications related to mobile terminated short message transfer

which may be transferred to the originating SC

Error indication S1) Meaning

Unknown subscriber P The PLMN rejects the short message TPDU because there is not allocated

an IMSI or a directory number for the mobile subscriber in the HLR (see

GSM 09.02).

Teleservice not provisioned P The PLMN rejects the short message TPDU because the recipient MS has

no SMS subscription (see GSM 09.02).

Call barred T The PLMN rejects the short message TPDU due to barring of the MS (see

GSM 09.02, description of the Barring supplementary service, GSM 02.04

and 03.11), description of Call barred due to Unauthorised Message

Originator, GSM 09.02, and description of Operator Determined Barring,

GSM 02.41 and 03.15).

Facility not supported T The VPLMN rejects the short message TPDU due to no provision of the

SMS in the VPLMN (see GSM 09.02).

Absent subscriber T The PLMN rejects the short message TPDU because

- there was no paging response via the SGSN, MSC or both, (see

GSM 04.08 & GMS 09.02)

- the IMSI GPRS or both records are marked detached (see GSM 09.02),

- the MS is subject to roaming restrictions (see "Roaming not allowed",

GSM 09.02).

- deregistered in the HLR. The HLR does not have an MSC, SGSN or both

numbers stored for the target MS, (see GSM 09.02)

- Unidentified subscriber (see GSM 09.02)

- MS purged, (see GMS 09.02)

(The reasons for absence are assigned integer values in table 03.40/1a. The

appropriate integer value is sent with the absent subscriber error indication

as defined in GSM 09.02)

MS busy for MT SMS T The PLMN rejects the short message TPDU because of congestion

encountered at the visited MSC or the SGSN. Possible reasons include any

of the following events in progress:

- short message delivery from another SC;

- IMSI or GPRS detach

- Location Update or Inter SGSN Routing Area Update;

- paging;

- emergency call;

- call setup.

SMS lower layers

capabilities not provisioned

T The PLMN rejects the short message TPDU due to MS not being able to

support the Short Message Service.

The short message transfer attempt is rejected either due to information

contained in the class-mark, or the MSC not being able to establish

connection at SAPI = 3 (see GSM 04.08 and GSM 09.02).

Error in MS T The PLMN rejects the short message TPDU due to an error occurring within

the MS at reception of a short message, e.g. lack of free memory capacity or

protocol error.

Illegal Subscriber P The PLMN rejects the short message TPDU because the MS failed

authentication

Illegal Equipment P The PLMN rejects the short message TPDU because the IMEI of the MS

was black-listed in the EIR

System failure T The PLMN rejects the short message TPDU due to network or protocol

failure others than those listed above (see GSM 09.02)

Memory Capacity Exceeded T The MS rejects the short message since it has no memory capacity

available to store the message

1) : Status (Permanent or Temporary)

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 21 (GSM 03.40 version 7.3.0 Release 1998)

The relation between the two sets of error indications is given in the table 03.40/1. Each error is classified as either

"Temporary" or "Permanent". This classification gives an indication of whether or not it is probable that the MS

becomes attainable within a reasonable period, and so provides the recommended action to be taken by the SC, i.e.

either to store the message for later transfer, or to discard it.

Table 03.40/1a: Assignment of values to reasons for absence ( values must be in the range of 0 to

255, see GSM 09.02)

Values Reason for absence

0 - no paging response via the MSC

1 - IMSI detached

2 - roaming restriction

3 - deregistered in the HLR for non

GPRS

4 - MS purged for non GPRS

5 - no paging response via the

SGSN

6 - GPRS detached

7 - deregistered in the HLR for

GPRS

8 - MS purged for GPRS

9 - Unidentified subscriber via the

MSC

10 - Unidentified subscriber via the

SGSN

All ´non GPRS´ reasons (except for roaming restriction) can be combined with all

´GPRS´ reasons and vice-versa

All other integer values are reserved.

3.4 Unsuccessful short message TPDU transfer MS -> SC

The error indications related to mobile originated short message transfer which may be transferred to the originating MS

are given in GSM 04.11. In some cases, additional diagnostic information may be provided.

3.4.1 Errors occurring during transfer of TPDU to SC

These errors are generally due to barring or unsupported service in the PLMN. An error indication is returned to the MS

from the MSC or the SGSN, but further diagnostic information from the SC will not be available.

3.4.2 Errors occurring after TPDU arrives at SC

These errors may occur due to the SC not supporting optional short message service features, or in connection with a

short message application. An error indication shall be returned to the MS from the MSC or from the SGSN.

Additionally, a TPDU (SMS-SUBMIT-REPORT) containing diagnostic information may be conveyed from the SC to

the originating MS, transparently through the PLMN, as defined in GSM 09.02 and GSM 04.11. The sending of the

diagnostic information is optional at the SC, but when it is sent, the PLMN shall convey the information to the MS, and

the MS shall support reception of the information.

NOTE: The SMS-SUBMIT-REPORT is part of the negative acknowledgement to the mobile originated short

message, and is not part of the status report capabilities described in subclause 3.2.9.

3.5 Use of Supplementary Services in combination with the

Short Message Service

Only a sub-set of the Supplementary Services defined in GSM 02.04 and 03.11 may be used in combination with the

Short Message Service. This sub-set comprises the following Supplementary Services:

All the 5 Barring services.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 22 (GSM 03.40 version 7.3.0 Release 1998)

3.6 Applicability of Operator Determined Barring to the Short

Message Service

The network feature Operator Determined Barring (see GSM 02.41) applies to the Short Message Service.

If a short message fails due to operator determined barring then an appropriate error cause is returned to the originator.

3.7 Multiple short message transfer

To avoid the need for a mobile to be paged, authenticated etc. for each message waiting in the Service Centre, the SC

may indicate to the SMS-GMSC that there are more messages to send. When this indication is given, MAP procedures

are invoked such that this indication is passed to the VMSC, and the VMSC does not release the MS until all short

messages waiting in the SC have been transferred.

3.8 SMS and Internet Electronic Mail interworking

The interworking between Internet electronic mail and SMS is offered in both directions which enables new and old

mobiles to send/receive Internet electronic mails via SMS. The interworking is according to the following procedures:

- An SMS message which is required to interwork with Internet email may have its TP-PID value set for Internet

electronic mail;

- Either single or concatenated SMS can be used to transport the email;

- Concatenation may be achieved by the TPUDH mechanism or text-based means described below;

- Email cc fields are not supported;

- Where multiple fields are present, additional spaces may be inserted by the sender to improve presentation of the

message. Spaces may not be inserted into the actual email address (e.g. user@domain1.domain2).

3.8.1 Basic Format

The basic format for transferring email in either direction consists of the following:

MT SMS:

[<from-address><space>]<message>

MO SMS:

[<to-address><space>]<message>

where [] denote optional fields and <> delimit fields.

The to-address or from address may take the form

user@domain1.domain2

or

User Name <user@domain1.domain2>

In the latter case the angle brackets <> are part of the address and are actually transmitted.

Depending on the nature of the gateway, the destination/origination address is either derived from the content of the

SMS TP-OA or TP-DA field, or the TP-OA/TP-DA field contains a generic gateway address and the to/from address is

added at the beginning as shown above.

Multiple addresses may be identified in MO messages by separating each address by a comma like this:

address1,address2,address3<space><message>

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 23 (GSM 03.40 version 7.3.0 Release 1998)

It is optional for the receiving gateway to support this. If the receiving gateway does not support multiple messages then

it shall reject the original message by returning an appropriate error in a text message.

3.8.2 Optional Fields

The following further optional fields are supported. An email <-> SMS gateway may insert additional spaces in the MT

message for presentation to the user, and must accept additional spaces in the MO message from the user.

3.8.2.1 Subject

The subject is placed between the address and the message, delimited by round brackets () or preceded by ##, for

example:

[<to-address>](<subject>)<message>

or

[<to-address>]##<subject>#<message>

An MO message may contain either format. An MT message may contain either format. Developers must ensure that

both forms are supported for full compatibility.

3.8.2.2 Real Name

The Real Name field contains the real name of the sender and is used only in MO messages. The SC or email gateway

will generate an email message according to standard email procedures containing Real Name

<user@domain1.domain2> (the angle brackets being part of the address and hence transmitted). If a subject is to be

included with the Real Name then only the ## prefix is used.

The syntax is:

[<to-address>]#<real-name>[##<subject>]#<message>

3.8.2.3 Optional Control Flag

An optional control flag may be added to the start of the message in MO messages only. This consists of a single

character <CF> following a # symbol as follows:

[#<CF>#][<to-address>]<space><message>

This may also be used in combination with the above fields. It is intended for use where a particular SC or email

gateway specific function is required to be invoked. For example, the control flag #A# might add a particular

(pre-stored) signature to the end of the message or #R# might change the from-address to a pre-stored value or #5#

might add the text "Please phone me at the office". All of these functions are open for definition by Service Centre or

email gateway operators.

3.8.3 Text concatenation

If the GSM binary concatenation protocol is not supported by the transmitting or receiving entity, the following textual

concatenation mechanism may be used. The first message is ended with a + sign, and each subsequent message start and

end with + signs until the final message which starts with a + sign but does not end with a + sign.

<message1>+

+<message2>+

+<message3>

Any header fields placed on the front of an MO or MT message are not added to the second and subsequent messages.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 24 (GSM 03.40 version 7.3.0 Release 1998)

This provides a simple mechanism which is completely backward compatible. There is no indication of the number of

messages and should a message be lost by the system or arrive out of sequence then the original message cannot be

reconstructed. Therefore, wherever possible the GSM binary concatenation mechanism specified in

subclause 9.2.3.24.1 should be used instead.

3.8.4 Alternative characters for Internet email addresses in MO SMS

It is difficult or impossible to generate some characters on a mobile phone and so the following alternatives may be

used:

@ may be replaced by *

_ (underscore) may be replaced by $

3.9 SMS COMPRESSION

Short Messages may be compressed in accordance with the compression algorithm described in GSM 03.42.

Compression and Decompression may take place between SME's or between an SME and the SC.

The compression only applies to the TP-User-Data part of the TPDU and excludes any TP-User-Data-Header which

may be present. The Compression Header ( see GSM 03.42 ) must commence at the first octet of the TP-User-Data field

immediately following any TP-User-Data-Header field which may be present.

The TP-UDL value must be set in accordance with that value defined for the compressed TP-User-Data case in

subclause 9.2.3.16.

The TP-DCS parameter indicates whether or not a short message is compressed. If the TP-DCS parameter indicates that

the short message is compressed then the alphabet encoding values ( bits 2 and 3 in GSM 03.38 ) must be ignored by the

receiving entity.

In the case where a short message after compression is greater than 140 octets (including the Compression Header and

Footer ( see GSM 03.42 ) and any TP-User-Data-Header which may be present ) then the sending entity must

concatenate the short message in the normal way as described in subclause 9.2.3.24.1 if it wishes to continue to send the

short message. Only the first segment of the concatenated short message must contain the Compression Header defined

in GSM TS 03.42. All segments other than the final segment must be 140 octets in length. Only the final segment

contains the Compression Footer ( see GSM 03.42 ).

For mobile terminated compressed messages, where the MMI or the Message Class indicated in the TP-DCS requires

the message to be stored in the MS then the MS shall store the compressed message as received. In the case where the

MS is capable of decompression then the MS may display the decompressed message. Such an MS may optionally store

the message in decompressed form subject to the MS being configured to do this via MMI. However, prior to storing

the message in decompressed form, the MS may have to create a concatenated SM and carry out component

modification on the TP-UDL and TP-DCS values to indicate the correct length values and that the message is no longer

compressed. Transfer of messages direct from the radio interface or those stored in the MS to a TE is according to the

procedure defined in GSM 07.05 and is independent of whether the message is compressed or uncompressed.

For mobile originated compressed messages, an MS capable of compression may compress a short message generated

within the MS itself prior to sending it to the radio interface. An MS capable of compression may optionally compress

an uncompressed message received from a TE subject to the MS being configured to do this via MMI. In such a case the

MS would have to carry out component modification on the TP-UDL and TP-DCS values to indicate the correct length

values and that the message is compressed. A TE may send a message ( compressed or uncompressed ) to the MS using

the procedures defined in GSM 07.05. The MS will store the compressed message as received and/or transfer it directly

to the radio interface.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 25 (GSM 03.40 version 7.3.0 Release 1998)

4 Network architecture

4.1 Basic network structure

The exchange of messages between an MS and an SME involves the entities shown in figure 03.40/4.

The basic network structure of the SMS is depicted in figure 03.40/5.

..

SME SC MSC/SGSN** MS

SMS-GMSC /

SMS-IWMSC *

Outside the scope of the GSM

specifications

Inside the scope of the GSM

specifications

> <

*) : SMS-GMSC when the short message is transferred from the SC to the MS, SMS-IWMSC when the short

message is transferred from the MS to the SC. The SC may be integrated with the

SMS-GMSC/SMS-IWMSC.

**): SGSN is used in place of the MSC in case of SMS transfer over GPRS

Figure 03.40/4: Entities involved in the provision of SM MT and SM MO: SC, SMS-GMSC/SMS-IWMSC,

SGSN, MSC and MS

The links of figure 03.40/5 support the short message transfer in the following way:

- message transfer on link 1 is described in clause 5;

- the operations performed on links 2 and 4 is described in GSM 09.02;

- message transfer on link 3 is described in subclause 4.2;

- message transfer on link 5 is supported by protocol described in GSM 04.11.

SC MSC/SGSN MS

SMS-GMSC /

SMS-IWMSC

HLR VLR

↑↑

< > > > < <

1. 3. 5.

2. 4.*

<

<

*): This interface is not used in case of SMS transfer via the SGSN

Figure 03.40/5: The main network structure serving as a basis for the short message transfer

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 26 (GSM 03.40 version 7.3.0 Release 1998)

4.2 Transfer on link 3

The link 3 is used to support communications between MSC, SMS-GMSC and SMS-IWMSC, or between SGSN, SMSGMSC

and SMS-IWMSC. Two cases can be distinguished according to whether or not the MSC, SMS-GMSC, SMSIWMSC

and SGSN are located in the same PLMN.

In the first case, the link definition is left to the operators. For example, this link may use:

- PSPDNor

- CCITT SS no 7 (according to GSM 09.02).

In the second case, CCITT SS no 7 shall be used over link 3 according to GSM 09.02, unless otherwise bilaterally

agreed.

5 Service Centre and PLMN interconnection

The present document deals with the SC only with regard to the interchange of messages between SC and MS. Only the

requirements put upon the SC by the SMS functionality are specified in the present document.

5.1 Service centre connection

One SC may be connected to several PLMNs, and may be connected to several MSCs (SMS-GMSCs or SMS-IWMSCs)

within one and the same PLMN.

The SC is addressed from the mobile by an E.164 number in the numbering plan of the PLMN to which the SC is

connected. This E.164 number shall uniquely identify the SC to that PLMN.

There may be an intermediate network between the PLMN and the SC; in this case the PLMN must autonomously make

a connection to the SC using the SC address in this intermediate network.

No mandatory protocol between the SC and the MSC below the transfer layer is specified by GSM; this is a matter for

agreement between SC and PLMN operators. However, annex A provides an example protocol stack which could be

used.

5.2 Routing requirements

5.2.1 Mobile terminated short message

The SC sends the short message to the SMS-GMSC. The SMS-GMSC interrogates the HLR to retrieve routing

information necessary to forward the short message, and then sends the message to the relevant MSC or SGSN,

transiting other networks if necessary. The MSC or SGSN then sends the short message to the MS.

5.2.2 Mobile originated short message

The MS sends the short message to the MSC or the SGSN. The MS will always address the required SC by an E.164

address. The visited PLMN will route the message to the appropriate SMS-IWMSC in the SC's PLMN, transiting other

networks if necessary.

6 Service Centre functionality

In the present document, only the SC functionality related to the short message point-to-point service between the SC

and the MS is specified.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 27 (GSM 03.40 version 7.3.0 Release 1998)

6.1 Service Centre capabilities

The SC should be capable of

- submitting a short message to an MS, retaining the responsibility of the message until

1) the report has been received; or

2) the Validity-Period expires.

- receiving a report from the PLMN;

- receiving a short message from an MS;

- returning a report to the PLMN for a previously received short message.

6.2 SC functional requirements

The detailed functionality of the SC is outside the scope of the present document, and is for the SC operator to define.

However, the following functional requirements are mandatory for all SCs in order to support the SM-TP (see clause 9)

towards the PLMN:

1) To identify each SMS-DELIVER sent to an MS in a unique way, a time stamp value is included in the field

TP-Service-Centre-Time-Stamp, TP-SCTS, of the SMS-DELIVER. The time stamp gives the time when the

message arrived at the SC with the accuracy of a second. If two or more messages to the same MS arrive at the

SC within one second, the SC shall modify the time stamp of those messages in such a way that

a) all messages to the MS contain different time stamps;

b) the modification of the time stamps is kept to a minimum.

2) The SC is only allowed to have one outstanding SMS-DELIVER (i.e. a message for which a report has not been

received) to a specific MS at a given time.

3) The SC shall be able to initiate overwriting of short messages previously received by the SC if requested by the

same originating address (MS or any other source) by use of the same message type.

7 MS functionality

In the present document, only the MS functionality related to the short message point-to-point service between the SC

and the MS is specified.

7.1 MS capabilities

The MS, when equipped for SMS, should be capable of

- submitting a short message TPDU to an SC, retaining the responsibility of the message until:

1) the report arrives from the network; or

2) a timer expires.

- receiving a short message TPDU from an SC;

- returning a delivery report to the network for a previously received short message;

- receiving a report from the network;

- notifying the network when it has memory capacity available to receive one or more short messages when it has

previously rejected a short message because its memory capacity was exceeded;

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 28 (GSM 03.40 version 7.3.0 Release 1998)

- notifying the SC when a short message is intended to replace a short message the MS has previously submitted to

the same destination address.

It is recommended that an MS supporting both replying and automatic SC selection (as specified in clause D.2 of

annex D) follows procedures specified in annex D when replying to MT short messages with MO short messages.

It is recommended that an MS supporting a capability for requesting a reply path follows procedures specified in

annex D.

7.2 MS configuration

The reference configuration is assumed as in figure 03.40/6, i.e. only the case where the terminal is integrated in the MS

is considered.

MTO

Um

Figure 03.40/6: Reference configuration of the MS which apply to the SMS

NOTE: It is foreseen that a terminal interface may be offered, e.g. for higher layer protocols, memory capacity

reasons or to be able to type in mobile originated messages. This terminal interface is regarded as an

implementation option, although, where offered, it must be based upon an R- or S-reference point.

GSM 07.05 provides an example based on the R reference point.

8 Node functionality

The overall requirements to the MSC, SMS-GMSC, SMS-IWMSC and SGSN with respect to handling of the Short

Message Service point-to-point is to cater for the routing and necessary intermediate buffering of the short messages.

8.1 Node functionality related to SM MT

8.1.1 Functionality of the SMS-GMSC

When receiving a short message TPDU from the SC, the SMS-GMSC is responsible for the following operations:

- reception of the short message TPDU;

- inspection of the parameters.

NOTE: The SMS-GMSC may be identical to the MSC.

if parameters are incorrect:

- returning the appropriate error information to the SC in a failure report (see clauses 9 and 10);

if errors are not found within parameters:

- interrogating the HLR ("sendRoutingInfoForShortMsg", see clause 10); retrieving routing information or possible

error information;

if HLR is returning error information:

- returning the appropriate error information to the SC in a failure report (see clauses 9 and 10);

if no errors are indicated by the HLR:

- transferring the short message TPDU to the MSC or SGSN using the routing information obtained from the HLR

("forwardShortMessage", see clause 10).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 29 (GSM 03.40 version 7.3.0 Release 1998)

NOTE: In case where two addresses (SGSN and MSC) are received from HLR, the SMS-GMSC may choose

(operator dependant) via which nodes (SGSN or MSC) the SMS is first to be sent. The SMS delivery via

the SGSN is normally more radio resource efficient than the SMS delivery via the MSC.

if one address (SGSN or MSC) is received from HLR:

- When receiving the report associated with the short message from the MSC or SGSN (positive or negative

outcome of "forwardShortMessage", see clause 10), the SMS-GMSC is responsible for the following operations:

if the report indicates successful delivery:

- notifying the HLR of the successful delivery via the MSC or the SGSN, which will cause the HLR to alert any

service centres whose addresses are stored in the MWD for the MS;

- creating and sending the successful report to the SC;

if the report is a failure report indicating "absent subscriber" via the MSC or the SGSN (see subclause 3.3):

- requesting the HLR to insert the address of the originating SC into the MWD (if implemented) with cause

Absent Subscriber ("SM_DeliveryReportStatus", see clauses 9 and 10);

- informing the HLR of the reason for the MS being absent via the MSC or the SGSN (if this information is

available);

- establishing, where necessary, a link with the addressed SC (see clause 5);

- creating and sending the negative report to the SC which should include the reason for the MS being absent

(if this information is available) so that the SC may adjust any retry algorithm appropriately (see clauses 9 and

10);

if the report is a failure report indicating "MS memory capacity exceeded" via the MSC or the SGSN (see

subclause 3.3):

- requesting the HLR to insert the address of the originating SC into the MWD (if implemented) with cause MS

Memory Capacity Exceeded via the MSC or the SGSN ("SM_DeliveryReportStatus" , see clauses 9 and 10);

- establishing, where necessary, a link with the addressed SC (see clause 5);

- creating and sending the report to the SC (see clauses 9 and 10).

if two addresses (SGSN and MSC) are received from HLR:

- When receiving the first report associated with the short message from the MSC or SGSN (positive or negative

outcome of "forwardShortMessage", see clause 10), the SMS-GMSC is responsible for the following operations:

if the first report indicates successful delivery:

- notifying the HLR of the successful delivery via the MSC or the SGSN, which will cause the HLR to alert any

service centres whose addresses are stored in the MWD for the MS;

- creating and sending the successful report to the SC;

if the first report is a failure report indicating

- Unidentified subscriber

- Facility not supported

- Absent subscriber with indication: GPRS or IMSI Detach

- System failure

- Unexpected data value

- Data missing

- GPRS connection suspended (see TS GSM 09.02) :

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 30 (GSM 03.40 version 7.3.0 Release 1998)

- transferring the short message TPDU to the second path using the routing information obtained from HLR.

if the second report indicates successful delivery:

- notifying the HLR of the successful delivery of the second transfer via the MSC or SGSN, which will

cause the HLR to alert any service centres whose addresses are stored in the MWD for the MS;

- notifying the HLR of the unsuccessful delivery at first transfer only with cause "absent subscriber";

- notifying the HLR of the reason for the MS being absent via the MSC or the SGSN (if this information is

available);

- establishing, when necessary, a link with the addressed SC (see clause 5);

- creating and sending the successful report to the SC;

if the second report is a failure report:

- requesting the HLR to insert the address of the originating SC into the MWD (if implemented) only if at

least one of the first or second report failed due to "MS Memory Capacity Exceeded" or "Absent

Subscriber" ("SM_DeliveryReportStatus", see clauses 9 and 10);

- notifying the HLR only with the causes "Absent Subscriber", "Memory Capacity Exceeded" via the MSC

or the SGSN, or both;

- notifying the HLR of the reason for the MS being absent via the MSC, SGSN or both (if this information

is available);

- establishing, where necessary, a link with the addressed SC (see clause 5);

- creating and sending the negative report to the SC with errors from first and second path (see clauses 9

and 10);

8.1.2 Functionality of the MSC

When receiving a short message TPDU from the SMS-GMSC ("forwardShortMessage", see clause 10), the MSC is

responsible for the following operations:

- reception of the short message TPDU;

- retrieving information from the VLR ("sendInfoFor-MT-SMS", see clause 10); location area address and, when

appropriate, error information;

if errors are indicated by the VLR:

- returning the appropriate error information to the SMS-GMSC in a failure report (negative outcome of

"forwardShortMessage" see clauses 10 and 11);

if no errors are indicated by the VLR:

- transferring the short message to the MS (see GSM 04.11).

When receiving a confirmation that the message is received by the MS (see GSM 04.11):

- relaying the delivery confirmation to the SMS-GMSC in a delivery report (positive outcome of

"forwardShortMessage", see clauses 10 and 11).

When receiving a failure report of the short message transfer to the MS (see GSM 04.11):

- returning the appropriate error information to the SMS-GMSC in a failure report (negative outcome of

"forwardShortMessage", see clause 10).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 31 (GSM 03.40 version 7.3.0 Release 1998)

When receiving a notification from the MS that it has memory available to receive one or more short messages (see

GSM 04.11):

- relaying the notification to the VLR ("mSMemoryCapacityAvailable", see clause 10);

if errors are indicated by the VLR:

- returning the appropriate error information to the MS in a failure report (negative outcome of "ReadyForSM", see

clauses 10 and 11).

When there is an ongoing MT-SMS transfer to the MS (see GSM 04.11), or other busy condition for MT-SMS, the

MSC has the option to store the TPDU in a queue for a short time (which must be shorter than the supervision timer

defined in GSM 09.02). The maximum time that a message may be queued is related to the permitted delay for the MSC

to respond to the SMS-GMSC. When the MS becomes available for MT-SMS transfer, the stored TPDUs are delivered

to the MS on a first-in first-out basis. If a message is not successfully transferred to the MS within the permitted time,

the MSC returns an appropriate error to the SMS-GMSC.

8.1.3 Functionality of the SGSN

When receiving a short message TPDU from the SMS-GMSC ("forwardShortMessage", see clause 10), the SGSN is

responsible for the following operations:

- reception of the short message TPDU;

if errors are detected by the SGSN:

- returning the appropriate error information to the SMS-GMSC in a failure report (negative outcome of

"forwardShortMessage" see clauses 10 and 11);

if no errors are detected by the SGSN:

- transferring the short message to the MS (see GSM 04.11).

When receiving a confirmation that the message is received by the MS (see GSM 04.11):

- relaying the delivery confirmation to the SMS-GMSC in a delivery report (positive outcome of

"forwardShortMessage", see clauses 10 and 11).

When receiving a failure report of the short message transfer to the MS (see GSM 04.11):

- returning the appropriate error information to the SMS-GMSC in a failure report (negative outcome of

"forwardShortMessage", see clause 10).

When receiving a notification from the MS that it has memory available to receive one or more short messages (see

GSM 04.11):

if errors are detected by the SGSN:

- returning the appropriate error information to the MS in a failure report (negative outcome of

"ReadyForSM", see clauses 10 and 11).

if no errors are detected by the SGSN:

- notifying the HLR of memory available in the MS via the SGSN with "ReadyForSM" (see clauses 10 and

11).

When the MS is becoming reachable again (see GSM 04.08):

- notifying the HLR of MS being reachable via the SGSN (and via the MSC if any) with "ReadyForSM" (see

clauses 10).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 32 (GSM 03.40 version 7.3.0 Release 1998)

When there is an ongoing MT-SMS transfer to the MS (see GSM 04.11), or other busy condition for MT-SMS, the

SGSN has the option to store the TPDU in a queue for a short time (which must be shorter than the supervision timer

defined in GSM 09.02). The maximum time that a message may be queued is related to the permitted delay for the

SGSN to respond to the SMS-GMSC. When the MS becomes available for MT-SMS transfer, the stored TPDUs are

delivered to the MS on a first-in first-out basis. If a message is not successfully transferred to the MS within the

permitted time, the SGSN returns an appropriate error to the SMS-GMSC.

8.2 Node functionality related to SM MO

8.2.1 Functionality of the MSC

When receiving a short message TPDU from the MS, the MSC is responsible for the following operations:

- reception of the short message TPDU (see GSM 04.11);

- retrieving information from the VLR ("sendInfoForMO-SMS", see clause 10); the MSISDN of the MS and, when

appropriate, error information. The retrieval of information from the VLR is followed by the VLR investigating

the MNRF (to be used in the alerting procedure, see clause 10)

if errors are indicated by the VLR:

- returning the appropriate error information to the MS in a failure report (negative outcome of

"sendInfoForMO-SMS" see clauses 10 and 11);

if no errors are indicated by the VLR:

- inspection of the RP-DA parameter;

if parameters are incorrect:

- returning the appropriate error information to the MS in a failure report (see GSM 04.11);

if no parameter errors are found:

NOTE: The SMS-IWMSC may be identical to the MSC.

- transferring the short message TPDU to the SMS-IWMSC ("forwardShortMessage", see clause 10).

When receiving the report of the short message from the SMS-IWMSC (positive or negative outcome of the

"forwardShortMessage", see clause 10), the MSC is responsible for the following operations:

- relaying the report to the MS (see GSM 04.11).

8.2.2 Functionality of the SMS-IWMSC

When receiving a short message TPDU from the MSC or SGSN ("forwardShortMessage", see clause 10), the

SMS-IWMSC is responsible for the following operations:

- reception of the short message TPDU;

- establishing, where necessary, a link with the addressed SC (see clause 5);

- transferring the short message TPDU to the SC (if the address is valid).

If a report associated with the short message is received from the SC, the SMS-IWMSC is responsible for the following

operations:

- relaying of the report to the MSC or SGSN (positive or negative outcome of "forwardShortMessage", see

clause 10).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 33 (GSM 03.40 version 7.3.0 Release 1998)

If a report associated with the short message is not received from the SC before a timer expires or if the SC address is

invalid, the SMS-IWMSC is responsible for the following operations:

- returning the appropriate error information to the MSC or SGSN in a failure report (negative outcome of

"forwardShortMessage", see clause 10).

The value of the timer is dependent on the protocol between the SC and the SMS-IWMSC.

8.2.3 Functionality of the SGSN

When receiving a short message TPDU from the MS, the SGSN is responsible for the following operations:

- reception of the short message TPDU (see GSM 04.11);

- inspection of the RP-DA parameter;

if parameters are incorrect:

- returning the appropriate error information to the MS in a failure report (see GSM 04.11);

if no parameter errors are found:

- transferring the short message TPDU to the SMS-IWMSC ("forwardShortMessage", see clause 10).

When receiving the report of the short message from the SMS-IWMSC (positive or negative outcome of the

"forwardShortMessage", see clause 10), the SGSN is responsible for the following operations:

- relaying the report to the MS (see GSM 04.11).

8.3 SMS-IWMSC functionality related to alerting

When receiving an alert from the HLR ("alertServiceCentre", see clause 10), the SMS-IWMSC is responsible for the

following operations:

- inspect the SC address;

- generate an RP-Alert-SC (see clause 9);

- transferring the RP-Alert-SC to the SC.

NOTE: If the SC address is not valid, then no further action will be taken.

9 Protocols and protocol architecture

The protocol layers of the SMS are structured as shown in figure 03.40/7.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 34 (GSM 03.40 version 7.3.0 Release 1998)

>

>

>

>

>

>

>

>

>

<

<

<

<

<

<

<

<

<

SME SC

SMS-GMSC /

SMS-IWMSC MSC/SGSN MS

SM-AL

SM-TL

SM-RL

SM-LL

Figure 03.40/7: Protocol layer overview for the Short Message Service point-to-point

The present document specifies the protocol at the SM-TL, the service offered by the SM-TL at the MS and the SC, and

the service offered by the SM-RL at the SC.

9.1 Protocol element features

9.1.1 Octet and Bit transmission order

The octets are transmitted according to their individual numbering; the octet with the lowest number being transmitted

first. The bits within each octet are transmitted according to their individual numbering also; the bits with the lowest

internal number being transmitted first.

9.1.2 Numeric and alphanumeric representation

For parameters within the TPDUs, there are four ways of numeric representation: Integer representation, octet,

semi-octet and alphanumeric representation.

9.1.2.1 Integer representation

Wherever the bits from a number of octets, complete or in fractions, are to represent an integer, the interpretation will be

according to the following:

1) Between octets: The octets with the lowest octet numbers will contain the most significant bits.

2) Within an octet: The bits with the highest bit numbers will be the most significant.

Below is given an example of octet and bit representation and transmission order of an integer represented field.

Let the 2 rightmost bits of octet no 5, the complete octet no 6 and 7, and the 3 leftmost bits of octet no 8 represent an

integer, as shown in figure 03.40/8.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 35 (GSM 03.40 version 7.3.0 Release 1998)

. . . . . . Oct.no.

7 6 5 4 3 2 1 0

. .

. . . . . . . .

5

6

7

8





b1 b0

b7 b6 b5 b4 b3 b2 b1 b0

5 5

6 6 6 6 6 6 6 6

7 7 7 7 7 7 7 7 b7 b6

b6

b5

b5

b4 b3 b2 b1 b0

8 b7 8 8

5

b1

5

b0

6

b7

6

b6 b1

6b0 7

b7

7b6 b1 7b0 8b7 8b6 8b5 .... 6 .... 7

*) >

*) >

_)

5b0 5b1 b2 5b3 5b4 5b5 5b6 5b7 b0 6b1 6b2 6b3 6b4 6b5 6b6 6b7 > 5 6

> 7b0 7

b1

7b2 7b3 7b4 7b5 7b6 7b7 b0 8b1 8b2 8b3 8b4 b5 8b6 8b7 8 8

*) : Bits not representing the integer.

Figure 03.40/8: 21 bits from the octets 5, 6, 7, and 8 in a short message ) will represent an integer as

shown in ), and will be transmitted in an order as shown in )

9.1.2.2 Octet representation

A field which is octet represented, will always consist of a number of complete octets. Each octet within the field

represents one decimal digit. The octets with the lowest octet numbers will contain the most significant decimal digits.

9.1.2.3 Semi-octet representation

A field which is semi-octet represented, will consist of a number of complete octets and - possibly - one half octet. Each

half octet within the field represents one decimal digit. The octets with the lowest octet numbers will contain the most

significant decimal digits. Within one octet, the half octet containing the bits with bit numbers 0 to 3, will represent the

most significant digit.

In the case where a semi-octet represented field comprises an odd number of digits, the bits with bit numbers 4 to 7

within the last octet are fill bits and shall always be set to "1111".

If a mobile receives an address field containing non-integer information in the semi-octets other than "1111" (e.g. 1110)

it shall display the semi-octet as the representation given in GSM 04.08 under "called BCD number", viz 1010="*",

1011="#", 1100="a", 1101="b", 1110="c". In the event of a discrepancy between the values quoted here and the values

specified in GSM 04.08 then GSM 04.08 shall take precedence. If a mobile receives "1111" in a position prior to the last

semi-octet then processing shall commence with the next semi-octet and the intervening semi-octet will be ignored.

Within each semi octet, the bits with the highest bit numbers will be the most significant.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 36 (GSM 03.40 version 7.3.0 Release 1998)

Below is given an example:

Octet no:

Digit 2 Digit 1

Digit 4 Digit 3

Digit 5

n+1

n+2

n+3 1 1 1 1

9.1.2.4 Alphanumeric representation

A field which uses alphanumeric representation will consist of a number of 7-bit characters represented as the default

alphabet defined in GSM 03.38.

9.1.2.5 Address fields

Address fields used by SM-RL are specified in GSM 04.11 and 09.02.

Each address field of the SM-TL consists of the following sub-fields: An Address-Length field of one octet, a

Type-of-Address field of one octet, and one Address-Value field of variable length; as shown below:

Address-Length

Type-of-Address

Address-Value Addr.

..

................................

1

2

3

4

5

µ

..

The Address-Length field is an integer representation of the number of useful semi-octets within the Address-Value

field, i.e. excludes any semi octet containing only fill bits.

The Type-of-Address field format is as follows:

Type-of-number Numbering-plan-identification 1

Type-of-number:

Bits 6 5 4

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 37 (GSM 03.40 version 7.3.0 Release 1998)

0 0 0 Unknown 1)

0 0 1 International number 2)

0 1 0 National number 3)

0 1 1 Network specific number 4)

1 0 0 Subscriber number 5)

1 0 1 Alphanumeric, (coded according to GSM TS 03.38 7-bit default alphabet)

1 1 0 Abbreviated number

1 1 1 Reserved for extension

The MS will interpret reserved values as "Unknown" but will store them exactly as received.

The SC may reject messages with a type of number containing a reserved value or one which is not supported.

1) "Unknown" is used when the user or network has no a priori information about the numbering plan. In this case,

the Address-Value field is organized according to the network dialling plan, e.g. prefix or escape digits might be

present.

2) The international format shall be accepted also when the message is destined to a recipient in the same country as

the MSC or as the SGSN.

3) Prefix or escape digits shall not be included.

4) "Network specific number" is used to indicate administration/service number specific to the serving network, e.g.

used to access an operator.

5) "Subscriber number" is used when a specific short number representation is stored in one or more SCs as part of a

higher layer application. (Note that "Subscriber number" shall only be used in connection with the proper PID

referring to this application).

Numbering-plan-identification (applies for Type-of-number = 000,001,010)

Bits 3 2 1 0

0 0 0 0 Unknown

0 0 0 1 ISDN/telephone numbering plan (E.164/E.163)

0 0 1 1 Data numbering plan (X.121)

0 1 0 0 Telex numbering plan

1 0 0 0 National numbering plan

1 0 0 1 Private numbering plan

1 0 1 0 ERMES numbering plan (ETSI DE/PS 3 01-3)

1 1 1 1 Reserved for extension

All other values are reserved.

For Type-of-number = 101 bits 3,2,1,0 are reserved and shall be transmitted as 0000. Note that for addressing any of the

entities SC, MSC, SGSN or MS, Numbering-plan-identification = 0001 will always be used. However, for addressing

the SME, any specified Numbering-plan-identification value may be used.

The MS will interpret reserved values as "Unknown" but will store them exactly as received.

The SC may reject messages with a type of number containing a reserved value or one which is not supported.

Within the Address-Value field, either a semi-octet or an alphanumeric1) representation applies.

The maximum length of the full address field (Address-Length, Type-of-Address and Address-Value) is 12 octets.

1) Applies only to addressing at the SM-TL.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 38 (GSM 03.40 version 7.3.0 Release 1998)

9.2 Service provided by the SM-TL

9.2.1 General

The Short Message Transfer Layer (SM-TL) provides a service to the Short Message Application Layer (SM-AL). This

service enables the SM-AL to transfer short messages to its peer entity, receive short messages from its peer entity and

receive reports about earlier requests for short messages to be transferred.

In order to keep track of messages and reports about those messages, primitives between the SM-AL and SM-TL contain

a Short Message Identifier (SMI), which is a reference number for the message associated with the primitive. This Short

Message Identifier is mapped to and from the Short Message Identifier used between the SM-TL and the Short Message

Relay Layer (SM-RL). The Short Message Identifier is not carried between entities and therefore a given message may

have different SMIs at the MS and SC sides (see subclause 9.3.1 below).

The SM-TL communicates with its peer entity by the protocol described in the following subclauses.

9.2.2 PDU Type repertoire at SM-TL

The SM-TL comprises the following six PDUs:

SMS-DELIVER, conveying a short message from the SC to the MS;

SMS-DELIVER-REPORT, conveying

a) a failure cause (if necessary);

b) information as part of a positive or negative acknowledgement to an SMS-DELIVER or SMS-STATUSREPORT

SMS-SUBMIT, conveying a short message from the MS to the SC;

SMS-SUBMIT-REPORT, conveying

a) a failure cause (if necessary);

b) information as part of a positive or negative acknowledgement to an SMS-SUBMIT or SMS-COMMAND

SMS-STATUS-REPORT, conveying a status report from the SC to the MS;

SMS-COMMAND, conveying a command from the MS to the SC.

9.2.2.1 SMS-DELIVER type

Basic elements of the SMS-DELIVER type:

Abbr. Reference P1) R2) Description

TP-MTI TP-Message-Type-Indicator M 2b Parameter describing the message

type.

TP-MMS TP-More-Messages-to-Send M b Parameter indicating whether or not

there are more messages to send

TP-RP TP-Reply-Path M b Parameter indicating that Reply Path

exists.

TP-UDHI TP-User-Data-Header-Indicator O b Parameter indicating that the TP-UD

field contains a Header

TP-SRI TP-Status-Report-Indication O b Parameter indicating if the SME has

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 39 (GSM 03.40 version 7.3.0 Release 1998)

Abbr. Reference P1) R2) Description

requested a status report.

TP-OA TP-Originating-Address M 2-12o Address of the originating SME.

TP-PID TP-Protocol-Identifier M o Parameter identifying the above layer

protocol, if any

TP-DCS TP-Data-Coding-Scheme M o Parameter identifying the coding

scheme within the TP-User-Data.

TP-SCTS TP-Service-Centre-Time-Stamp M 7o Parameter identifying time when the

SC received the message.

TP-UDL TP-User-Data-Length M I Parameter indicating the length of the

TP-User-Data field to follow.

TP-UD TP-User-Data O 3)

1) Provision;Mandatory (M) or Optional (O).

2) Representation; Integer (I), bit (b), 2 bits (2b), Octet (o), 7 octets (7o), 2-12 octets (2-12o)

3) Dependent on the TP-DCS

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 40 (GSM 03.40 version 7.3.0 Release 1998)

Layout of SMS-DELIVER:

Bitno. 7 6 5 4 3 2 1 0

1 TP-MTI, TP-MMS, TP-SRI, TP-UDHI, TPRP

Number of octets 1

2

2 to 12 TP-OA

1 TP-PID

1 TP-DCS

TP-SCTS

1 TP-UDL

1

TP-UD

NOTE: Any unused bits will be set to zero by the sending entity and will be ignored by the receiving entity.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 41 (GSM 03.40 version 7.3.0 Release 1998)

9.2.2.1a SMS-DELIVER-REPORT type

An SMS-DELIVER-REPORT TPDU is carried as a RP-User-Data element within an RP-ERROR PDU and is part of

the negative acknowledgement to an SMS-DELIVER or SMS-STATUS-REPORT.

An SMS-DELIVER-REPORT TPDU is also carried as a RP-User-Data element within an RP-ACK PDU and is part of

a positive acknowledgement to a SMS-DELIVER or SMS-STATUS REPORT

(i) SMS-DELIVER-REPORT for RP-ERROR

Basic elements of the SMS-DELIVER-REPORT type:

Abbr. Reference P1) P2) Description

TP-MTI TP-Message-Type-Indicator M 2b Parameter describing the message type

TP-UDHI TP-User-Data-Header-Indication O b Parameter indicating that the TP-UD field

contains a Header

TP-FCS TP-Failure-Cause M I Parameter indicating the reason for

SMS-DELIVER failure

TP-PI TP-Parameter-Indicator M o Parameter indicating the presence of any of

the optional parameters which follow

TP-PID TP-Protocol-Identifier O o see subclause 9.2.3.9

TP-DCS TP-Data-Coding-Scheme O o see subclause 9.2.3.10

TP-UDL TP-User-Data-Length O o see subclause 9.2.3.16

TP-UD TP-User-Data O 3) 4) see subclause 9.2.3.24

1) Provision:Mandatory (M) or Optional (O)

2) Representation: Integer (I), bit (b), 2bits (2b), octet (o)

3) Dependent upon the TP-DCS

4) The TP-User-Data field in the SMS-DELIVER-REPORT is only available for use by the MT.

Layout of SMS-DELIVER-REPORT:

Bit Number

Number of

Octets

7 6 5 4 3 2 1 0

1 TP-MTI,TPUDHI

1 TP-FCS

1 TP-PI

0,1 TP-PID

0,1 TP-DCS

0,1 TP-UDL

0 to 158 TP-UD

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 42 (GSM 03.40 version 7.3.0 Release 1998)

Bits 7 and 5 - 2 in octet 1 are presently unused and the sender shall set them to zero. If any of these bits is non-zero, the

receiver shall not examine the other field and shall treat the TP-Failure-Cause as "Unspecified error cause".

(ii) SMS-DELIVER-REPORT for RP-ACK

Basic elements of the SMS-DELIVER-REPORT type:

Abbr Reference P1) P2) Description

TP-MTI TP-Message Type Indicator M 2b Parameter describing the message type

TP-UDHI TP-User-Data-Header-Indication O b Parameter indicating that the TP-UD field

contains a Header

TP-PI TP-Parameter-Indicator M o Parameter indicating the presence of any of the

optional parameters which follow

TP-PID TP-Protocol-Identifier O o see subclause 9.2.3.9

TP-DCS TP-Data-Coding-Scheme O o see subclause 9.2.3.10

TP-UDL TP-User-Data-Length O o see subclause 9.2.3.16

TP-UD TP-User-Data O 3) 4) see subclause 9.2.3.24

1) Provision: Mandatory (M) or Optional (O)

2) Representation: Integer (I), Bit (b), 2 bits (2b), octet (o)

3) Dependent upon the TP-DCS

4) The TP-User-Data field in the SMS-DELIVER-REPORT is only available for use by the MT.

Layout of SMS-DELIVER-REPORT:

Bit Number

Number of

Octets

7 6 5 4 3 2 1 0

1 TP-MTI,TPUDHI

1 TP-PI

0,1 TP-PID

0,1 TP-DCS

0,1 TP-UDL

0 to 159 TP-UD

Bits 7 - 2 in the TP-MTI are presently unused in the SMS-DELIVER-REPORT and the sender shall set them to zero,. If

any of these bits is non-zero, the receiver shall ignore them.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 43 (GSM 03.40 version 7.3.0 Release 1998)

9.2.2.2 SMS-SUBMIT type

Basic elements of the SMS-SUBMIT type:

Abbr. Reference P1) P2) Description

TP-MTI TP-Message-Type-Indicator M 2b Parameter describing the message type.

TP-RD TP-Reject-Duplicates M b Parameter indicating whether or not the SC

shall accept an SMS-SUBMIT for an SM still

held in the SC which has the sam TP-MR and

the same TP-DA as a previously submitted SM

fromthe same OA

TP-VPF TP-Validity-Period-Format M 2b Parameter indicating whether or not the TP-VP

field is present.

TP-RP TP-Reply-Path M b Parameter indicating the request for Reply

Path.

TP-UDHI TP-User-Data-Header-Indicator O b Parameter indicating that the TP-UD field

contains a Header.

TP-SRR TP-Status-Report-Request O b Parameter indicating if the MS is requesting a

status report.

TP-MR TP-Message-Reference M I Parameter identifying the SMS-SUBMIT.

TP-DA TP-Destination-Address M 2-12o Address of the destination SME.

TP-PID TP-Protocol-Identifier M o Parameter identifying the above layer protocol,

if any

TP-DCS TP-Data-Coding-Scheme M o Parameter identifying the coding scheme

within the TP-User-Data.

TP-VP TP-Validity-Period O o/7o Parameter identifying the time from where the

message is no longer valid.

TP-UDL TP-User-Data-Length M I Parameter indicating the length of the

TP-User-Data field to follow.

TP-UD TP-User-Data O 3)

1) Provision;Mandatory (M) or Optional (O).

2) Representation; Integer (I), bit (b), 2 bits (2b), Octet (o), 7 octets (7o), 2-12 octets (2-12o).

3) Dependent on the TP-DCS

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 44 (GSM 03.40 version 7.3.0 Release 1998)

Layout of SMS-SUBMIT:

Bitno 7 6 5 4 3 2 1 0

1 TP-MTI, TP-RD, TP-VPF TP-SRR, TP-UDHI, TP-RP

1 TP-MR

Number of 1

octets 2

2 to 12 TP-DA

1 TP-PID

1 TP-DCS

1

0, 1 or 7 TP-VP

1 TP-UDL

1

0 to 140 TP-UD

NOTE: Any unused bits will be set to zero by the sending entity and will be ignored by the receiving entity.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 45 (GSM 03.40 version 7.3.0 Release 1998)

9.2.2.2a SMS-SUBMIT-REPORT type

An SMS-SUBMIT-REPORT TPDU is carried as a RP-User-Data element within an RP-ERROR PDU and is part of the

negative acknowledgement to an SMS-SUBMIT or SMS-COMMAND.

An SMS-SUBMIT-REPORT TPDU is also carried as a RP-User-Data element with an RP-ACK PDU and is part of a

positive acknowledgement to a SMS-SUBMIT or SMS-COMMAND.

(I) SMS-SUBMIT-REPORT for RP-ERROR

Basic elements of the SMS-SUBMIT-REPORT type:

Abbr. Reference P1) P2) Description

TP-MTI TP-Message-Type-Indicator M 2b Parameter describing the message type

TP-UDHI TP-User-Data-Header-Indication O b Parameter indicating that the TP-UD field

contains a Header

TP-FCS TP-Failure-Cause M I Parameter indicating the reason for

SMS-SUBMIT failure

TP-PI TP-Parameter-Indicator M o Parameter indicating the presence of any of the

optional parameters which follow

TP-SCTS TP-Service-Centre-Time-Stamp M 7o

5)

Parameter identifying the time when the SC

received the SMS-SIBMIT

See subclause 9.2.3.11

TP-PID TP-Protocol-Identifier O o See subclause 9.2.3.9

TP-DCS TP-Data-Coding-Scheme O o see subclause 9.2.3.10

TP-UDL TP-User-Data-Length O o see subclause 9.2.3.16

TP-UD TP-User-Data O 3) 4) see subclause 9.2.3.24

1) Provision:Mandatory (M) or Optional (O)

2) Representation: Integer (I), bit (b), 2bits (2b), octet (o)

3) Dependent upon the TP-DCS;

4) The TP-User-Data field in the SMS-SUBMIT-REPORT is only available for use by the SC.;

5) This same time value will also be carried in the SMS-STATUS-REPORT relating to a particular SM. See

subclause 9.2.2.3. This will allow the submitting SME to associate a particular SMS-SUBMIT with a subsequent

SMS-STATUS-REPORT by correlating the TP-SCTS values.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 46 (GSM 03.40 version 7.3.0 Release 1998)

Layout of SMS-SUBMIT-REPORT:

Bit Number

Number of

Octets

7 6 5 4 3 2 1 0

1 TP-MTI,TPUDHI

1 TP-FCS

1 TP-PI

7 TP-SCTS

0,1 TP-PID

0,1 TP-DCS

0,1 TP-UDL

0 to 151 TP-UD

Bits 7 and 5 - 2 in octet 1 are presently unused and the sender shall set them to zero. If any of these bits is non-zero, the

receiver shall not examine the other field and shall treat the TP-Failure-Cause as "Unspecified error cause".

(ii) SMS-SUBMIT-REPORT for RP-ACK

Basic elements of the SMS-SUBMIT_REPORT type:

Abbr Reference P1) P2) Description

TP-MTI TP-Message Type-Indicator M 2b Parameter describing the message type

TP-UDHI TP-User-Data-Header-Indication O b Parameter indicating that the TP-UD field contains

a Header

TP-PI TP-Parameter-Indicator M o Parameter indicating the presence of any of the

optional parameters which follow

TP-SCTS TP-Service-Centre-Time-Stamp M 7o

5)

Parameter identifying the time when the SC

received the SMS-SIBMIT

See subclause 9.2.3.11

TP-PID TP-Protocol-Identifier O o See subclause 9.2.3.9

TP-DCS TP-Data-Coding-Scheme O o see subclause 9.2.3.10

TP-UDL TP-User-Data-Length O o see subclause 9.2.3.16

TP-UD TP-User-Data O 3) 4) see subclause 9.2.3.24

1) Provision: Mandatory (M) or Optional (O);

2) Representation: Integer (I), Bit (B), 2bits (2b), octet (o);

3) Dependent upon the TP-DCS;

4) The TP-User-Data field in the SMS-SUBMIT-REPORT is only available for use by the SC.;

5) This same time value will also be carried in the SMS-STATUS-REPORT relating to a particular SM. See

subclause 9.2.2.3. This will allow the submitting SME to associate a particular SMS-SUBMIT with a subsequent

SMS-STATUS-REPORT by correlating the TP-SCTS values.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 47 (GSM 03.40 version 7.3.0 Release 1998)

Layout of SMS-SUBMIT REPORT

Bit Number

Number

of Octets

7 6 5 4 3 2 1 0

1 TP-MTI,TPUDHI

1 TP-PI

7 TP-SCTS

0,1 TP-PID

0,1 TP-DCS

0,1 TP-UDL

0 to 152 TP-UD

Bits 7 - 2 in the TP-MTI are presently unused in the SMS-SUBMIT-REPORT and the sender shall set them to zero. If

any of these bits is non-zero, the receiver shall ignore them.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 48 (GSM 03.40 version 7.3.0 Release 1998)

9.2.2.3 SMS-STATUS-REPORT type

Basic elements of the SMS-STATUS-REPORT type:

Abbr. Reference P1) R2) Description

TP-MTI TP-Message-Type-Indicator M 2b Parameter describing the message type

TP-UDHI TP-User-Data-Header-Indication O b Parameter indicating that the TP-UD field

contains a Header

TP-MMS TP-More-Messages-to-Send M b Parameter indicating whether or not there are

more messages to send

TP-SRQ TP-Status-Report-Qualifier M b Parameter indicating whether the previously

submitted TPDU was an SMS_SUBMIT or

an SMS-COMMAND

TP-MR TP-Message-Reference 3) M I Parameter identifying the previously

submitted SMS-SUBMIT or

SMS-COMMAND

TP-RA TP-Recipient-Address M 2-12o Address of the recipient of the previously

submitted mobile originated short message

TP-SCTS TP-Service-Centre-Time-Stamp M 7o Parameter identifying time when the SC

received the previously sent SMS-SUBMIT

TP-DT TP-Discharge-Time M 7o Parameter identifying the time associated with

a particular TP-ST outcome

TP-ST TP-Status M o Parameter identifying the status of the

previously sent mobile originated short

message

TP-PI TP-Parameter-Indicator O

4)

o Parameter indicating the presence of any of

the optional parameters which follow

TP-PID TP-Protocol-Identifier O o see subclause 9.2.3.9. TP-PID of original

SMS-SUBMIT

TP-DCS TP-Data-Coding-Scheme O o see subclause 9.2.3.10

TP-UDL TP-User-Data-Length O o see subclause 9.2.3.16

TP-UD TP-User-Data O 5) see subclause 9.2.3.24

1) Provision: Mandatory (M) or Optional (O).

2) Representation: Integer (I), bit (b), 2 bits (2b), Octet (o), 7 octets (7o), 2-12 octets (2-12o)

3) Where the SMS-STATUS-REPORT is the result of an SMS-COMMAND and the TP-Command-Type was an

Enquiry, the TP-MR returned in the SMS-STATUS-REPORT shall be the TP-MN which was sent in the

SMS-COMMAND (i.e. the TP-MR of the previously submitted SM to which the Enquiry refers).

4) Mandatory if any of the optional parameters following TP-PI is present, otherwise optional.

5) TP-UD contains information related to a SMS-DELIVER; can contain information transported in the TP-UD of

SMS-DELIVER-REPORT, and information inserted by the SMSC. The length of the TP-UD field is limited and

might not be long enough to fit information both from the original receiving terminal (as included into the SMSDELIVER-

REPORT) and information added by the SMSC. In these cases the former information has higher

priority, and the latter will be truncated.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 49 (GSM 03.40 version 7.3.0 Release 1998)

Layout of SMS-STATUS-REPORT:

Bitno. 7 6 5 4 3 2 1 0

Number of octets 1 TP-MTI, TP-MMS, TP-SRQ, TP-UDHI

1 TP-MR

1

2 —TP-RA

2 to 12

7 TP-SCTS

7 —TP-DT

1 TP-ST

1 TP-PI

1 TP-PID

1 TP-DCS

1 . . . . . . TP-UDL

1

0to143 . . . . . . . . TP-UD

NOTE: Any unused bits will be set to zero by the sending entity and will be ignored by the receiving entity.

The maximum guaranteed length of TP-UD is 131 octets. In order to achieve the maximum stated above

(143 octets), the TP-RA field must have a length of 2 octets and TP-PID and TP-DCS must not be

present.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 50 (GSM 03.40 version 7.3.0 Release 1998)

9.2.2.4 SMS-COMMAND type

Basic elements of the SMS-COMMAND type:

Abbr. Reference P1) R2) Description

TP-MTI TP-Message-Type-Indicator M 2b Parameter describing the type

TP-UDHI TP-User-Data-Header-Indication O b Parameter indicating that the TP-CD field

contains a Header

TP-SRR TP-Status-Report-Request O b Parameter indicating if the SMS Command is

requesting a status report.

TP-MR TP-Message Reference M I Parameter identifying the SMS-COMMAND

TP-PID TP-Protocol- Identifier M o Parameter identifying the above layer

protocol, if any

TP-CT TP-Command-Type M o Parameter specifying which operation is to be

performed on a SM

TP-MN TP-Message-Number M3) o Parameter indicating which SM in the SC to

operate on

TP-DA TP-Destination-Address M4) 2-12o Parameter indicating the Destination Address

to which the TP-Command refers

TP-CDL TP-Command-Data-Length M o Parameter indicating the length of the TP-CD

field in octets

TP-CD TP-Command-Data O o Parameter containing user data

1) Provision:Mandatory (M) or Optional (O).

2) Representation: Integer (I), bit (b), 2bits (2b), octet (o)

3) For TP-Command-Types which are not for a specific SM this field shall be ignored when received. Its value is of

no concern but the field must be present to maintain the structure.

4) For certain TP-Command-Types which operate on a specific SM (e.g. Enquire, Delete etc.) the full TP-DA must

be specified. For TP-Command-Types which do not operate on a specific SM, the address length must be set to

zero indicating that the Address-Value fields are not present. The Type-of-Address field must be present (see

9.1.2.5) and shall be set to zero and ignored.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 51 (GSM 03.40 version 7.3.0 Release 1998)

Layout of SMS-COMMAND:

Bitno. 7 6 5 4 3 2 1 0

Number 1 TP-MTI, TP-SRR,

TP-UDHI

of octets 1 TP-MR

1 TP-PID

1 TP-CT

1 TP-MN

2 to 12 TP-DA

………….…………………….

1 TP-CDL

………….…………………….

0 to 156 TP-CD

NOTE: The maximum guaranteed length of TP-CD is 146 octets. In order to achieve the maximum stated above

(156 octets), the TP-DA field must have a length of 2 octets.

9.2.3 Definition of the TPDU parameters

9.2.3.1 TP-Message-Type-Indicator (TP-MTI)

The TP-Message-Type-Indicator is a 2-bit field, located within bits no 0 and 1 of the first octet of all PDUs which can

be given the following values:

bit1 bit0 Message type

0 0 SMS-DELIVER (in the direction SC to MS)

0 0 SMS-DELIVER REPORT (in the direction MS to SC)

1 0 SMS-STATUS-REPORT (in the direction SC to MS)

1 0 SMS-COMMAND (in the direction MS to SC)

0 1 SMS-SUBMIT (in the direction MS to SC)

0 1 SMS-SUBMIT-REPORT (in the direction SC to MS)

1 1 Reserved

If an MS receives a TPDU with a "Reserved" value in the TP-MTI it shall process the message as if it were an

"SMS-DELIVER" but store the message exactly as received.

9.2.3.2 TP-More-Messages-to-Send (TP-MMS)

The TP-More-Messages-to-Send is a 1-bit field, located within bit no 2 of the first octet of SMS-DELIVER and

SMS-STATUS-REPORT, and to be given the following values:

Bit no 2: 0 More messages are waiting for the MS in this SC

1 No more messages are waiting for the MS in this SC

NOTE: In the case of SMS-STATUS-REPORT this parameter refers to messages waiting for the mobile to which

the status report is sent. The term message in this context refers to SMS-messages or status reports.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 52 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.3 TP-Validity-Period-Format (TP-VPF)

The TP-Validity-Period-Format is a 2-bit field, located within bit no 3 and 4 of the first octet of SMS-SUBMIT, and to

be given the following values:

bit4 bit3

0 0 TP-VP field not present

1 0 TP-VP field present - relative format

0 1 TP-VP field present - enhanced format

1 1 TP-VP field present - absolute format

Any unsupported value may be rejected by the SC by returning the 'TP-VPF not supported' TP-FCS value in the SMS

Submit Report for RP-Error.

9.2.3.4 TP-Status-Report-Indication (TP-SRI)

The TP-Status-Report-Indication is a 1-bit field, located within bit no. 5 of the first octet of SMS-DELIVER, and to be

given the following values:

Bit no. 5: 0 A status report will not be returned to the SME

1 A status report will be returned to the SME

9.2.3.5 TP-Status-Report-Request (TP-SRR)

The TP-Status-Report-Request is a 1-bit field, located within bit no. 5 of the first octet of SMS-SUBMIT and

SMS-COMMAND, and to be given the following values:

Bit no. 5: 0 A status report is not requested

1 A status report is requested

9.2.3.6 TP-Message-Reference (TP-MR)

The TP-Message-Reference field gives an integer representation of a reference number of the SMS-SUBMIT or

SMS-COMMAND submitted to the SC by the MS. The MS increments TP-Message-Reference by 1 for each

SMS-SUBMIT or SMS-COMMAND being submitted. The value to be used for each SMS-SUBMIT is obtained by

reading the Last-Used-TP-MR value from the SMS Status data field in the SIM (see GSM 11.11) and incrementing this

value by 1. After each SMS-SUBMIT has been submitted to the network, the Last-Used-TP-MR value in the SIM is

updated with the TP-MR that was used in the SMS-SUBMIT operation. The reference number may possess values in the

range 0 to 255. The value in the TP-MR assigned by the MS is the same value which is received at the SC.

In the case where no acknowledgement or an appropriate RP-Error is received in response to an SMS-SUBMIT or

SMS-COMMAND, then the MS may automatically repeat the SMS-SUBMIT or SMS-COMMAND but must use the

same TP-MR value. The number of times the MS may repeat the SMS-SUBMIT or SMS-COMMAND is an

implementation matter.

If all automatic attempts fail (including the case where no automatic repeat is provided), the user shall be informed. The

failed message shall be stored in the mobile in such a way that the user can request a retransmission using the same

TP-MR value, without needing to re-enter any information. Such storage need only be provided for a single failed

message, the one most recently attempted.

The SC may discard an SMS-SUBMIT or SMS-COMMAND which has the same TP-MR value as the previous

SMS-SUBMIT or SMS-COMMAND received from the same originating address.

A Phase 2 or later ME using a Phase 1 SIM cannot read or update the TP-Message-Reference from/to the SIM, and so

the ME shall always retain the Last-Used-TP-MR value in its own memory, to be used only in the case of a Phase 1

SIM.

The SMS-STATUS-REPORT also contains a TP-Message-Reference field. The value sent to the MS will be the same as

the TP-Message-Reference value generated by the MS in the earlier SMS-SUBMIT or SMS-COMMAND to which the

status report relates.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 53 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.7 TP-Originating-Address (TP-OA)

The TP-Originating-Address field is formatted according to the formatting rules of address fields.

9.2.3.8 TP-Destination-Address (TP-DA)

The TP-Destination-Address field is formatted according to the formatting rules of address fields.

9.2.3.9 TP-Protocol-Identifier (TP-PID)

The TP-Protocol-Identifier parameter serves the purposes indicated in subclause 3.2.3. It consists of one octet, and the

bits in the octet are used as follows:

The MS will interpret reserved or unsupported values as the value 00000000 but shall store them exactly as received.

The SC may reject messages with a TP-Protocol-Identifier containing a reserved value or one which is not supported.

bits usage

7 6

0 0 Assigns bits 0..5 as defined below

0 1 Assigns bits 0..5 as defined below

1 0 reserved

1 1 Assigns bits 0-5 for SC specific use

In the case where bit 7 = 0 and bit 6 = 0,

bit 5 indicates telematic interworking:

value = 0 : no interworking, but SME-to-SME protocol

value = 1 : telematic interworking

In the case of telematic interworking, the following five bit patterns in bits 4..0 are used to indicate different types of

telematic devices:

4.. .0

00000 implicit - device type is specific to this SC, or can be concluded on the basis of the address

00001 telex (or teletex reduced to telex format)

00010 group 3 telefax

00011 group 4 telefax

00100 voice telephone (i.e. conversion to speech)

00101 ERMES (European Radio Messaging System)

00110 National Paging system (known to the SC)

00111 Videotex (T.100/T.101)

01000 teletex, carrier unspecified

01001 teletex, in PSPDN

01010 teletex, in CSPDN

01011 teletex, in analog PSTN

01100 teletex, in digital ISDN

01101 UCI (Universal Computer Interface, ETSI DE/PS 3 01-3)

01110..01111 (reserved, 2 combinations)

10000 a message handling facility (known to the SC)

10001 any public X.400-based message handling system

10010 Internet Electronic Mail

10011..10111 (reserved, 5 combinations)

11000..11110 values specific to each SC, usage based on mutual agreement between the SME and the SC (7

combinations available for each SC)

11111 A GSM mobile station. The SC converts the SM from the received TP-Data-Coding-Scheme to

any data coding scheme supported by that MS (e.g. the default).

If bit 5 has value 1 in an SMS-SUBMIT PDU, it indicates that the SME is a telematic device of a type which is indicated

in bits 4..0, and requests the SC to convert the SM into a form suited for that device type. If the destination network is

ISDN, the SC must also select the proper service indicators for connecting to a device of that type.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 54 (GSM 03.40 version 7.3.0 Release 1998)

If bit 5 has value 1 in an SMS-DELIVER PDU, it indicates that the SME is a telematic device of a type which is

indicated in bits 4..0.

If bit 5 has value 0 in an SMS-DELIVER PDU, the value in bits 4..0 identifies the SM-AL protocol being used between

the SME and the MS.

Note that for the straightforward case of simple MS-to-SC short message transfer the Protocol Identifier is set to the

value 0.

In the case where bit 7 = 0, bit 6 = 1, bits 5..0 are used as defined below

5 .. . .0

000000 Short Message Type 0

000001 Replace Short Message Type 1

000010 Replace Short Message Type 2

000011 Replace Short Message Type 3

000100 Replace Short Message Type 4

000101 Replace Short Message Type 5

000110 Replace Short Message Type 6

000111 Replace Short Message Type 7

001000..011110 Reserved

011111 Return Call Message

100000..111100 Reserved

111101 ME Data download

111110 ME De-personalization Short Message

111111 SIM Data download

A short message type 0 indicates that the ME must acknowledge receipt of the short message but may discard its

contents.

The Replace Short Message feature is optional for the ME and the SIM but if implemented it shall be performed as

described here.

For MT short messages, on receipt of a short message from the SC, the MS shall check to see if the associated Protocol

Identifier contains a Replace Short Message Type code.

If such a code is present, then the MS will check the originating address and replace any existing stored message having

the same Protocol Identifier code and originating address with the new short message and other parameter values. If

there is no message to be replaced, the MS shall store the message in the normal way. The MS may also check the SC

address as well as the Originating Address. However, in a network which has multiple SCs, it is possible for a Replace

Message type for a SM to be sent via different SCs and so it is recommended that the SC address should not be checked

by the MS unless the application specifically requires such a check.

If a Replace Short Message Type code is not present then the MS will store the message in the normal way.

In MO short messages the SC reacts similarly but only the address of the originating MS or any other source is checked.

A Return Call Message indicates to the MS to inform the user that a call (e.g. a telephone call) can be established to the

address specified within the TP-OA. The RP-OA contains the address of the SC as usual. The message content (if

present) gives displayable information (e.g. the number of waiting voice messages). The message is handled in the same

way as all other messages of the Replace Short Message Types.

The ME De-personalization Short Message is a ME-specific message which instructs the ME to de-personalities the ME

(see GSM 02.22 [25]). The TP-DCS shall be set to Uncompressed, Default Alphabet, and Message Class 1

(ME-specific), which corresponds to a bit coding of 00010001. The TP-UD field contains de-personalization

information coded according to GSM 02.22 [25]. This information shall not be displayed by an ME which supports the

scheme. The acknowledgement to this message is a SMS-DELIVER-REPORT for RP-ACK in which the TP-User-Data

shall be coded according to GSM 02.22.

SIM Data download is a facility whereby the ME must pass the short message in its entirety including all SMS elements

contained in the SMS deliver to the SIM using the mechanism described in GSM 11.11. The DCS shall be set to 8 bit

message class 2 (either bit coding 1111 0110 or 00010110). The entire user data field is available for SIM Data

download.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 55 (GSM 03.40 version 7.3.0 Release 1998)

ME Data download is a facility whereby the ME shall process the short message in its entirety including all SMS

elements contained in the SMS deliver to the ME. The DCS shall be set to message class 1. The entire user data field is

available for ME data download.

9.2.3.10 TP-Data-Coding-Scheme (TP-DCS)

The TP-Data-Coding-Scheme is defined in GSM 03.38.

9.2.3.11 TP-Service-Centre-Time-Stamp (TP-SCTS)

The TP-Service-Centre-Time-Stamp field is given in semi-octet representation, and represents the local time in the

following way:

Year: Month: Day: Hour: Minute: Second: Time Zone

Digits:

(Semi-octets)

2 2 2 2 2 2 2

The Time Zone indicates the difference, expressed in quarters of an hour, between the local time and GMT. In the first

of the two semi-octets, the first bit (bit 3 of the seventh octet of the TP-Service-Centre-Time-Stamp field) represents the

algebraic sign of this difference (0 : positive, 1 : negative).

The Service-Centre-Time-Stamp, and any other times coded in this format that are defined in the present document,

represent the time local to the sending entity.

If the MS has knowledge of the local time zone, then any time received (e.g. Service-Centre-Time-Stamp) at the MS

may be displayed in the local time rather than the time local to the sending entity. Messages shall be stored as received

without change to any time contained therein.

The Time Zone code enables the receiver to calculate the equivalent time in GMT from the other semi-octets in the

Service-Centre-Time-Stamp, or indicate the time zone (GMT, GMT+1H etc.), or perform other similar calculations as

required by the implementation.

If the MS receives a non-integer value in the SCTS, it shall assume that the digit is set to 0 but shall store the entire field

exactly as received.

9.2.3.12 TP-Validity-Period (TP-VP)

9.2.3.12.1 TP-VP (Relative format)

The TP-Validity-Period comprises 1 octet in integer representation, giving the length of the validity period, counted

from when the SMS-SUBMIT is received by the SC.

The representation of time is as follows:

TP-VP value Validity period value

0 to 143 (TP-VP + 1) x 5 minutes (i.e. 5 minutes intervals up to 12 hours)

144 to 167 12 hours + ((TP-VP -143) x 30 minutes)

168 to 196 (TP-VP - 166) x 1 day

197 to 255 (TP-VP - 192) x 1 week

9.2.3.12.2 TP-VP (Absolute format )

The TP-Validity Period comprises 7 octets in semi octet representation giving the absolute time of the validity period

termination

The representation of time is identical to the representation of the TP-Service-Centre-Time-Stamp.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 56 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.12.3 TP-VP ( Enhanced format )

The TP-Validity Period comprises 7 octets. The presence of all octets is mandatory although they may not all be used.

The first octet indicates the way in which the following 6 octets are used. Any reserved/unused bits or octets must be set

to zero.

Octet 1 TP-VP functionality indicator

bit 7 Extension bit

Set to 1 if the TP-VP functionality indicator is to be extended to another octet. A setting of 0 indicates that there

are no more TP-VP functionality indicator extension octets to follow.

Any such extension octet will immediately follow the previous TP-VP functionality indicator.

bit 6 Single shot SM.

Set to 1 if the SC is required to make up to one delivery attempt. The TP-Validity Period, where present, will be

applicable to the Single shot SM.

bits 5, 4, 3 Reserved

bits 2, 1, 0 Validity Period Format.

Value bits 2 1 0

0 0 0 No Validity Period specified

0 0 1 Validity Period is as specified for the relative case. The following octet contains the

TP-VP value as described in 9.2.3.12.1

0 1 0 Validity period is relative in integer representation and the following octet contains

the TP-VP value in the range 0 to 255 representing 0 to 255 seconds. A TP-VP value

of zero is undefined and reserved for future use.

0 1 1 Validity period is relative in semi-octet representation. The following 3 octets contain

the relative time in Hours Minutes and Seconds giving the length of the validity

period counted from when the SMS SUBMIT is received by the SC. The

representation of time uses the same representation as the Hours, Minutes and

Seconds in the TP-Service-Centre-Time-Stamp.

1 0 0 Reserved

1 0 1 Reserved

1 1 0 Reserved

1 1 1 Reserved

The SC will reject any Unsupported/ Reserved values received by returning the 'TP-VP not supported' TP-FCS value in

the Submit SM Report for RP-Error

9.2.3.13 TP-Discharge-Time (TP-DT)

The TP-Discharge-Time field indicates the time at which a previously submitted SMS-SUBMIT was successfully

delivered to or attempted to deliver to the recipient SME or disposed of by the SC.

In the case of "transaction completed" the time shall be the time of the completion of the transaction. In the case of "SC

still trying to transfer SM" the time shall be the time of the last transfer attempt. In the case of "permanent or temporary

error - SC not making any more transfer attempts" the time shall be the time of either the last transfer attempt or the time

at which the SC disposed of the SM according to the Status outcome in TP-ST.

The TP-Discharge-Time is given in semi-octet representation in a format identical to the TP-SCTS.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 57 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.14 TP-Recipient-Address (TP-RA)

The TP-Recipient-Address field indicates the address of the SME that was the destination of the previously submitted

mobile originated short message being subject to the status report. The field is formatted according to the formatting

rules of address fields.

9.2.3.15 TP-Status (TP-ST)

The TP-Status field indicates the status of a previously submitted SMS-SUBMIT and certain SMS COMMANDS for

which a Status -Report has been requested. It consists of one octet and the bits in the octet are used as follows:

The MS will interpret any reserved values as "Service Rejected" (01100011) but shall store them exactly as received.

bits value/usage

7 0 Bits 0..6 as defined below:

6....0 Indicate whether the previously submitted short message was successfully forwarded to the

SME, or whether an error condition has been encountered, as follows:

Short message transaction completed

0000000 Short message received by the SME

0000001 Short message forwarded by the SC to the SME but the SC is

unable to confirm delivery

0000010 Short message replaced by the SC

Reserved values

0000011..0001111 Reserved

0010000..0011111 Values specific to each SC

Temporary error, SC still trying to transfer SM

0100000 Congestion

0100001 SME busy

0100010 No response from SME

0100011 Service rejected

0100100 Quality of service not available

0100101 Error in SME

0100110..0101111 Reserved

0110000..0111111 Values specific to each SC

Permanent error, SC is not making any more transfer attempts

1000000 Remote procedure error

1000001 Incompatible destination

1000010 Connection rejected by SME

1000011 Not obtainable

1000100 Quality of service not available

1000101 No interworking available

1000110 SM Validity Period Expired

1000111 SM Deleted by originating SME

1001000 SM Deleted by SC Administration

1001001 SM does not exist (The SM may have previously existed in the SC but the SC

no longer has knowledge of it or the SM

may never have previously existed in the SC)

1001010..1001111 Reserved

1010000..1011111 Values specific to each SC

Temporary error, SC is not making any more transfer attempts

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 58 (GSM 03.40 version 7.3.0 Release 1998)

1100000 Congestion

1100001 SME busy

1100010 No response from SME

1100011 Service rejected

1100100 Quality of service not available

1100101 Error in SME

1100110..1101001 Reserved

1101010..1101111 Reserved

1110000..1111111 Values specific to each SC

bits value/usage

7 1 Bits 0..6 reserved

9.2.3.16 TP-User-Data-Length (TP-UDL)

If the TP-User-Data is coded using the GSM 7 bit default alphabet, the TP-User-Data-Length field gives an integer

representation of the number of septets within the TP-User-Data field to follow. If the 7bit default-alphabet extension

mechanism is used within the TP-User-Data (see GSM 03.38), the actual number of characters in the message will be

less than the number of septets. If a TP-User-Data-Header field is present, then the TP-User-Data-Length value is the

sum of the number of septets in the TP-User-Data-Header field (including any padding) and the number of septets in the

TP-User-Data field which follows. See figure 9.2.3.24.(a).If the TP-User-Data is coded using 8-bit data, the

TP-User-Data-Length field gives an integer representation of the number of octets within the TP-User-Data field to

follow. If a TP-User-Data-Header field is present, then the TP-User-Data-Length value is the sum of the number of

octets in the TP-User-Data-Header field and the number of octets in the TP-User-Data field which follows. See

figure 9.2.3.24.(b).

If the TP-User-Data is coded using UCS2 [24] data, the TP-User-Data-Length field gives an integer representation of

the number of octets within the TP-User-Data field to follow. If a TP-User-Data-Header field is present, then the

TP-User-Data-Length value is the sum of the number of octets in the TP-User-Data-Header field and the number of

octets in the TP-User-Data field which follows. See figure 9.2.3.24.(b).

If the TP-User-Data is coded using compressed GSM 7 bit default alphabet or compressed 8 bit data or compressed

UCS2 [24] data, the TP-User-Data-Length field gives an integer representation of the number of octets after

compression within the TP-User-Data field to follow. If a TP-User-Data-Header field is present, then the

TP-User-Data-Length value is the sum of the number of uncompressed octets in the TP-User-Data-Header field and the

number of octets in the compressed TP-User-Data field which follows. See figure 9.2.3.24.(c)

For other Data Coding Schemes, see GSM 03.38.If this field is zero, the TP-User-Data field will not be present.

9.2.3.17 TP-Reply-Path (TP-RP)

The TP-Reply-Path is a 1-bit field, located within bit no 7 of the first octet of both SMS-DELIVER and SMS-SUBMIT,

and to be given the following values:

Bit no 7: 0 TP-Reply-Path parameter is not set in this SMS-SUBMIT/DELIVER

1 TP-Reply-Path parameter is set in this SMS-SUBMIT/DELIVER

Please refer to annex D for details about the Reply procedures.

9.2.3.18 TP-Message-Number (TP-MN)

The TP-Message-Number is an 8-bit field allowing an MS to refer uniquely to an SM in the SC which that MS has

previously submitted. The TP-MN value is the TP-MR value of a previously submitted SM.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 59 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.19 TP-Command-Type (TP-CT)

The TP-Command-Type is an 8-bit field specifying the type of operation that the SC is to perform. It has the following

values:

Value (bit 7 .. 0) Command Description Status Report

Request Value

00000000 Enquiry relating to previously submitted short message 1

00000001 Cancel Status Report Request relating to previously

submitted short message

0

00000010 Delete previously submitted Short Message 0

00000011 Enable Status Report Request relating to previously

submitted short message

0

00000100..00011111 Reserved unspecified

11100000..11111111 Values specific for each SC 1 or 0

The SC will return an RP-Error with an appropriate TP-Failure-Cause for any TP-Command value which is reserved,

unsupported or invalid or the actioning of the command has failed.

The SC will return an RP-ACK if the actioning of the Command has succeeded.

A successful Enquiry will result in the SC sending a SMS-STATUS-REPORT for the SM to which the Enquiry refers.

In the case where the SC has a number of SMs which have the same TP-MR, the same TP-DAand have come fromthe

same originating address the SC will send a SMS-STATUS-REPORT for each SM.

In the case where a TP-Command is to Delete a previously submitted short message, the SC will send a Status Report

indicating that the SM has been deleted if the original Submit SM request requested a status Report.

9.2.3.20 TP-Command-Data-Length (TP-CDL)

The TP-Command-Data-Length field is used to indicate the number of octets contained within the

TP-Command-Data-field. If this field is set to zero, the TP-Command-Data field will not be present.

9.2.3.21 TP-Command-Data (TP-CD)

The TP-Command-Data field contains data relating to the operation requested by the MS which is to be performed at the

SC. The maximum length of this field is 157 octets. The usage and provision of the optional TP-Command-Data field

will be determined by the function selected by the TP-Command-Type field.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 60 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.22 TP-Failure-Cause (TP-FCS)

The TP-Failure-Cause field is used to report the reason for failure to transfer or process a short message. It consists of a

single octet used as follows:

TP-FCS

Value

(Hex)

Meaning When used

MO MT

00 - 7F Reserved

80 - 8F TP-PID errors

80 Telematic interworking not supported x

81 Short message Type 0 not supported x x

82 Cannot replace short message x x

83 - 8E Reserved

8F Unspecified TP-PID error x x

90 - 9F TP-DCS errors

90 Data coding scheme (alphabet) not supported x

91 Message class not supported x

92 - 9E Reserved

9F Unspecified TP-DCS error x x

A0 - AF TP-Command Errors

A0 Command cannot be actioned x

A1 Command unsupported x

A2 - AE Reserved

AF Unspecified TP-Command error x

B0 TPDU not supported x x

B1 - BF Reserved

C0 SC busy x

C1 No SC subscription x

C2 SC system failure x

C3 Invalid SME address x

C4 Destination SME barred x

C5 SM Rejected-Duplicate SM x

C6 TP-VPF not supported X

C7 TP-VP not supported X

C8 - CF Reserved

D0 SIM SMS storage full x

D1 No SMS storage capability in SIM x

D2 Error in MS x

D3 Memory Capacity Exceeded X

D4 SIM Application Toolkit Busy x

D5 SIM data download error x

D6 - DF Reserved

E0 - FE Values specific to an application x x

FF Unspecified error cause x x

NOTE: Any reserved codes which are received should be treated as an unspecified error cause.

MT and MO refer to the overall mobile terminated and mobile originated services; not the direction of

transmission of TP-FCS.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 61 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.23 TP-User-Data-Header-Indicator (TP-UDHI)

The TP-User-Data-Header-Indicator is a 1 bit field within bit 6 of the first octet of the following six PDUs:

- SMS-SUBMIT,

- SMS-SUBMIT-REPORT

- SMS-DELIVER,

- SMS-DELIVER-REPORT

- SMS-STATUS-REPORT

- SMS-COMMAND.

TP-UDHI has the following values.

Bit no. 6 0 The TP-UD field contains only the short message

1 The beginning of the TP-UD field contains a Header in addition to the short message

9.2.3.24 TP-User Data (TP-UD)

The length of the TP-User-Data field is defined in the PDU's of the SM-TL ( see subclause 9.2.2 ).

The TP-User-Data field may comprise just the short message itself or a Header in addition to the short message

depending upon the setting of TP-UDHI.

Where the TP-UDHI value is set to 0 the TP-User-Data field comprises the short message only, where the user data can

be 7 bit (default alphabet) data, 8 bit data, or 16 bit (UCS2) data.

Where the TP-UDHI value is set to 1 the first octets of the TP-User-Data field contains a Header in the following order

starting at the first octet of the TP-User-Data field.

Irrespective of whether any part of the User Data Header is ignored or discarded, the MS shall always store the entire

TPDU exactly as received.

FIELD LENGTH

Length of User Data Header 1 octet

Information-Element-Identifier "A" 1 octet

Length of Information-Element "A" 1 octet

Information-Element "A" Data 1 to "n" octets

Information-Element-Identifier "B" 1 octet

Length of Information-Element "B" 1 octet

Information-Element "B" Data 1 to "n" octets

Information-Element-Identifier "n" 1 octet

Length of Information-Element "n" 1 octet

Information-Element "n" Data 1 to "n" octets

The diagram below shows the layout of the TP-User-Data-Length and the TP-User-Data for uncompressed GSM 7 bit

default alphabet data. The UDHL field is the first octet of the TP-User-Data content of the Short Message.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 62 (GSM 03.40 version 7.3.0 Release 1998)

UDL UDHL IEIa IEDa IEIb ......... IEIn IEDLn IEDn Fill bits SM (7bit data)

Septet Boundary Total number of Octets

Length Indicator

Total number of Septets

Length Indicator

Octets Octets

IEIDLa

Figure 9.2.3.24 (a)

The diagram below shows the layout of the TP-User-Data-Length and the TP-User-Data for uncompressed 8 bit data or

uncompressed UCS2 data. The UDHL field is the first octet of the TP-User-Data content of the Short Message.

UDL UDHL IEIa IEDa IEIb ......... IEIn IEDLn IEDn

Octet Boundary Total number of Octets

Length Indicator

Total number of Octets

Length Indicator

Octets Octets

IEIDLa SM (8 bit data

or UCS-2 data)

Figure 9.2.3.24 (b)

The diagram below shows the layout of the TP-User-Data-Length and the TP-User-Data for compressed GSM 7 bit

default alphabet data, compressed 8 bit data or compressed UCS2 data. The UDHL field is the first octet of the TPUser-

Data content of the Short Message.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 63 (GSM 03.40 version 7.3.0 Release 1998)

UDL UDHL IEIa IEDa IEIb ......... IEIn IEDLn IEDn

Octet Boundary Total number of Octets

Length Indicator

Total number of Octets

Length Indicator

Octets Octets

IEIDLa Compressed SM (octets)

Figure 9.2.3.24 (c)

The definition of the TP-User-Data-Length field which immediately precedes the "Length of User Data Header" is

unchanged and will therefore be the total length of the TP-User-Data field including the Header, if present.

(see 9.2.3.16)

The "Length-of-Information-Element" fields shall be the integer representation of the number of octets within its

associated "Information-Element-Data" field which follows and shall not include itself in its count value.

The "Length-of-User-Data-Header" field shall be the integer representation of the number of octets within the

"User-Data-Header" information fields which follow and shall not include itself in its count or any fill bits which may be

present (see text below).

Information Elements may appear in any order and need not necessarily follow the order used in the present document.

If Information Elements are duplicated (either with the same or different content) then the contents of the last occurrence

of the Information Element shall be used. If the length of the User Data Header overall is such that there appear to be

too few or too many octets in the final Information Element then the whole User Data Header shall be ignored.

If any reserved values are received within the content of any Information Element then that part of the Information

Element shall be ignored.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 64 (GSM 03.40 version 7.3.0 Release 1998)

The Information Element Identifier octet shall be coded as follows:

VALUE (hex) MEANING

00 Concatenated short messages, 8-bit reference number

01 Special SMS Message Indication

02 Reserved

03 Value not used to avoid misinterpretation as <LF> character

04 Application port addressing scheme, 8 bit address

05 Application port addressing scheme, 16 bit address

06 SMSC Control Parameters

07 UDH Source Indicator

08 Concatenated short message, 16-bit reference number

09 Wireless Control Message Protocol

0A-6F Reserved for future use

70-7F SIM Toolkit Security Headers

80 - 9F SME to SME specific use

A0 - BF Reserved for future use

C0 - DF SC specific use

E0 - FF Reserved for future use

A receiving entity shall ignore (i.e. skip over and commence processing at the next information element) any information

element where the IEI is Reserved or not supported. The receiving entity calculates the start of the next information

element by looking at the length of the current information element and skipping that number of octets.

The SM itself may be coded as 7, 8 or 16 bit data.

If 7 bit data is used and the TP-UD-Header does not finish on a septet boundary then fill bits are inserted after the last

Information Element Data octet up to the next septet boundary so that there is an integral number of septets for the entire

TP-UD header. This is to ensure that the SM itself starts on an septet boundary so that an earlier Phase mobile will be

capable of displaying the SM itself although the TP-UD Header in the TP-UD field may not be understood.

It is optional to make the first character of the SM itself a Carriage Return character encoded according to the default

7 bit alphabet so that earlier Phase mobiles, which do not understand the TP-UD-Header, will over-write the displayed

TP-UD-Header with the SM itself.

If 16 bit (USC2) data is used then padding octets are not necessary. The SM itself will start on an octet boundary.

If 8 bit data is used then padding is not necessary. An earlier Phase mobile will be able to display the SM itself although

the TP-UD header may not be understood.

It is also possible for mobiles not wishing to support the TP-UD header to check the value of the TP-UDHI bit in the

SMS-Deliver PDU and the first octet of the TP-UD field and skip to the start of the SM and ignore the TP-UD header.

9.2.3.24.1 Concatenated Short Messages

This facility allows short messages to be concatenated to form a longer message.

In the case of uncompressed 8-bit data, the maximum length of the short message within the TP-UD field is 134 (140-6)

octets.

In the case of uncompressed GSM Default 7 bit data, the maximum length of the short message within the TP-UD field

is 153 (160-7) characters.

In the case of 16 bit uncompressed USC2 data, the maximum length of the short message within the TP-UD field is 67

((140-6)/2) characters. A UCS2 character must not be split in the middle; if the length of the User Data Header is odd,

the maximum length of the whole TP-UD field is 139 octets.

In the case of compressed GSM Default alphabet 7 bit data, 8 bit data or UCS2 the maximum length of the compressed

short message within the TP-UD field is 134 ( 140-6) octets including the Compression Header and Compression

Footer, both or either of which may be present ( See subclause 3.9).

The maximum length of an uncompressed concatenated short message is 39015 (255*153) default alphabet characters,

34170 (255*134) octets or 17085 (255*67) UCS2 characters.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 65 (GSM 03.40 version 7.3.0 Release 1998)

The maximum length of a compressed concatenated message is 34170 (255*134) octets including the Compression

Header and Compression Footer ( see subclause 3.9 and Fig 9.2.3.24.1(a) below.

Compression Footer Compressed Data (CD) Compression Header

CD CH TP-UDH CD TP-UDH CD CF TP-UDH

First segment Intermediate segments Final segment

Segmentation / De-segmentation

Figure 9.2.3.24.1.(a) Concatenation of a Compressed short message

The Information-Element-Data field contains information set by the application in the SMS-SUBMIT so that the

receiving entity is able to re-assemble the short messages in the correct order. Each concatenated short message contains

a reference number which together with the originating address and Service Centre address allows the receiving entity to

discriminate between concatenated short messages sent from different originating SMEs and/or SCs. In a network which

has multiple SCs, it is possible for different segments of a concatenated SM to be sent via different SCs and so it is

recommended that the SC address should not be checked by the MS unless the application specifically requires such a

check.

The TP elements in the SMS-SUBMIT PDU, apart from TP-MR, TP-SRR, TP-UDL and TP-UD, should remain

unchanged for each SM which forms part of a concatenated SM, otherwise this may lead to irrational behaviour. TP-MR

must be incremented for every segment of a concatenated message as defined in subclause 9.2.3.6. A SC willl handle

segments of a concatenated message like any other short message. The relation between segments of a concatenated

message is made only at the originator, where the message is segmented, and at the recipient, where the message is

reassembled. SMS-COMMANDs identify messages by TP-MR and therefore apply to only one segment of a

concatenated message. It is up to the originating SME to issue SMS-COMMANDs for all the required segments of a

concatenated message.

The Information-Element-Data octets shall be coded as follows.

Octet 1 Concatenated short message reference number

This octet shall contain a modulo 256 counter indicating the reference number for a particular

concatenated short message. This reference number shall remain constant for every short message which

makes up a particular concatenated short message.

Octet 2 Maximum number of short messages in the concatenated short message.

This octet shall contain a value in the range 0 to 255 indicating the total number of short messages within

the concatenated short message. The value shall start at 1 and remain constant for every short message

which makes up the concatenated short message. If the value is zero then the receiving entity shall ignore

the whole Information Element.

Octet 3 Sequence number of the current short message.

This octet shall contain a value in the range 0 to 255 indicating the sequence number of a particular short

message within the concatenated short message. The value shall start at 1 and increment by one for every

short message sent within the concatenated short message. If the value is zero or the value is greater than

the value in octet 2 then the receiving entity shall ignore the whole Information Element.

9.2.3.24.2 Special SMS Message Indication

There are three levels of "Message Waiting" indication provided within the present document. The first level is to set the

Protocol Identifier to "Return Call message", which indicates that a message is waiting and relies on the text of the

message to supply the detail. The second level uses the Data Coding Scheme with or without Return Call Message (see

GSM 03.38) to indicate the type of message waiting and whether there are some messages or no messages. The third

level is described here, and provides the maximum detail level for analysis by the mobile, i.e. an indication of the

number and type of messages waiting in systems connected to the PLMN. This third level is provided for future

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 66 (GSM 03.40 version 7.3.0 Release 1998)

flexibility, as it cannot immediately be used without compatibility problems with the earliest Phase mobiles. It is

envisaged that this scheme can start to be used once mobiles supporting TP-UDH become widely available.

This information may be stored by the MS in a form other than an SMS message, for example an indicator may be

shown if the number of messages is non-zero or removed if the number of messages is zero. The MS may also store

actual number of messages waiting and provide some other MMI to access this information. Text may be included by

the SMS Service Centre for backward compatibility with the earliest Phase mobiles and the Data Coding Scheme may

also be used to convey this information in parallel for backward compatibility with "middle" Phase mobiles (which

support the use of Data Coding Scheme for Message Waiting Indication but not the use of TP-UDH for Message

Waiting Indication).

The information-Element octets shall be coded as follows:

Octet 1 Message Indication type and Storage

Bit 7 Indicates whether or not the message shall be stored.

Bit 7

0 Discard message after updating indication

1 Store message

In the event of a conflict between this setting and the setting of the Data Coding Scheme (see GSM 03.38) then

the message shall be stored if either the DCS indicates this, or Octet 1 above indicates this.

Bits 6..0 show the message indication type

000 0000 Voice Message Waiting

000 0001 Fax Message Waiting

000 0010 Electronic Mail Message Waiting

000 0011 Other Message Waiting (see GSM 03.38 for definition of "other")

Other values are reserved for future use

Octet 2 Message Count

This octet shall contain a value in the range 0 to 255 indicating the number of messages of the type specified

in Octet 1 waiting. The value 255 shall be taken to mean 255 or greater. In the event of a conflict between this

setting and the setting of the Data Coding Scheme (see GSM 03.38) then the Message Count in the TP-UDH

shall override the indication in the TP-DCS.

If more than one type of message is required to be indicated within one SMS message, then further octets must be used,

as in the following example:

[00] TP-UDL [1E] (30 decimal septets)

[01] Length of TP-UDH [08]

[02] IEI = Special SMS Message Indication [01]

[03] Length = 02

[04] Octet 1 = Voice Mail, do not store [00]

[05] Octet 2 = 04 Messages

[06] IEI = Special SMS Message Indication [01]

[07] Length = 02

[08] Octet 1 = Fax Mail, Store [81]

[09] Octet 2 = 02 Messages

+ 5 Fill bits

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 67 (GSM 03.40 version 7.3.0 Release 1998)

+ 19 seven-bit character message text

The Total number of bits is 210.

9.2.3.24.3 Application Port Addressing 8 bit address

This facility allows short messages to be routed to one of multiple applications in the TE (terminal equipment), using a

method similar to TCP/UDP ports in a TCP/IP network. An application entity is uniquely identified by the pair of TPDA/

TP-OA and the port address. The port addressing is transparent to the transport, and also useful in Status Reports.

The total length of the IE is 2 octets

octet 1 Destination port

This octet contains a number indicating the receiving port, i.e. application, in the receiving device.

octet 2 Originator port

This octet contains a number indicating the sending port, i.e. application, in the sending device.

The port range is up to 255 using 8 bit addressing space. The Integer value of the port number is presented as in GSM

03.40 subclause 9.1.2.1.

VALUE (port number) MEANING

0 - 239 Reserved

240 - 255 Available for allocation by applications

A receiving entity shall ignore (i.e. skip over and commence processing at the next information element) any information

element where the value of the Information-Element-Data is Reserved or not supported.

9.2.3.24.4 Application Port Addressing 16 bit address

This facility allows short messages to be routed to one of multiple applications in the TE (terminal equipment), using a

method similar to TCP/UDP ports in a TCP/IP network. An application entity is uniquely identified by the pair of TPDA/

TP-OA and the port address. The port addressing is transparent to the transport, and also useful in Status Reports.

The total length of the IE is 4 octets

octet 1,2 Destination port

These octets contain a number indicating the receiving port, i.e. application, in the receiving device.

octet 3,4 Originator port

These octets contain a number indicating the sending port, i.e. application, in the sending device.

The port range is up to 65535 using 16 bit addressing space. The Integer value of the port number is presented as in

GSM 03.40 subclause 9.1.2.1.

VALUE (port number) MEANING

0 - 15999 As allocated by IANA (http://www.IANA.com/)

16000 - 16999 Available for allocation by applications

17000 - 65535 Reserved

A receiving entity shall ignore (i.e. skip over and commence processing at the next information element) any information

element where the value of the Information-Element-Data is Reserved or not supported.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 68 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.24.5 SMSC Control Parameters

The facility enables the SMS protocol headers to be expanded using a flexible method. It may be used to control the

SMSC, but is also passed transparently to the receiving mobile. The Information Element must be present in every short

message affected by it, i.e. in every short message in a concatenated message.

The Information Element data octets shall be coded as follows:

octet 1 Selective Status Report

This facility is used to control the creation of Status Reports, depending on the error code of the particular

message. It is also used by the sending entity to request inclusion of the original UDH into the Status

Report. In this case the original UDH must be separated from the rest of the UDH using the Source

Indicator. The TP-SRR must be set in order for the Selective Status Report to be enabled. The bits are

defined as follows

bit 0

0 No Status Report for short message transaction completed

1 Status Report for short message transaction completed

bit 1

0 No Status Report for permanent error when SC is not making any more transfer attempts

1 Status Report for permanent error when SC is not making any more transfer attempts

bit 2

0 No Status Report for temporary error when SC is not making any more transfer attempts

1 Status Report for temporary error when SC is not making any more transfer attempts

bit 3

0 No Status Report for temporary error when SC is still trying to transfer SM

1 Status Report for temporary error when SC is still trying to transfer SM

bits 4 and 5

reserved for future use.

bit 6

0 No activation

1 A Status Report generated by this Short Message, due to a permanent error or last temporary error,

cancels the SRR of the rest of the Short Messages in a concatenated message. This feature can only be

used where a SC is aware of the segmentation of a concatenated SM and is therefore an implementation

matter.

bit 7

0 Do not include original UDH into the Status Report

1 Include original UDH into the Status Report

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 69 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.24.6 UDH Source Indicator

The facility is used to separate the UDH of the original message, a UDH created by the SMSC, and a UDH provided by

the original receiving entity. The Source Indicator is placed in front of the content inserted by the source. The indicated

content (one or more Information-Elements) ends at the next UDH-Source-Indicator, or at the end of the UDH. The

Separator is intended to be used especially in Status Reports, but can also be used by the SMSC to add information into

Short Message (for example Message waiting). The default content for a UDH in a SMS-DELIVERY is the headers

inserted by the sending device, and the default content for a UDH in a SMS-STATUS-REPORT is the headers copied

from the SMS-DELIVERY-REPORT.

Values of octet:

01 The following part of the UDH is created by the original sender (valid in case of Status Report)

02 The following part of the UDH is created by the original receiver (valid in case of Status Report)

03 The following part of the UDH is created by the SMSC (can occur in any message or report)

9.2.3.24.7 SIM Toolkit Security Headers

There are no IEI data values associated with these IEI values and so the associated Length of Information element field

is present but set to zero.

These IEI values implicitly define that a Security Header is always present at the start of the TP-User-Data field which

immediately follows the TP-User-Data-Header. Details of the Security Header will be found in GSM 03.48.

In the case where a concatenated message contains a Security Header then the Security Header will only be present in

the first segment of a concatenated message.

In the case where SMS compression is applied to a TP-User-Data field which contains a Security Header then the SMS

compression header (GSM 03.42) will immediately precede the Security Header.

9.2.3.24.8 Concatenated short messages, 16-bit reference number

This facility is an enhanced variant of the Concatenated Short Message facility (see subclause 9.2.3.24.1). The

enhancement is a 16-bit reference number, instead of the short 8-bit reference number. The larger reference number

reduces the probability that two different concatenated messages are mistakenly sent with identical reference numbers to

a receiver. Except for the size of the reference number this facility is identical to the Concatenated Short Message

facility (see subclause 9.2.3.24.1).

In the case of uncompressed 8-bit data, the maximum length of the short message within the TP-UD field is 133 (140-7)

octets.

In the case of uncompressed GSM Default 7 bit data, the maximum length of the short message within the TP-UD field

is 151 (160-9) characters.

In the case of 16 bit uncompressed USC2 data, the maximum length of the short message within the TP-UD field is 66

((140-7)/2) characters. A UCS2 character must not be split in the middle; if the length of the User Data Header is odd,

the maximum length of the whole TP-UD field is 139 octets.

In the case of compressed GSM Default alphabet 7 bit data, 8 bit data or UCS2 the maximum length of the compressed

short message within the TP-UD field is 133 ( 140-7) octets including the Compression Header and Compression

Footer, both or either of which may be present ( see subclause 3.9).

The relation between compression and concatenation is the same as for Concatenated Short Messages (see

subclause 9.2.3.24.1).

The Information-Element-Data field contains information set by the application in the SMS-SUBMIT so that the

receiving entity is able to re-assemble the short messages in the correct order. Each concatenated short message contains

a reference number which together with the originating address and Service Centre address allows the receiving entity to

discriminate between concatenated short messages sent from different originating SMEs and/or SCs. In a network which

has multiple SCs, it is possible for different segments of a concatenated SM to be sent via different SCs and so it is

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 70 (GSM 03.40 version 7.3.0 Release 1998)

recommended that the SC address should not be checked by the MS unless the application specifically requires such a

check.

The TP elements in the SMS-SUBMIT PDU, apart from TP-MR, TP-UDL and TP-UD, should remain unchanged for

each SM which forms part of a concatenated SM, otherwise this may lead to irrational behaviour. TP-MR must be

incremented for every segment of a concatenated message as defined in subclause 9.2.3.6. A SC will handle segments of

concatenated message like any other short message. The relation between segments of a concatenated message is made

at the originator, where the message is segmented, and at the receipient, where the message is reassembled. SMSCOMMANDs

identify messages by TP-MR and therefore apply to only one segment of a concatenated message. It is up

to the originating SME to issue SMS-COMMANDs for all the required segments of a concatenated message.

The Information-Element-Data octets shall be coded as follows.

Octet 1-2 Concatenated short messages, 16-bit reference number

This octet shall contain a modulo 65536 counter indicating the reference number for a particular enhanced

concatenated short message. This reference number shall remain constant for every short message which

makes up a particular enhanced concatenated short message.

Octet 3 Maximum number of short messages in the enhanced concatenated short message.

This octet shall contain a value in the range 0 to 255 indicating the total number of short messages within

the concatenated short message. The value shall start at 1 and remain constant for every short message

which makes up the enhanced concatenated short message. If the value is zero then the receiving entity

shall ignore the whole Information Element.

Octet 4 Sequence number of the current short message.

This octet shall contain a value in the range 0 to 255 indicating the sequence number of a particular short

message within the concatenated short message. The value shall start at 1 and increment by one for every

short message sent within the concatenated short message. If the value is zero or the value is greater than

the value in octet 3 then the receiving entity shall ignore the whole Information Element.

9.2.3.24.9 Wireless Control Message Protocol

The Wireless Control Message Protocol (WCMP) is part of the WAP suite of protocols; an open standard specified by

the WAP Forum Ltd.

The protocol specifies a set of messages that can be used by the receiver to notify the sender if an error occurs. This can

be due to routing problems, no application listening at the destination port number, or due to insufficient buffer capacity.

The error messages can be used by the sender to avoid retransmitting packets, that can not be properly handled at the

receiver. WCMP can also be used for diagnostics and informational purposes. WCMP messages are usually generated

by a datagram transport layer or a management entity.

The Information-Element-Data octet(s) shall be coded as follows.

Octet 1-n Protocol Data Unit of WCMP

This octet(s) shall contain a WCMP protocol data unit.

9.2.3.25 TP-Reject-Duplicates (TP-RD)

The TP-Reject-Duplicates is a 1 bit field located within bit 2 of the first octet of SMS-SUBMIT and has the following

values.

Bit no. 2: 0 Instruct the SC to accept an SMS-SUBMIT for an SM still held in the

SC which has the same TP-MR and the same TP-DA as a previously submitted SM from the

same OA.

1 Instruct the SC to reject an SMS-SUBMIT for an SM still held in the

SC which has the same TP-MR and the same TP-DA as the previously submitted SM from

the same OA. In this case an appropriate TP-FCS value will be returned in the

SMS-SUBMIT-REPORT.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 71 (GSM 03.40 version 7.3.0 Release 1998)

9.2.3.26 TP-Status-Report-Qualifier (TP-SRQ)

The TP-Status-Report-Qualifier is a 1 bit field located within bit 5 of the first octet of SMS-STATUS-REPORT and has

the following values

Bit no. 5: 0 The SMS-STATUS-REPORT is the result of a SMS-SUBMIT.

1 The SMS-STATUS-REPORT is the result of an SMS-COMMAND e.g.

an Enquiry.

9.2.3.27 TP-Parameter-Indicator (TP-PI)

The TP-Parameter-Indicator comprises a number of octets between 1 and n where each bit when set to a 1 indicates that

a particular optional parameter is present in the fields which follow. The TP-PI is present as part of the RP-User-Data in

the RP-ACK for both the SMS-DELIVER TPDU and the SMS-SUBMIT TPDU.

The structure of the TP-PI is as follows:

Octet 1

bit 7 bit 6 bit 5 bit 4 bit 3 bit 2 bit 1 bit 0

Extension bit Reserved Reserved Reserved Reserved TP-UDL TP-DCS TP-PID

The most significant bit in octet 1 and any other TP-PI octets which may be added later is reserved as an extension bit

which when set to a 1 will indicate that another TP-PI octet follows immediately afterwards.

If the TP-UDL bit is set to zero then by definition then neither the TP-UDL field or the TP-UD field can be present.

If a Reserved bit is set to "1" then the receiving entity shall ignore the setting. The setting of this bit will mean that

additional information will follow the TP-User-Data, so a receiving entity shall discard any octets following the

TP-User-Data.

9.3 Service provided by the SM-RL

9.3.1 General

The Short Message Relay Layer (SM-RL) provides a service to the Short Message Transfer Layer (SM-TL). This

service enables the SM-TL to send Transfer Protocol Data Units (TPDUs) to its peer entity, receive TPDUs from its

peer entity and receive reports about earlier requests for TPDUs to be transferred.

In order to keep track of TPDUs and reports about those TPDUs, primitives between the SM-TL and SM-RL contain a

Short Message Identifier (SMI), which is a reference number for the TPDU associated with the primitive. This Short

Message Identifier is not carried via the SM-RL protocol of subclause 9.3.2. It is carried via the relay layer service

between the SC and GMSC. It is also carried by SM-RL of GSM 04.11, between the visited MSC and MS. The

parameter is not carried by MAP but is mapped to and from the TCAP dialogue Identifier (see CCITT

Recommendation Q.771, "Blue Book") at the GMSC and the visited MSC (therefore the Message Identifier at the

SC/GMSC interface is not the same as at the visited MSC/MS interface).

The SM-RL communicates with its peer entity by the protocol described in the following subclauses.

9.3.2 Protocol element repertoire at SM-RL

Different protocols are required between different pairs of SM-RL entities. Those are described in other GSM

specifications. This subclause gives a survey of the different information elements which have to be conveyed between

those entities. (Note that the notation of the protocol and information elements may vary between different GSM

specifications).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 72 (GSM 03.40 version 7.3.0 Release 1998)

The SM-RL comprises the following 6 protocol elements:

RP-MO-DATA for transferring a TPDU from MS to SC

RP-MT-DATA for transferring a TPDU from SC to MS

RP-ACK for acknowledging an RP-MO-DATA, an RP-MT-DATA or an

RP-SM-MEMORY-AVAILABLE

RP-ERROR for informing of an unsuccessful RP-MO-DATA or an RP-MT-DATA transfer attempt

RP-ALERT-SC for alerting the SC that the MS has recovered operation (information

sent from the HLR to the SC)

RP-SM-MEMORY-AVAILABLE for notifying the network that the MS has memory available to

accept one or more short messages (information sent from the MS to

the HLR)

9.3.2.1 RP-MO-DATA

Basic elements of the RP-MO-DATA type.

Abbr. Reference P1) Description

RP-OA RP-Originating-Address ++- Address of the originating MS.

RP-DA RP-Destination-Address -++ Address of the destination SC.

RP-UD RP-User-Data +++ Parameter containing the TPDU

1) Provision on the links SC<->MSC, MSC<->MSC or MSC<->SGSN, and MSC<->MS or SGSN<->MS indicated

by "xxx", where x may be either "+" or "-", dependent on whether the parameter is mandatory or not on the

respective link.

9.3.2.2 RP-MT-DATA

Basic elements of the RP-MT-DATA type.

Abbr. Reference P1) Description

RP-PRI RP-Priority-Request +-- Parameter indicating whether or not the short

message transfer should be stopped if the originator

SC address is already contained in the MWD.

RP-MMS RP-More-Messages-To-Send OO- Parameter indicating that there are more messages

waiting in the SC

RP-OA RP-Originating-Address +++ Address of the originating SC.

RP-DA RP-Destination-Address ++- Address of the destination MS.

RP-UD RP-User-Data +++ Parameter containing the TPDU

RP-MTI RP-Message Type Indicator O-- Parameter indicating if the TPDU is a SMS Deliver

or a SMS Status Report 2)

RP-SMEA RP-originating SME-Address O-- Address of the originating SME 2)

1) Provision on the links SC<->MSC, MSC<->MSC or MSC<->SGSN, and MSC<->MS or SGSN<->MS

indicated by "xxx", where xmay be "+", "-" or "O", dependent on whether the parameter is mandatory, not present

or optional on the respective link.

2) These information elements may be included in the "Send Routing Information for SM" sent by the SMS-GMSC

to the HLR.

When transmitted, the RP-SMEA shall take the TP-OA value.

When transmitted, the RP-MTI shall be given the following values:

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 73 (GSM 03.40 version 7.3.0 Release 1998)

0 SMS Deliver

1 SMS Status Report.

This may be used by the HLR to distinguish the two cases in order not to apply any filtering mechanism based on

the RP-SMEA value in case of a SMS-Status Report transmission.

9.3.2.3 RP-ACK

The RP-ACK contains the RP-User-Data which is a parameter containing the TPDU (see 9.2.2.1a and 9.2.2.2a).

9.3.2.4 RP-ERROR

Basic elements of the RP-ERROR type.

Abbr. Reference P1) Description

RP-MSI RP-MW-Set-Indication +-- Parameter indicating whether or not the MWI has been

up-dated. 2)

RP-CS RP-Cause +++ Parameter identifying the error type. The RP-Cause

parameter gives the reason why a short message

transfer attempt fails. In practice three relay layer

protocols are used - SC to GMSC/IWMSC (see

GSM 03.47), MAP (see GSM 09.02) and via the radio

interface (see GSM 04.11)

RP-MSIsdn RP-international--MS-ISDN-numbe

r

+-- MSIsdn-Alert of the MS, see subclause 3.2.7 3)

RP-UD RP-User-Data OO O Parameter containing a TPDU

1) Provision on the links SC<->MSC, MSC<->MSC or MSC<->SGSN, and MSC<->MS or SGSN<->MS indicated

by "xxx", where x may be "+", "-" or "O" dependent on whether the parameter is mandatory, not present or

optional on the respective link.

2) Only present when the RP-ERROR is transferred from the SMS-GMSC to the SC.

3) Only present when the RP-MT-DATA transfer attempt failed because the MS is not reachable or because the MS

memory capacity was exceeded and the MSIsdn-Alert is different from the MSIsdn used by the SC to address the

recipient MS

9.3.2.5 RP-ALERT-SC

Basic elements of the RP-ALERT-SC type:

Abbr. Reference P1) Description

RP-MSIsdn RP-International-MS-ISDN-Numbe

r

M MSIsdnoftheMS.

1) Provision;Mandatory (M).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 74 (GSM 03.40 version 7.3.0 Release 1998)

9.3.2.6 RP-SM-MEMORY-AVAILABLE

Basic elements of the RP-SM-MEMORY-AVAILABLE type:

Abbr. Reference P1) Description

RP-IMSI RP-International-Mobile-Subscriber

-Identity

++- IMSI of the MS.

1) Provision on the links HLR<->VLR or HLR<->SGSN, VLR<->MSC and MSC<->MS or SGSN<->MS indicated

by "xxx", where x may be either "+" or "-", dependent on whether the parameter is mandatory or not present on

the respective link.

10 Fundamental procedures within the point-to-point

SMS

The point-to-point SMS comprises 3 fundamental procedures:

1) Short message mobile terminated. This procedure consists of all necessary operations to:

a) transfer a short message or status report from the SC to the MS;

b) return a report to the SC, containing the result of the message transfer attempt.

2) Short message mobile originated. This procedure consists of all necessary operations to:

a) transfer a short message from the MS to the SC;

b) return a report to the MS, containing the result of the message transfer attempt.

3) Transfer of an Alert. This procedure consists of all necessary operations for an HLR or a VLR to initiate a

transfer of an Alert to a specific SC, informing the SC that the MS has recovered operation.

GSM 09.02 defines operations necessary for the provision of the Short Message Service point-to-point. The operations

defined in clause 10 describe the requirement that the Short Message Service puts upon the network functionality. If

discrepancies exist in nomenclature, it is the GSM 09.02 that will be the reference.

Annex C indicates the flow of primitives and parameters during the short message transfer between the SC and the MS.

Both the Mobile terminated and the Mobile originated cases are covered.

10.1 Short message mobile terminated

The entities involved in this procedure are depicted in figure 03.40/14.

SC SMSC-GMSC MSC

MS

x

HLR VLR

SGSN

NOTE: Since the short message mobile terminated procedure covers the functionality required at SM-RL for

transferring TPDUs from SC to MS, the procedure described covers both short message (SMS-DELIVER)

and status report (SMS-STATUS-REPORT) transfer. The term "short message transfer" therefore, in this

clause, covers both cases.

Figure 03.40/14: Interfaces involved in the Short message mobile terminated procedure.

GSM 03.02. X is the interface between an MSC and an SC as defined in clause 5.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 75 (GSM 03.40 version 7.3.0 Release 1998)

In figure 03.40/15, sequence diagrams are shown for the following basic situations of short message mobile terminated

transfer attempt:

- Successful short message transfer via the MSC or the SGSN;

- Short message transfer attempt failing due to error at the SMS-GMSC;

- Short message transfer attempt failing due to negative outcome of HLR information retrieval;

- Short message transfer attempt failing due to error at the MSC or SGSN;

- Short message transfer attempt failing due to negative outcome of VLR information retrieval;

- Short message transfer attempt failing due to erroneous message transfer on the radio path.

- Short message transfer attempt failing over the first path (e.g. SGSN) and succeeding over the second path (e.g.

MSC)

- Short message transfer attempt failing over the first path (e.g. SGSN) and over the second path (e.g. MSC)

References to the relevant specifications of the different operations are given in clause 4.

SC SMS-GMSC HLR MSC or SGSN VLR

1a. Message

transfer

2. SendRoutingInfo

ForShortMsg

4a. ForwardShortMessage

5. sendInfoFor-

MT-SMS

6. Message transfer

3. SM-Delivery

report

1b. Delivery

ReportStatus

4b. Delivery report

Operation invocation or message transfer.

Successful operation invocation or message transfer including report.

MS

-

1)

NOTE:

1): This operation is not used by the SGSN

Figure 03.40/15a): Successful short message transfer attempt via the MSC or the SGSN

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 76 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-GMSC HLR MSCor SGSN VLR MS

1a. Message

transfer

1c. Failure

report

Operation invocation or message transfer

Error report

Figure 03.40/15b): Short message transfer attempt failing due to error at the SMS-GMSC

SC SMS-GMSC HLR MSC or SGSN VLR MS

1a. Message

transfer

2. sendRoutingInfo

ForShortMsg

1c. Failure

report

7. InformSC

Operation invocation or message transfer.

Error report

-

Unsuccessful operation invocation ro message transfer including report

Figure 03.40/15c): Short message transfer attempt failing due to negative outcome of

HLR information retrieval

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 77 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-GMSC HLR MSC or SGSN VLR MS

1a. Message

transfer

2. SendRoutingInfo

ForShortMsg

4a. ForewardShortMessage

1c. Failure

report

4c. Failure report

3a. SM-Delivery

ReportStatus

Operation invocation or message transfer.

Successful operation invocation or message transfer including report.

Unsuccessful operation invocation or message transfer including report.

Error report

(or with missing confirmation)

-

Figure 03.40/15d): Short message transfer attempt failing due to error at the MSC or SGSN

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 78 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-GMSC HLR MSC VLR MS

Operation invocation or message transfer.

Successful operation invocation or message transfer including report.

Unsuccessful operation invocation or message transfer including report.

Error report

(or with missing confirmation)

1a. Message

transfer

2. SendRoutingInfo

ForShortMsg

4a. ForwardShortMessage

5. sendInfoFor-

MT-SMS

4c. Failure report

3a. SM-Delivery

ReportStatus

1c. Failure

report

-

Figure 03.40/15e): Short message transfer attempt failing due to negative outcome of

VLR information retrieval

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 79 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-GMSC HLR MSC or SGSN VLR MS

Operation invocation or message transfer.

Successful operation invocation or message transfer including report.

Unsuccessful operation invocation or message transfer including report.

Error report

(or with missing confirmation)

1a. Message

transfer

2. SendRoutingInfo

ForShortMsg

4a. ForwardShortMessage

4c. Failure report

3. SM-Delivery

ReportStatus

1c. Failure

report

5. sendInfoFor-

MT-SMS

6. Message transfer

-

1)

NOTE:

1): This operation is not used by the SGSN

Figure 03.40/15f): Short message transfer attempt failing due to erroneous message transfer

on the radio path

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 80 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-GMSC HLR MSC or SGSN VLR MS

1a. Message

transfer 2. SendRoutingInfo

-

ForShortMsg 2)

4a. ForwardShortMessage (e.g over SGSN)

5. sendInfoFor- 1)

MT-SMS

4c. Failure Report

4a. ForwardShortMessage (e.g over MSC) 4)

5. sendInfoFor- 1)

MT-SMS

6. Message Transfer

4b. Delivery Report

3. SM-Delivery

ReportStatus3)

1b. Delivery

report

Operation invocation or message transfer.

Successful operation invocation or message transfer including report.

Error report

Unsuccessful operation invocation or message transfer including report.

(or with missing confirmation)

NOTES:

1): This operation is not used by the SGSN

2): Two addresses (SGSN and MSC) are received from HLR

3): Successful transfer over second path and unsuccessful transfer over first path (e.g. Absent subscriber) are sent to

HLR

4): The SMS transfer towards the second path is only triggered by the reception of some MAP errors on the first path

as described in chapter 8.1.1.

Figure 03.40/15g): Short message transfer attempt failing over the first path (e.g. SGSN) and

succeeding over the second path (e.g. MSC)

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 81 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-GMSC HLR MSC or SGSN VLR MS

1a. Message

transfer 2. SendRoutingInfo

-

ForShortMsg 2)

4a. ForwardShortMessage (e.g over SGSN)

5. sendInfoFor- 1)

MT-SMS

4c. Failure Report

4a. ForwardShortMessage (e.g over MSC) 4)

5. sendInfoFor- 1)

MT-SMS

6. Message Transfer

4c. Failure Report

3. SM-Delivery

ReportStatus3)

1b. Failure

report

Operation invocation or message transfer.

Successful operation invocation or message transfer including report.

Error report

Unsuccessful operation invocation or message transfer including report.

(or with missing confirmation)

NOTES:

1): This operation is not used by the SGSN

2): Two addresses (SGSN and MSC) are received from HLR

3): Unsuccessful transfer over the second path (e.g. MemoryCapacityExceeded) and over the first path (e.g. Absent

subscriber) are sent to HLR

4): The SMS transfer towards the second path is only triggered by the reception of some MAP errors on the first path

as described in chapter 8.1.1.

Figure 03.40/15h): Short message transfer attempt failing over the first path (e.g. SGSN) and

over the second path (e.g. MSC)

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 82 (GSM 03.40 version 7.3.0 Release 1998)

Operation 1: Message transfer SC -> SMS-GMSC

This operation is used to transfer a short message from an SC to an SMS-GMSC.

The operation consists of:

- the transfer of a message containing the TPDU from the SC to the SMS-GMSC (see "1a. Message transfer" in

figure 03.40/15); and

- the return of either a "Failure report" (see 1c. in figure 03.40/15) or a "Delivery report" (see 1b. in

figure 03.40/15).

"Failure report" is returned to the SC when the SMS-GMSC has received indication from another entity (MSC, SGSN or

HLR) the procedure was unsuccessful. The error indications which the SMS-GMSC may receive from the MSC, SGSN,

HLR, VLR or MS enable the SMS-GMSC to return one of the error indications given in subclause 3.3 back to the SC.

Operation 2: sendRoutingInfoForShortMsg

The operation is an interrogation of the HLR by the SMS-GMSC to retrieve information necessary to forward the short

message.

The result may contain the MSC, SGSN or both addresses, and shall also indicates which address belongs the MSC and

the SGSN.

Operation 3: SM-DeliveryReportStatus

The operation provides a means for the SMS-GMSC to request the HLR to add an SC address to the MWD, and is

activated when the SMS-GMSC receives an absent subscriber indication from the MSC, SGSN or both, and/or when the

SMS-GMSC receives a failure report for a short message transfer with cause MS Memory Capacity Exceeded via the

MSC or SGSN. The Return Result optionally contains the MSIsdn-Alert.

This operation is also activated at successful delivery short message when the MNRF, MNRG or both are set in HLR.

The operation consists of:

- the transfer of a message, containing the MSISDN of the MS to which the short message was addressed, the

SC-address, the successful outcome and/or the causes (Absent Subscriber, MS memory capacity exceeded or

both) for updating the MWD, from the SMS-GMSC to the HLR (see 3. in figure 03.40/15).

Operation 4: forwardShortMessage

The operation provides a means for the SMS-GMSC to transfer a short message to the MSC or to the SGSN at which the

MS is currently located.

The operation works in tandem with the forwarding of the short message from the MSC or from the SGSN to the MS.

Thus, the outcome of the operation comprises either success, i.e. that the message has been delivered to the MS; or a

failure that may be caused by several reasons, e.g. failure in the transfer SMS-GMSC -> MSC or SMS-GMSC -> SGSN,

MS being detached, or no paging response.

It should be noted that the MNRG setting is implicitly carried out in SGSN when the message transfer is denied due to

GPRS DETACH

Operation 5: sendInfoForMT-SMS

The operation provides a means for the MSC to retrieve subscriber information from VLR for mobile terminated short

message transfer. The operation may be associated with an authentication procedure, as shown in figure 03.40/16.

Unsuccessful retrieval (e.g. absent subscriber) is indicated by a cause indication to the SMS-GMSC.

An overall depiction of how operation 5 interacts with signalling on the radio path is given in figure 03.40/16.

It should be noted that the MNRF setting is implicitly carried out when the message transfer is denied due to IMSI

DETACH.

NOTE: This operation is not used by the SGSN.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 83 (GSM 03.40 version 7.3.0 Release 1998)

Operation 6: Message transfer MSC -> MS

The operation is used to transfer a short message from the MSC to the MS.

If the transfer is not successful, e.g. due to the MS losing radio coverage after having successfully authenticated, a

failure report (RP-ERROR) is returned to the SMS-GMSC. In this case, MWD and MCEF in the HLR will be updated

only for the case where the transfer fails with cause MS Memory Capacity Exceeded.

If the MS notifies the network that the MS has been unable to accept a short message because its memory capacity has

been exceeded, then the ME will set the memory capacity Exceeded Notification flag if present.

Operation 7: InformSC

The operation is used to transfer the MSIsdn-Alert from the HLR to the SMS-GMSC in case of the error Absent

Subscriber or positive result given as an answer to the operation SendRoutingInfoForSM.

SC SMS-GMSC HLR MSC or SGSN VLR MS





4a. forwardShortMessage

>



5a. sendInfoFor-

>

MT-SMS 2)

Page 1) 

<> 





Authent. 1) 

<> 



5b. sendInfoFor-

<

MT-SMS (Ack) 2)





6. Message transfer (correct) 

<> 



4b. Delivery report

<



>: Operation invocation or message transfer

<>: Successful operation invocation or message transfer incl. report

NOTES:

1): Described in GSM 04.08 and GSM 09.02

If the SGSN is used, Paging and Authentication are performed from SGSN

2): This operation is not used by the SGSN

Figure 03.40/16a): "Send information for MT SMS" procedure; error free case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 84 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-GMSC HLR MSC or SGSN VLR MS





4a. forwardShortMessage 

> 



5a. sendInfoFor-

>

MT-SMS 1)





5c. Failure 

<- - - - - - - -

report 1)



4c. Failure report 

<- - - - - - - - - - - - - - - - - -



3a. SMDelivery 

>

ReportStatus

>: Operation invocation or message transfer

- - - -> : Error report

NOTE:

1): The GPRS DETACH information is in the SGSN

This operation is not used by the SGSN

Figure 03.40/16b): "Send information for MT SMS" procedure;

erroneous case: absent subscriber (e.g. IMSI DETACH or GPRS DETACH)

SC SMS-GMSC HLR MSC or SGSN VLR MS





4a. forwardShortMessage 

>



5a. sendInfoFor-

>

MT-SMS 2)

Page 1) 

>



5c. Paging 

<- - - - - - - -

failure2) 





4c. Failure report 

<- - - - - - - - - - - - - - - - - -



3a. SM-Delivery 

>

ReportStatus 

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 85 (GSM 03.40 version 7.3.0 Release 1998)

>: Operation invocation or message transfer

- - - -> : Error report

NOTES:

1): Described in GSM 04.08 and GSM 09.02

If the SGSN is used, Paging is performed from SGSN

2): This operation is not used by the SGSN

Figure 03.40/16c): "Send information for MT SMS" procedure;

erroneous case: Absent subscriber (e.g. no paging response)

SC SMS-GMSC HLR MSC or SGSN VLR MS





4a. forwardShortMessage 

> 



5a. sendInfoFor-

>

MT-SMS 2)

Page 1) 

<> 





Authent. 1) 

<- - - - - - - ->

(incorr. resp.)



5c. 

<- - - - - - - -

auth. failure 2)



4c. Failure report 

<- - - - - - - - - - - - - - - - - -



>: Operation invocation or message transfer

- - - -> : Error report

<- - - -> : Unsuccessful operation invocation or message transfer including error report

(or with missing confirmation)

NOTES:

1): Described in GSM 04.08 and GSM 09.02

If the SGSN is used, Paging and Authentication are performed from SGSN

2): This operation is not used by the SGSN

Figure 03.40/16d): "Send information for MT SMS" procedure; incorrect authentication

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 86 (GSM 03.40 version 7.3.0 Release 1998)

10.2 Short message mobile originated

The entities involved in this procedure is depicted in figure 03.40/17.

SC

SMS-IWMSC

MSC MS

x

VLR

SGSN

Figure 03.40/17: Interfaces involved in the Short message mobile originated procedure

GSM 03.02. X is the interface between an MSC or an SGSN and an SC as defined in chapter 5

Note that since the short message mobile originated procedure covers the functionality required at SM-RL for

transferring TPDUs from SC to MS, the procedure described covers both short message (SMS-SUBMIT) and command

(SMS-COMMAND) transfer. The term "short message transfer" therefore in this subclause, covers both cases.

In figure 03.40/18, sequence diagrams for the following basic situations of short message mobile terminated transfer

attempt:

- Successful short message transfer;

- Short message transfer attempt failing due to error at the MSC or SGSN;

- Short message transfer attempt failing due to negative outcome of VLR information retrieval;

- Short message transfer attempt failing due to error at the SMS-IWMSC;

- Short message transfer attempt failing due to error at the SC.

References to the relevant specifications of the different operations are given in clause 4.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 87 (GSM 03.40 version 7.3.0 Release 1998)



Access request 

<>

and possible 

authentication 1)





7a. Message transfer 

<





8a. sendInfoFor-

<>

MO-SMS 2)





9. forwardShortMessage 

<



10a. Message

<

transfer





10b. Delivery

>

report 



9b. Delivery report 

>



7b. Delivery report 

>



> : Operation invocation or message transfer

<> : Successful operation invocation or message transfer including report

NOTES:

1): Described in GSM 04.08 and GSM 09.02.

2): This operation is not used by the SGSN

Figure 03.40/18a): Successful short message transfer attempt

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 88 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-IWMSC HLR MSC or SGSN VLR MS





Access request 

<>

and possible 

authentication 1)





7a. Message transfer 

<





7c. Failure report 

- - - - - - - - - - - - - - - - ->



> : Operation invocation or message transfer

<> : Successful operation invocation or message transfer including report

- - - -> : Error report

NOTE:

1) :Described in GSM 04.08 and GSM 09.02

Figure 03.40/18b): Short message transfer attempt failing due to error at the MSC or SGSN

SC SMS-IWMSC HLR MSC or SGSN VLR MS





Access request 

<>

and possible 

authentication 1)





7a. Message transfer 

<





8. sendInfoFor-

<- - - - - - - ->

MO-SMS 2)





7c. Failure report 

- - - - - - - - - - - - - - - - ->



> : Operation invocation or message transfer

<> : Successful operation invocation or message transfer including report

- - - -> : Error report

<- - - -> : Unsuccessful operation invocation or message transfer incl. error report (or with

missing confirmation)

NOTES:

1): Described in GSM 04.08 and GSM 09.02

2): This operation is not used by the SGSN

Figure 03.40/18c): Short message transfer attempt failing due to negative outcome of

VLR information retrieval

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 89 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-IWMSC HLR MSC or SGSN VLR MS



Access request 

<>

and possible 

authentication 1)





7a. Message transfer 

<





8a. sendInfoFor-

<>

MO-SMS 2)





9. forwardShortMessage 

<







9c. Failure report 

- - - - - - - - - - - - - - - - - ->



7c. Failure report 

- - - - - - - - - - - - - - - - ->



> : Operation invocation or message transfer

<> : Successful operation invocation or message transfer including report

- - - -> : Error report

NOTES:

1): Described in GSM 04.08 and GSM 09.02

2): This operation is not used by the SGSN

Figure 03.40/18d): Short message transfer attempt failing due to error at the SMS-IWMSC

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 90 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-IWMSC HLR MSC or SGSN VLR MS



Access request 

<>

and possible 

authentication 1)





7a. Message transfer 

<





8a. sendInfoFor-

<>

MO-SMS 2) 





9. forwardShortMessage 

<



10a. Message

<

transfer





10c. Failure

- - - - - - - ->

report 



9c. Failure report 

- - - - - - - - - - - - - - - - - ->



7c. Failure report 

- - - - - - - - - - - - - - - - ->



> : Operation invocation or message transfer

<> : Successful operation invocation or message transfer including report

- - - -> : Error report

NOTES:

1): Described in GSM 04.08 and GSM 09.02.

2): This operation is not used by the SGSN

Figure 03.40/18e): Short message transfer attempt failing due to error at the SC

Operation 7: Message transfer MS -> MSC or MS -> SGSN

The operation is used to transfer a shortmessage fromthe MS to theMSC or to the SGSN.

Operation 8: sendInfoForMO-SMS

The operation provides a means for the MSC to verify from the VLR that the mobile originated short message transfer

does not violate supplementary services invoked or restrictions imposed using the network feature Operator Determined

Barring.

A successful VLR response carries the MSIsdn of the originating MS being transferred to the SC at SM-RL.

NOTE: This operation is not used by SGSN.

Operation 9: forwardShortMessage

The operation provides a means for the MSC or for the SGSN to transfer a short message to the SMS-IWMSC.

The procedure is required if the serving MSC or SGSN cannot access the SC directly, e.g. because it has no connection

to SC (see clause 5).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 91 (GSM 03.40 version 7.3.0 Release 1998)

The procedure works in tandem with the forwarding of the short message from the SMS-IWMSC to the SC. Thus, the

outcome of the operation comprises either success, i.e. that the message has been delivered to the SC; or a failure that

may be caused by several reasons, e.g. failure in the transfer MSC --> SMS-IWMSC or SGSN --> SMS-IWMSC, SC

does not comply.

Operation 10: Message transfer SMS-IWMSC -> SC

The operation is used to transfer a short message from an SMS-IWMSC to an SC, and consists of:

- the transfer of a message containing the TPDU from the SMS-IWMSC to the SC (see "10a. Message transfer" in

figure 03.40/18); and

- the return of either a "Failure report" (see 10c. in figure 03.40/18) or a "Delivery report" (see 10b. in

figure 03.40/18).

"Failure report" is returned to the MS when the SMS-IWMSC has received indication from the network or the SC that

the procedure was unsuccessful.

10.3 Alert transfer

The entities involved in this procedure are depicted in figure 03.40/19.

SC SMS-IWMSC MSC MS

x

VLR HLR

SGSN

Figure 03.40/19: Interfaces involved in the Alert procedure. X is the interface between an SC and

an MSC as defined in clause 5

This procedure consists of the operations shown in figure 03.40/20.

Three cases are distinguished:

- the MS becomes reachable when the MNRF, MNRG or both are set but the MCEF is not set (figure 03.40/20a);

- the MS becomes reachable when the MNRF, MNRG or both, and the MCEF are set (figure 03.40/20b);

- the MS notifies the network that it has memory available to receive one or more short messages when the MCEF

is set (figure 03.40/20c).

The operations between MSC and VLR, between HLR and VLR or SGSN and between HLR and SMS-IWMSC are

specified in GSM 09.02. The operation between MS and MSC or SGSN is specified in GSM 04.11. References to

specifications of other operations are given in clause 4.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 92 (GSM 03.40 version 7.3.0 Release 1998)

SC SMS-IWMSC HLR MSC VLR or SGSN MS





11. ReadyForSM 

<

(MS reachable) 1) 



12. alertService-

<

Centre 





13. Service- 

<

CentreAlert



>: Operation invocation or message transfer

NOTE:1): In case ReadyForSM is sent by the SGSN, the reason may be MS reachable via the SGSN, or MS

reachable via the SGSN and the MSC (see GSM 03.60).

Figure 03.40/20a: The alert procedure when the MS becomes reachable,

MNRF, MNRG or both are set and MCEF is not set

SC SMS-IWMSC HLR MSC VLR or SGSN MS





11. ReadyForSM 

<

(MS reachable) 1) 

>: Operation invocation or message transfer

NOTE:1): In case ReadyForSM is sent by the SGSN, the reason may be MS reachable via the SGSN, or MS

reachable via the SGSN and the MSC (see GSM 03.60).

Figure 03.40/20b: The alert procedure when the MS becomes reachable,

MNRF, MNRG or both are set and MCEF is set

SC SMS-IWMSC HLR MSC or SGSN VLR MS



ReadyForSM 

14. (smMemoryCapacityAvailable) 1) 

<>





12. alertService-

<

Centre 



13. Service- 

<

Centrealert





> : Operation invocation or message transfer

<> : Successful operation invocation or message transfer including report

NOTE:1): Described in GSM 04.11 and GSM 09.02.

Figure 03.40/20c: The alert procedure when the MS notifies the network that it has

memory available to receive one or more short messages and MCEF is set

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 93 (GSM 03.40 version 7.3.0 Release 1998)

Operation 11: ReadyForSM (MS reachable)

The operation provides a means to transfer alert information from VLR or SGSN to HLR.

The procedure is activated when the VLR or the SGSN detects that the MS is active, i.e. when the MS responds to a

paging request.

Operation 12: alertServiceCentre

The operation provides a means to transfer alert information from HLR to MSC.

Operation 13: ServiceCentrealert

The operation provides a means to transfer alert information from an SMS-IWMSC to an SC.

The operation consists of transfer of a message ("RP-ALERT-SC") from the SMS-IWMSC to the SC.

Operation 14: ReadyForSM (smMemoryCapacityAvailable)

The operation provides a means for the MS to notify the network that it has memory available to receive one or more

short messages.

The following applies if the memory capacity available notification flag is implemented in the SIM.

The operation consists of transfer of a message ("RP-SM-MEMORY-AVAILABLE") from the MS to the HLR, and the

return of an acknowledgement to the MS. When the MS rejects a short message due to lack of available memory

capacity the need to transfer notification shall be stored in the SIM. After a attempt to transfer the

RP-SM-Memory-Available message the following applies:

If the MS receives a positive acknowledgement it will unset the memory capacity exceeded notification flag in the SIM

and exit this procedure.

If the MS receives a negative acknowledgement indicating a permanent failure condition (as specified in GSM 04.11) it

will unset the memory capacity exceeded notification flag in the SIM and exit the procedure.

If the MS receives a negative acknowledgement indicating a temporary failure condition (as specified in GSM 04.11) or

receives no acknowledgement or an indication of failure by lower layers, it will repeat the attempt to transfer the

message in accordance with procedures defined in GSM 04.11. If these repeat procedures fail, the mobile will unset the

memory capacity exceeded notification flag in the SIM and exit this procedure.

If memory capacity has become available because memory is cleared, the value of the memory capacity exceeded

notification flag is read. If the flag is set, the MS notifies the network that memory capacity is now available as

described above.

When the mobile is powered up or the SIM is inserted, the mobile shall check the memory capacity exceeded

notification flag in the SIM; if the flag is set and the SIM has memory available to receive a short message the mobile

shall attempt to notify the network that it has memory available, as described above.

11 Mapping of error causes between RP layers

This clause describes the interworking between the relay layers on the radio interface (i.e. between the servicing

MSC/SGSN and the mobile station), and within the network (i.e. between servicing MSC/SGSN, VLR, HLR, or

GMSC).

11.1 Mobile Terminated short message transfer

If errors are indicated by the VLR after invocation of the "sendInfoFor-MT-SMS" operation, the appropriate error

information is returned to the SMS-GMSC in a failure report as specified in GSM 09.02 (negative outcome of

"forwardShortMessage" see clause 10),

If errors are detected by the MSC or by the SGSN during the transfer on the radio interface, the error cause returned in

the return error of the MAP procedure ForwardShortMessage shall be set as follows:

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 94 (GSM 03.40 version 7.3.0 Release 1998)

Failure at the MSC or SGSN Return error to be included in the MAP-proc

RP-ERROR message with error cause:

22 Memory capacity exceeded SM_DeliveryFailure with

cause "MemoryCapacityExceeded"1)

Other error causes SM_DeliveryFailure with

cause "equipmentProtocolError"1)

CP or lower layer error SM_DeliveryFailure with

(e.g. RR, layer 2 failure)2) cause "equipmentProtocolError"1)

Mobile has no SM capability SM_DeliveryFailure with

cause "equipmentNotSM-Equiped"1)0

TR1N timeout 2) SM_DeliveryFailure with

MNSMS-error-ind (No SAPI 3) cause "equipmentProtocolError"1)

1) For definition of MAP error SM_DeliveryFailure and its parameter "cause" see GSM 09.02.

2) The error causes of the RP-ERROR message, the CP layer and timer TR1N are defined in

GSM 04.11.

11.2 Memory available notification

If errors are indicated by the HLR (via the VLR or the SGSN) after invocation of the "ReadyForSM" operation, the

MSC or the SGSN shall return the appropriate error information to the MS in a failure report (i.e. a RP-ERROR

message) containing the following error cause:

Return error from ReadyForSM

(Alert Reason is "memory available")

Cause value in the RP-ERROR message

DataMissing

UnexpectedDataValue

UnknownSubscriber

FacilityNotSupported

System Failure

38 Network out of order

38 Network out of order

30 Unknown Subscriber

69 Requested facility not implemented

38 Network out of order

Local or lower layer failure

(e.g. reject condition, timer expired or transaction abort)

38 Network out of order

NOTE: The coding and the use of the RP-ERROR message is specified in GSM 04.11.

11.3 Mobile Originated short message transfer

If errors are indicated by the VLR after invocation of the "sendInfoForMO-SMS" operation.(see clause 10), the MSC

shall return the appropriate error information to the MS in a failure report (i.e. a RP-ERROR message) containing the

following error cause:

Return error from SendInfoForMO-SMS Cause value in the RP-ERROR message

DataMissing 38 Network out of order

UnexpectedDataValue 38 Network out of order

TeleserviceNotProvisioned 50 Requested facility not subscribed

CallBarred

- barringServiceActive 10 Call barred

- operatorBarring 8 Operator determined barring

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 95 (GSM 03.40 version 7.3.0 Release 1998)

NOTE: The coding and the use of the RP-ERROR message is specified in GSM 04.11.The operation

SendInfoForMO-SMS is not used by the SGSN.

If errors are indicated by the SMS-IWMSC (negative outcome of the "forwardShortMessage),) the MSC or the SGSN

shall send a failure report (i.e. a RP-ERROR message) to the MS, with the error cause coded as follows:

Return error from ForwardShortMessage Cause value in the RP-ERROR message

DataMissing 38 Network out of order

FacilityNotSupported 69 Requested facility not implemented

UnexpectedDataValue 38 Network out of order

SM-DeliveryFailure 1 Unassigned number

cause: unknownSC

SM-DeliveryFailure 42 Congestion

cause: SC-Congestion

SM-DeliveryFailure 21 Short message transfer rejected

cause: invalidSME-Addr

SM-DeliveryFailure 28 Unidentified subscriber

cause: subscriberNotSC-Subscriber

Local or lower layer failure 38 Network out of order

(e.g. reject condition,

timer expired or transaction abort)

NOTE: The coding and the use of the RP-ERROR message is specified in GSM 04.11.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 96 (GSM 03.40 version 7.3.0 Release 1998)

Annex A (informative):

Protocol stacks for interconnecting SCs and MSCs

No mandatory protocol between the Service Centre (SC) and the Mobile Switching Centre (MSC) below the transfer

layer is specified by GSM; this is a matter of agreement between SC and PLMN operators.

Some example protocols are provided in GSM 03.47 to assist SC and PLMN operators. These are based on the

following principles, which SC and PLMN operators are recommended to follow even if they choose not to use one of

the examples given in GSM 03.47:

The protocol(s) between SC and MSC below transfer layer should:

a) provide the service defined for SM-RL (see Section 9.3);

b) be based on widely accepted telecommunications protocols in the public domain;

c) permit open interconnection.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 97 (GSM 03.40 version 7.3.0 Release 1998)

Annex B (informative):

Information now contained in GSM 03.38

Annex B held information that is now contained in GSM 03.38.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 98 (GSM 03.40 version 7.3.0 Release 1998)

Annex C (informative):

Short message information flow

The diagrams in this annex describe the flow of primitives and parameters during the short message transfer. These

diagrams refer to specifications GSM 03.40, 04.11 and 09.02. The parameters in dotted lines are optional. The

abbreviations used in diagrams are listed below. The relevant specifications are given in parentheses. (*) stands for a

common GSM abbreviations and (-) for a general abbreviation.

CM Call Management (*)

CS CauSe (-)

DA Destination Address (-)

DCS Data Coding Scheme (03.40)

DI Dialogue Identifier TCAP

GMSCA Gateway MSC Address

GPRS General Packet Radio Services (03.60)

HLR Home Location Register (*)

IMSI International Mobile Subscriber Identity (*)

MAL MSIsdn-Alert (03.40)

MMS More Messages to Send (03.40)

MR Message Reference (03.40)

MS Mobile Station (*)

MSC Mobile services Switching Centre (*)

MSCA MSC Address

MSI Mobile waiting Set Indication (03.40)

MSIsdn Mobile Station ISDN number (*)

MSM More Short Messages (09.02)

MSRN Mobile Station Roaming Number (*)

MT Message Type (04.11)

MTI Message Type Indicator (04.11)

MWS Message Waiting Set (03.40)

OA Originating Address (-)

OC Operation Code (09.02)

PCI Protocol Control Information (-)

PDI Protocol DIscriminator (*)

PRI PRIority (03.40)

RCT ReCeption Time (03.40)

REA REcipient Address (03.40)

RL ReLay function (04.11)

RP Reply Path (03.40)

SC Service Centre (03.40)

SCA Service Centre Address (03.40)

SCTS Service Centre Time Stamp (03.40)

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 99 (GSM 03.40 version 7.3.0 Release 1998)

SGSN Serving GPRS Support Node (03.0)

SM Short Message (03.40)

SM-AL Short Message Application Layer (03.40)

SME Short Message Entity (03.40)

SMI Short Message Identifier (03.40)

SM-RL Short Message Relay Layer (03.40, 04.11)

SMS-GMSC Short Message Service Gateway MSC (03.40)

SMS-IWMSC Short Message Service Interworking MSC (03.40)

SoR Status of Report (03.40)

SM-TL Short Message Transfer Layer (03.40)

SRI Status Report Indication (03.40)

SRR Status Report Request (03.40)

ST STatus (03.40)

TCAP Transaction Capabilities Application Part (-)

TID Transaction Identifier (*)

UD User Data (-)

UDL User Data Length (03.40)

VLR Visitor Location Register (*)

VP Validity Period (03.40)

VPF Validity Period Format (03.40)

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 100 (GSM 03.40 version 7.3.0 Release 1998)

DCS

SERVICE CENTRE

SMI DA OA PID SM

OA PID DCS SCTS MMS UDL MTI UD

SMI DA OA

PRI OA DA UD

SCA

UD

SM TL

SM RL

SMS-DELIVER

MSISDN SC

PRI

PRI

SME

RS-MT-DATA.REQ

TO THE SMS-GMSC

SM AL

SMI

SRI

RP SRI

RP

MMS

MMS RP-MT-DATA

TS-DELIVER.REQ

NOTE: SMI is not carried via SM-RL of subclause 9.3.5 but is carried via the relay service between the SC and GMSC (see subclause 9.3.4.1).

Figure 1.1: Mobile terminated short message

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 101 (GSM 03.40 version 7.3.0 Release 1998)

SM RL

H L R

PRI

DA OA UD PRI OA DA

DA TCAP

MSISDN

SMS-GMSC

OC MSISDN SCA

OC

FORWARD SHORT

MESSAGE (09.02)

UD

TO THE MSC

SEND ROUTING INFO FOR SHORT

MESSAGE (09.02)

SCA

SCA DA SMI DI

RP-MT-DATA

SCA

GMSCA DI

MSCA

SMI

FROM SC

SHORT MESSAGE ROUTING

INFORMATION MESSAGE (09.02)

MSM MMS UD

NOTE: A sequence of short messages will have MMS set to 1 in each RP-MT-DATA except the last (last will have MMS set to 0). Each RP-MT-DATA will be carried via

FORWARD SHORT MESSAGE via TCAP and will be assigned the same Dialogue Identifier as previous RP-MT-DATAS in the sequence.

Figure 1.2: Mobile terminated short message

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 102 (GSM 03.40 version 7.3.0 Release 1998)

OA PID DCS SCTS MMS UDL MTI UD

DA OA UD

SMS-DELIVER

MTI MR OA UD RP-DATA UDL

RL

(04.11)

TO THE MS

SME

+

SEND INFO FOR I/C

CALL SET UP (09.02)

OC

(04.11)

MSC

MNSMS-EST-REQ (04.11)

SM-RL-DATA-REQUEST

DA TCAP UD GMSCA DI

DI MR

FROM GMSC

SCA

RP SRI

FORWARD SHORT

MESSAGE (09.02) MSM

NOTE: MR is of local significance to the MSC/MS interface and is not the value supplied to the MSC

Figure 1.3: Mobile terminated short message

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 103 (GSM 03.40 version 7.3.0 Release 1998)

MTI MR OA

SMI OA UD

OA PID DCS SCTS UDL UD

DCS SMI OA PID MMS SM SCA

SMS-DELIVER

MOBILE STATION

SM-AL

SM-TL

SM-RL

CM

SC SME

SCTS

RP-DATA

PRI

(04.11)

TS-DELIVER.IND

(04.11)

MNSMS-EST-IND (04.11)

FROM THE MSC

SM-RL-DATA-IND (RS-MT-DATA.IND)

UDL + UD

SRI RP

MTI RP SRI MMS

Figure 1.4: Mobile terminated short message

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 104 (GSM 03.40 version 7.3.0 Release 1998)

SM-AL

SM-TL

SM-RL

MTI MR MTI MR

MOBILE STATION

CM

RP-ACK OR RP-ERROR

CS

PDI TID MT UD

MNSMS-DATA-REQ (04.11)

CP-DATA

(04.11)

RP-ACK

(04.11)

RP-DATA (04.11)

RP-ERROR (04.11)

TO THE MSC

UD

MTI FCS SMS-DELIVER-REPORT

Figure 2.1: Acknowledgement in the MT case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 105 (GSM 03.40 version 7.3.0 Release 1998)

MTI MR MR MTI

MSC

SM-RL

RL

MTI MR MR MTI

RP-ACK OR RP-ERROR

PDI TID MT UD

CS

CP-DATA

(04.11)

MNSMS-DATA-IND (04.11)

TO THE SMS-GMSC

SMRL-REPORT-IND

(04.11)

RP-ERROR (04.11) CS

RP-ACK

(04.11)

FROM THE MS

CM

MR DI

DI DI UD UD TCAP

UD

UD

NOTE: The cause carried via UD of TCAP is not the cause supplied via RP-ERROR but is the cause resulting from application of the mapping specified by table 8.5 of

04.11.

Figure 2.2: Acknowledgement in the MT case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 106 (GSM 03.40 version 7.3.0 Release 1998)

SMS-GMSC

SMI RP-ACK

SM-RL

SCA DA SMI DI

DI UD TCAP

FROM MSC

SMI CS MWS RP-ERROR

RESULT

TO THE SC

SET MESSAGE WAITING

DATA (09.02)

UD MAL

NOTE 1: The MAP operation "SetMessageWaitingData" is invoked only if a cause "Absent Subscriber" is carried in TCAP UD.

NOTE 2: The cause delivered to the SC is not necessarily the cause carried via TCAP but is one of the set specified by table 03.40/1.

Figure 2.3a: Acknowledgement in the MT case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 107 (GSM 03.40 version 7.3.0 Release 1998)

SMI

RP-ACK SMI RP-ERROR

SERVICE CENTRE

SMI

SMI CS MWS

SMI MWS

SMI

SM-RL

FROM SMS-GMSC

RS-REPORT

TS-REPORT

SM-TL

RS-ERROR

TS-REPORT SoR SoR

CS MWS

UD

MTI FCS SMS-DELIVER-REPORT

UD

MAL

MAL

Figure 2.3b: Acknowledgement in the MT case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 108 (GSM 03.40 version 7.3.0 Release 1998)

MOBILE STATION

DA PID DCS VP SM

MR DA PID DCS VP UDL UD

SMI DA UD

MR DA UD

SC

SMS-SUBMIT

SM-AL

SM-TL

SM-RL

CM

MTI

SCA

TO THE MSC

SME

UDL +

RP-DATA

(04.11)

SC

RP-DATA

TS-SUBMIT.REQ

(04.11)

MNSMS-EST-REQ (04.11)

RS-MO-DATA.REQ (SM-RL-DATA-REQ)

SMI SRI RP

MTI VPF RP SRI

NOTE: The mapping of SMI to MR by the MS is a local matter.

Figure 3.1: Mobile originated short message

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 109 (GSM 03.40 version 7.3.0 Release 1998)

MSC

MTI MR DA UD

MNSMS-EST-IND

SM-RL

CM

FROM THE MS

UDL +

OA UD DA

(04.11)

TO THE SMS-IWMSC

(RP-DATA)

SEND INFO FOR O/G CALL SET UP

(09.02)

COMPLETE CALL (09.02)

MSISDN

VLR

FORWARD

SHORT MESSAGE

(09.02)

OC

UD

MSISDN

OA MR DI

SCA

OA GMSCA TCAP DI

MSCA

Figure 3.2: Mobile originated short message

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 110 (GSM 03.40 version 7.3.0 Release 1998)

SM-RL

FROM THE MSC

UD

SMS-IWMSC

TO THE SC

OA UD

OA

OA UD

MR DI

IWMSCA DI

MR

FORWARD

SHORT MESSAGE

(09.02)

MSISDN SCA

OC

TCAP

TC-BEGIN

RP-DATA-MO

DA

NOTE: MR is of local significance to the IWMSC/SC interface and is not the value supplied by the MS via the MS/MSC interface

Figure 3.3: Mobile originated short message

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 111 (GSM 03.40 version 7.3.0 Release 1998)

SERVICE CENTRE

SM-AL

SM-TL

SM-RL

UD

SMI

MTI MR DA PID DCS VP UDL UD

DA OA PID DCS VP

MSISDN

RP-MO-DATA

UD

SM

OA

OA

VPF

SME

TS-SUBMIT.IND

RS-MO-DATA.IND

SMS-SUBMIT

FROM THE SMS-IWMSC

MR

SMI SRI

RP SRI

Figure 3.4: Mobile originated short message

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 112 (GSM 03.40 version 7.3.0 Release 1998)

SERVICE CENTRE

MR MR CS RP-ACK RP-ERROR

SM-RL

TO THE SMS-IWMSC

UD

MTI FCS SMS-SUBMIT-REPORT

Figure 4.1a: Acknowledgement in the MO case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 113 (GSM 03.40 version 7.3.0 Release 1998)

MR RP-ACK RP-ERROR

SMS-IWMSC

MR

MR CS

DI

FROM THE SC TO THE MSC

TCAP TCAP DI DI UD UD

Figure 4.1b: Acknowledgement in the MO case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 114 (GSM 03.40 version 7.3.0 Release 1998)

MSC

SM-RL

RP-ACK RP-ERRO

RP-ACK OR RP-ERROR

PDI TID MT UD CP-DATA (04.11)

MNSMS-DATA-RE

(04.11)

RP-ACK OR RP-ERROR

MR MR CS

(04.11) (04.11)

TCAP TCAP DI DI UD

FROM THE

SMS-IWMSC TO THE MS

OA MR DI

SM-CM

SM-TL

SM-RL-REPORT-RE

(04.11)

UD

Figure 4.2: Acknowledgement in the MO case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 115 (GSM 03.40 version 7.3.0 Release 1998)

MOBILE STATION

SM-RL

CM

SM-TL

RP-ACK RP-ERROR

SMI

SMI SoR

SMI

SMI SoR

RP-ACK OR RP-ERROR

CS

TS-REPORT.IND TS-REPORT.IND

MTI MR MTI MR

CS

MNSMS-DATA-IND (04.11)

CP-DATA (04.11)

FROM THE MSC

SM-RL-REPORT-IND SM-RL-REPORT-IND UD

MTI FCS SMS-SUBMIT-REPORT

UD

Figure 4.3: Acknowledgement in the MO case

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 116 (GSM 03.40 version 7.3.0 Release 1998)

Annex D (informative):

Mobile Station reply procedures

D.1 Introduction

The reply procedures specified in this annex should be followed by a mobile station when replying to a short message,

i.e. when generating a MO SM in response to a received MT SM, addressed to the originator of that MT SM. The main

purpose of this annex is to specify how the MS selects the service centre for delivering that MO SM: an arbitrary SME

may only be reached by submitting the reply SM to a specific SC, known to be able of delivering to that SME.

D.2 The scope of applicability

The reply procedures in clauses 5 and 6 of this annex should be followed by every MS which fulfils the following

criteria:

1) The MS automatically selects the value for the RP-Destination-Address parameter in RP-MO-DATA, or the MS

has the SC address within the SM-RL entity. (That is to say: the human user is not obliged to manually key in the

SC address for every MO short message).

2) The MS or an application within it supports some form of replying to a MT SM with a MO SM. (That is to say:

in the process of generating the reply MO SM, any reference whatsoever, implicit or explicit, is made to the

original MT SM.).

3) The replying support of (2) is to be equally available towards every SME.

When an SME submits an SM to an SC for delivery, it may request that the SC sets the TP-Reply-Path parameter in the

SM to be delivered. If the submitting SME is an MS, the reply path requesting procedure; in clause 4 of this annex may

be applied. However, an SC may support the reply procedures without supporting the reply path requesting procedure;

in that case, the SC sets the TP-Reply-Path parameter on another basis, which must be the case if the SM originates from

an SME which is not an MS.

D.3 Terminology

An originating SME submits an original SM to an original SC, which delivers the original MT SM to a replying MS.

The replying MS sends back a reply MO SM, a MO SM which is generated (automatically or by human operations) in

response to the original MT SM, and which is addressed to the originating SME.

If the originating SME is an MS, the original MT SM is submitted within an SMS-SUBMIT PDU; we say that reply

path is requested if the TP-Reply-Path parameter is set in the SMS-SUBMIT PDU of the original MT SM.

We say that reply path exists if the TP-Reply-Path parameter was set in the SMS-DELIVER PDU of the original MT

SM; we say that reply path does not exist otherwise.

The replying MS may have a default SC which is normally used for delivering all the MO short messages originated

from the replying MS. Alternatively, a human user or automatic application may specify a selected SC for delivering a

particular SM (thus the term selected SC refers to an SC address selected for one short message only).

D.4 The reply path requesting procedure

The discussion in this clause applies to cases when the originating SME is a mobile station only. The reply procedures

discussed in the clauses to follow this one are independent of the type of the originating SME.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 117 (GSM 03.40 version 7.3.0 Release 1998)

The reply path is requested by the originating SME (an MS) by setting the TP-Reply-Path parameter in the SMS

SUBMIT PDU of the original SM. If the original SC supports reply path requesting for the originating SME (an MS), it

will take notice of the TP-Reply-Path parameter in the SMS-SUBMIT PDU and set the TP-Reply-Path parameter in the

SMS-DELIVER PDU of the original MT SM towards the replying MS. Hence, reply path exists for the replying MS

towards the originating SME (an MS).

D.5 The reception of an original MT SM

When a replying MS receives an original MT SM, it then has:

1) originating SME = TP-Originating-Address in the SMS-DELIVER PDU;

2) original SC = RP-Originating-Address in RPS-MT-DATA; and

3) reply path exists / reply path does not exist = TP-Reply-Path in SMS-DELIVER PDU (set / not set).

D.6 The submission of the reply MO SM

According to clause 5, the replying MS knows if:

a) reply path exists or

b) reply path does not exist.

We then specify that when submitting the reply MO SM, the replying MS should use parameters as follows:

1) TP-Destination-Address in SMS-SUBMIT PDU = originating SME,

2a) If reply path exists:

RP-Destination-Address in RP-MO-DATA = original SC,

2b)If reply path does not exist:

RP-Destination-Address in RS-MO-DATA = selected SC or default SC or original SC,

3a) If reply path exists:

after submitting one reply MO SM, the reply path does not exist any more.

In case (2b), it is allowed to use the original SC or the default SC, but then there is no guarantee that the original/default

SC will deliver the reply MO SM. (The original SC may refuse to deliver, if the replying MS is not its subscriber; the

default SC may be unable to deliver, if it has no access path to the originating SME.)

Requirement (3a) states that the case (a), reply path exists, holds for one reply MO SM only (per original MT SM).

D.7 Usage of SCs for replying

The specification in this annex supports the following way of replying.

The original MT SM and the reply MO SM are delivered by the same SC, the original SC. This principle maximizes the

probability that the SC can e.g. route the reply MO SM to the proper data network for reaching the originating SME; this

principle is a must, if the originating SME is integrated within the original SC.

If the original SC by any means whatsoever knows that it is both willing and able to deliver one (potential) reply MO

SM, it may indicate this fact by setting the TP-Reply-Path parameter in the original MT SM. The original SC thus

commits itself to delivering one reply MO SM; let us call this reply delivery commitment.

One reason for the SC to make the reply delivery commitment may be the reply path requesting procedure specified in

clause 4 on this annex.

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 118 (GSM 03.40 version 7.3.0 Release 1998)

The reply path commitment is not valid forever, but the original SC pay have e.g. a time limit for maintaining this

commitment.

D.8 Replying possibilities for Phase 1 mobile stations

The Phase 2 mobile stations should support the procedures in this annex (if they fulfil the criteria in clause 2 of it). Yet,

Phase 1 mobile stations, too, may apply steps (1) and (2a) in clause 6 of this annex, i.e. reply via the original SC,

automatically or manually (by choosing selected SC = original SC), despite the fact that the TP-Reply-Path parameter

will be ignored by them. The delivery of the reply MO SM cannot be guarantied in this case, yet the possibility of

delivery may be improved (especially if the originating SME is not an MS.)

D.9 The resulting service for originating SMEs

As the consequence of the replying procedures specified in this annex, all SMEs and applications within them may

assume that replying from all mobile stations is always possible, provided that the mobile stations do support the proper

replying mechanism itself (human response in context with the original MT SM, automatic replying by an application,

application level protocols, etc.).

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 119 (GSM 03.40 version 7.3.0 Release 1998)

Annex E (informative):

Change History

SMG# TDoc SPEC VERS CR R

E

V

PHA

SE

C

A

T

SUBJECT NEW_VE

RS

WORKITE

M

s23 97-696 03.40 5.7.0 A060 R97 B Code points for SIM Toolkit secure messaging

Draft 1.0 of V6.0.0 (PT SMG internal)

6.0.0d1.0 SIM Toolkit

Security

s23 97-696 03.40 5.7.0 A062 R97 F User Data Header Indicator

Draft 1.0 of V6.0.0 (PT SMG internal)

6.0.0d1.0

s23 97-706 03.40 5.7.0 A063 R97 B SMS transfer over GPRS

Draft 1.0 of V6.0.0 (PT SMG internal)

6.0.0d1.0 GPRS

s24 97-918 03.40 5.7.0 A064 R97 B Security headers

Draft 2.0 of V6.0.0 (PT SMG internal)

6.0.0d2.0 SIM Toolkit

Security

s24 97-918 03.40 5.7.0 A065 R97 B Transmission of the SME OA

Draft 2.0 of V6.0.0 (PT SMG internal)

6.0.0d2.0 SMS Enh.:

Filtering

s25 98-096 03.40 5.7.0 A066 R97 B MS Management PID R97 6.0.0 MS

Management

s26 98-291 03.40 6.0.0 A071 R97 A Queuing of MT SMS at the VMSC and SGSN 6.1.0 SMS Mobile

Busy

s26 98-291 03.40 6.0.0 A074 R97 F Status-Report-Request for concatenated short messages 6.1.0 SMS

Concatenated

Messages

s26 98-291 03.40 6.0.0 A075 R97 F TP-User Data (TP-UD), SMSC Control Parameters 6.1.0 SMS

Concatenated

Messages

s26 98-291 03.40 6.0.0 A076 R97 F Redefinition SMS status report user data length 6.1.0 SMS

s26 98-291 03.40 6.0.0 A077 R97 B Use of TP-UD and other TP parameters with RP-ERROR 6.1.0 SIM Toolkit

s26 98-291 03.40 6.0.0 A079 R97 F TP-User Data (TP-UD), Concatenated Short Messages 6.1.0 SMS

Concatenated

Messages

s26 98-291 03.40 6.1.0 A072 R98 D Alignment of 03.40 concerning inclusion of 7bit defaultalphabet

extension mechanism in 03.38

7.0.0 TEI

s27 98-0738 03.40 7.0.0 A083 R98 B User Data Header Identifier value for Concatenated Short

Message, 16-bit reference number

7.1.0 TEI

s27 98-0738 03.40 7.0.0 A084 R98 B User Data Header Identifier value for Wireless Control

Message Protocol (WCMP)

7.1.0 TEI

s27 98-0738 03.40 7.0.0 A085 R98 D Insertion of padding bits to a user data header 7.1.0 TEI

s29 99-0482 03.40 7.1.0 A086 R98 C Clarification concerning SMSC address checking in the

MS for concatenated messages and replace message types

7.2.0 TEI

s29 99-0482 03.40 7.1.0 A087 R98 D Guidance regarding the SMSC address in a Status Report 7.2.0 TEI

s30 99-0675 03.40 7.2.0 A088 R98 C Change to reserved port number range for SMS 7.3.0 TEI

ETSI

ETSI TS 100 901 V7.3.0 (1999-11) 120 (GSM 03.40 version 7.3.0 Release 1998)

History

Document history

V7.2.0 July 1999 Publication

V7.3.0 November 1999 Publication