# WMOi3 TEST BOARD

## Introduction

The WMOi3 test board is designed to provide access to the WMOi3 embedded modem. It has a standard 9-pin serial RS232 connector, an SMA header for the antenna, 2 RJ-11 sockets for standard earpieces and microphones, Reset button, Boot button, on-off switch and a 12Vdc power input socket. Two LEDs are provided, one LED indicates input power, the other LED for WMOi3 status.

### Board layout

WMOi3

modem

Boot Button

Reset Button

SMA

Antenna						  	On/Off Switch

Serial		 Status    LED			Power LED

RS232

Port

Audio-2 Audio-1     12Vdc Input

Serial RS232 port (DB9/Female)			      5    4    3     2    1

Pin 1	DCD			Pin 6	DSR

Pin 2	RxD			Pin 7 	RTS

Pin 3	TxD			Pin 8	CTS

Pin 4	DTR			Pin 9	RI		       9    8     7    6

Pin 5	GND

### Audio-1 RJ11 socket		Audio-2 RJ11 socket

1  2  3  4

Pin 1	MIC1 +			Pin 1	MIC2 +

Pin 2	SPK1 -			Pin 2	SPK2 –

Pin 3	SPK1 +			Pin 3	SPK2 +

Pin 4	MIC1 -			Pin 4	MIC2 –

### VDC Input Port (12Vdc at 1Amp)

Middle pin	+12V

Outside		GND

Notes:

- Make sure the power is off before inserting or removing the SIM card

- When power is applied, if the status LED is not on, then turn the on/off switch to either side to turn the WMOi3 on.